An Ultracold Neutron Source for TRIUMF
Jeff Martin (U. Winnipeg)
for Lothar Buchmann, Chuck Davis, Michael Gericke, Bob Golub,
Akira Konaka, Larry Lee, Yasuhiro Masuda, Ania Micherdzinska,
Shelley Page, Des Ramsay, Wim van Oers
(KEK, TRIUMF, NCSU, U. Manitoba, U. Winnipeg)
1. Introduction to Ultracold Neutrons (UCN)
2. UCN physics experiments
3. Source work at RCNP for TRIUMF
4. TRIUMF facility
5. CFI, relationship, collaboration, KEK

---
Ultracold Neutrons
Ultracold Neutrons
UCN are neutrons that are moving so slowly that they are totally reflected from surfaces of materials.
So, they can be confined in material bottles for long periods of time.
Typical parameters:
  - velocity < 8 m/s
  - temperature < 4 mK
  - kinetic energy < 300 neV
Interactions:
  - gravity: V=mgh (h < 3 m)
  - weak interaction (allows UCN to decay)
  - magnetic fields: V=-B (100% polarization)
  - strong interaction
Experiments at UCN sources are chronically limited by UCN density. TRIUMF has the potential to be a world leader in this regard.

---
Gravity
Gravity
V = mgh
For a neutron on the planet Earth:
m = 1 GeV/c2, g = 10 m/s2, h = 3 m
 V = 300 neV
Recall, TUCN < 300 neV
Uses:
  - UCN gravity spectrometer
  - gravitational levels expt
no UCN
3 m
y
UCN
x

---
Weak Interaction
Weak Interaction
n  p + e- +  + 782 keV
 = 885.7 +/- 0.8 s
  - (needed for BBN)
a, B, A
  - (+ tau needed to extract Vud)
b, D, R
  - (are zero in SM)

---
Magnetic Interaction
Magnetic Interaction
The neutron has a magnetic moment:
 = -1.9 N = - 60 neV/T
The potential energy of a magnetic moment in a magnetic field is:
V = -   B
B = 7 T rejects one spin state of UCN (if adiabaticity obeyed)
=> UCN can be 100% polarized.

---
Strong Interaction
Strong Interaction
size 12{V \( r \) } {}
size 12{"neutron-Nucleus potential"} {}
size 12{r} {}
Attractive Nuclear Force
"40"" MeV"
size 12{r rSub { size 8{0} } approx " 2 fm"} {}
size 12{"For "T rSub { size 8{n} } <= " 1 MeV, "l "~" ital "pr" rSub { size 8{0} } "~" "0, "s-wave" scattering " \( "isotropic" \) } {}
alignl { stack { size 12{"For T" rSub { size 8{n} } "<<"" 1 MeV,"} {} # " "σ rSub { size 8{"tot"} } =" 4"π" a" rSup { size 8{2} } {} # " a" equiv " scattering length" {} } } {}

---
Scattering Length
Scattering Length
Weak potential
size 12{"a "<" 0"} {}
size 12{"a ">" 0"} {}
Strong potential
Many different potentials can
give rise to the same value for “a”
Odds are, a > 0

---
Fermi Potential
Fermi Potential
Let’s replace V(r) by an effective potential with the same a:
size 12{V rSub { size 8{ ital "eff"} } \( r \) = { {2π hbar rSup { size 8{2} } a} over {m} } δ \( r \) } {}
size 12{V rSub { size 8{ ital "eff"} } \( r \) = { {2π hbar } over {m} } rSup { size 8{2} } Sum cSub { size 8{i} } {a rSub { size 8{i} } δ \( r - r rSub { size 8{i} } \) } } {}
For many nuclei in a solid,
For a all the same, and small lattice spacing cf. neutron ,
size 12{V rSub { size 8{ ital "eff"} } \( r \) = { {4πa hbar } over {2m} } rSup { size 8{2} } N rSub { size 8{0} } Int { { {d rSup { size 8{3} } r'} over {V} } δ \( r - r' \) } = { {2πa hbar rSup { size 8{2} } n rSub { size 8{0} } } over {m} } θ \( r notin V \) equiv V rSub { size 8{0} } θ \( r notin V \) } {}

---
Fermi Potential
size 12{V rSub { size 8{"eff"} } \( r \) } {}
size 12{V rSub { size 8{0} } } {}
size 12{"Solid"} {}
size 12{r} {}
Even attractive potential can lead to
repulsive effective potential!
(the “Fermi Potential”)
Just as long as a > 0
Largest Fermi potential is for Nickel-58 (58Ni)
V0 = 335 neV

---
Physics Experiments
Using UCN
All previous experiments using UCN were chronically limited by UCN density.

---
UCN Source at TRIUMF would be
a world-class facility
Source type
Ec and τs
UCN density
ρUCN(UCN/cm3)
TRIUMF
5 kWav proton
0.8K He-II
Ec = 210 neV
τs = 150 s
1.8 x 104 at experimental port
Grenoble
60MW reactor
0.5K He-II
Ec = 250 neV
τs = 150 s
1000 in He-II
SNS
cold neutron beam
0.3K He-II
Ec = 134 neV
τs = 500 s
430 in He-II
Munich
20MW reactor
SD2
Ec = 250 neV
104 in source
North Carolina
1 MW reactor
SD2
Ec = 335 neV
1300 in source
PSI
12 kWav proton
SD2
Ec = 250 neV
τs = 888 s
2000 in source
Los Alamos
2.4 kWav proton
SD2
Ec = 250 neV
τs = 2.6 s
120 in source

---
The Most Successful UCN Experiments to Date
EDM
Lifetime
Gravity Levels
Mirror Neutrons
all of them were done at ILL, Grenoble

---
Future UCN Experiments
EDM
  - in vacuo (PSI)
  - in 4He/3He (SNS)
  - ILL
  - KEK
Lifetime
  - gravito-magnetic bottle (LANL)
  - magnetic bottle in 4He (SNS)
Gravity Levels
  - ILL with new 4He source
-Decay Correlations (A)
  - UCNA (LANL)
r-process, free neutron target
nnbar oscillations
mirror neutrons
surface physics
physics of UCN production
  - e.g. O2

---
UCN quantum states in gravity
test of gravity at 10 um scale

---
Possible topology
Measuring (n,ɣ) cross sections of the r-process (Buchmann)
132Sn stored in ring interacts
with free neutron (UCN) target.
132Sn current 5e17 /s
UCN density 2e4 /cc
meter-long target
sigma ~ 100 mb
=> 50 interactions per hour
recoil separator
Accelerator
Possible tunnel
UCN
Storage ring
Recoil separator

---
Surface Physics
Many ideas to use UCN to study 10 nm thin surface films
  - (n,gamma)
  - UCN loss measurements
  - n scattering
  - reflectometry
      - polarization for magnetic films
shown to be sensitive to low-frequency excitations (interesting for surface physics)
In all cases, lack of UCN worldwide is the problem
Korobkina, NCSU

---
UCN Source Design
and How We Would Achieve the World's Highest UCN Density
Most other proposed sources use solid deuterium (ortho) at ~4K
  - ice quality
  - material potential
  - para fraction, H-contamination
We would use superfluid He-II (Masuda et al PRL)
  - lower specific production
  - NO loss mechanisms.

---
RCNP UCN Source (Masuda, et al)
1 ua protons at 400 MeV
=> 10 UCN/cc to expt.
Already has external users!
- e.g. Korobkina, Young (NCSU)

---
Gain Factors for TRIUMF
O

---
Recent Progress on UCN at TRIUMF
Aug. 2007 TUG working group (Canadians + Masuda), draft of white paper.
Sept. 2007 International UCN Workshop (+ world experts).
Sept. 2007 Presentation to Agency Committee on TRIUMF (ACT)
Oct.-Nov. 2007 phone meetings relating to conceptual design
Nov. 2007 ACOT

---
My old advertisement slide...
International Workshop:
UCN Sources and Experiments
September 13-14, 2007
TRIUMF, Vancouver, Canada
http://www.triumf.info/hosted/UCN
~25 speakers from all over the world
ILL, FRM-II, NCSU, LANL, PSI, KEK, Mainz, ...
Supported by TRIUMF and TUNL

---
Speakers at TRIUMF
UCN Workshop
Sept. 13-14, 2007
H. Abele, Heidelberg
S. Baessler, Mainz/UVa
L. Buchmann, TRIUMF
M. Daum, PSI
S. Gardner, U. Kentucky
P. Geltenbort, ILL
E. Gutsmiedl, Munich FRM-II
R. Golub, NCSU
B. Filippone, Caltech
P. Huffman, NCSU
T. Ito, LANL
E. Korobkina, NCSU
C.-Y. Liu, Indiana U.
M. Makela, LANL
J.W. Martin, U. Winnipeg
Y. Masuda, KEK
P. Mumm, NIST
J. Nico, NIST
J. Ng, TRIUMF
M. Pospelov, U. Victoria/Perimeter Inst.
J.-M. Poutissou, TRIUMF
W.M. Snow, Indiana U.
F. Wietfeldt, Tulane U.
A. Young, NCSU
G. Hampel, Mainz
K. Hickerson, Caltech

---
Results of Workshop
Very strong statement from the international UCN community (particularly R. Golub) that a He-II source should be pursued. Masuda clearly regarded as a leader in this field.
TRIUMF would be an ideal venue for such a source.
Many interesting physics experiments would be possible with the higher UCN densities achievable at this source.

---
Schedule
Prior to 2010, pursue development of new UCN cryostat for TRIUMF at RCNP, Osaka.
  - This would allow us to demonstrate all the gain factors from horizontal extraction, better UCN guides. (aside from beam power)
After 2010, begin construction of UCN source at TRIUMF (2010 = coincident with major reconstruction for ISAC 3).

---
Experimental Plan
Conduct one initial high-profile, world's best, fundamental physics experiment (likely either n-lifetime or gravity)
Simultaneous development of surface physics apparatus
Developments towards future n-EDM experiments
Other large-scale experiments and transition to JPARC.

---
Technical Issues for UCN
Location.
Beam sharing.
Space (12m x 12m source + 12m x 6m expts)
To carry out precision experiments, it is highly advantageous to pulse the UCN source. E.g. RCNP uses 1 min beam on, 3 mins beam off. During beam off, UCN can be counted (or their decays, etc.)
  - pulsing at ion source incompatible with other users.
  - achieve pulsing by diverting beam to well-shielded dump using kicker.

---
Conceptual to technical design for the UCN source and experiment
LANL
Masuda
Other Issues:
radiation, remote handling
cryogenics
neutronics
division of tasks
Masuda, Golub, others? very interested in cryogenics and neutronics
need TRIUMF support to bring to fruition
LANL

---
UCN
- siting options
BL5

---
Cost
Cryostat, LHe cooling costs very well-understood (1.4 M$ CAD)
Masuda request to Japanese funding sources for 2.4 M$ CAD over the next four years (the above plus EDM development) explicitly mentions TRIUMF. (submitted Nov. 2007)
Interest in submitting a CFI proposal from the Canadian groups in 2008 for the remaining infrastructure.

---
Summary
An opportunity exists to create the world's highest density UCN source at TRIUMF
A flagship physics experiment done this facility would be world's best
The UCN facility would be tied to the ISAC-3 program in terms of both physics and facility
We would like to pursue this unique and timely opportunity

---
Back-ups

---
Cryogenics/Shielding Numbers from Masuda
According to MC + estimates, for time-avg p-beam power of 12 kW in W target:
  - 0.45e12 n/cm2/s in He-II
  - 2.3 W in He-II
  - 30-60 W in 20 K D2O
  - 1.7 kW in 300 K D2O
Masuda's current 3He pump can take 8 W.
Clever arrangement of 208Pb can reduce gamma-heating of He-II even lower.
Radiation #'s consistent/lower cf. LANL.

---
simultaneous operation with ISAC-3 by decoupling on kHz scale with kicker/ion source manipulation. Advantageous for ISAC-3: run all three targets simultaneously.
ion source current vs. time
I(t)
1 msec
10 msec
t
kick to ISAC-3-1
kick to ISAC-3-2
kick to ISAC-3-3
(UCN)

---
Solutions Discussed for Technical Issues
Location:
  - BL5 area
    - Advantages:
      - decoupled from ISAC 3.
    - Disadvantages:
      - new beam port must be constructed
      - beam line must not conflict with cyclotron probe extraction point
      - high-power dump required to achieve pulsing with kicker.
      - space in Proton Hall tighter – likely requires excavation for dump.

---
Shameless advertising
International Workshop:
UCN Sources and Experiments
September 13-14, 2007
TRIUMF, Vancouver, Canada
http://www.triumf.info/hosted/UCN
~25 speakers from all over the world
ILL, FRM-II, NCSU, LANL, PSI, KEK, Mainz, ...
Supported by TRIUMF and TUNL

---
Aug. 1
morning - plenary session, charge, and introduction of working groups
12:00 lunch
13:00 Welcome + Charge (Martin) (10+5)
13:15 UCN Sources Worldwide and for TRIUMF (Masuda) (45+10)
14:10 Photofission, (gamma,n) Sources and UCN (Behr) (10+10)
14:30 coffee (30)
15:00 SCRF joint session: Electron Linac Design (Koscielniak) (20+10)
15:30 UCN Infrastructure and Proton Hall Floorplan (Davis) (10+10)
15:50 Proton Hall Radiation Limits (Trudel) (10)
16:00 Discussion (Chair: Davis) (30)
16:30 tour of proton hall? (if desired) (Davis) (30)
Aug. 2
09:00 Continued infrastructure Discussion (60)
10:00 UCN Physics Intro (Martin) (10+5)
10:15 UCN Beta Decay (Melconian) (20+10)
10:45 coffee (30)
11:15 n-EDM (Masuda and/or Hayden?) (20+10)
11:45 radioactive beams (Buchmann) (10+10)
12:05 lunch
13:15 gravity levels (Konaka) (5+10)
13:30 other physics (Martin) (15+10)
13:55 discussion of physics priorities and strategy (chair: Martin) (35)
14:30 begin writing
      more joint sessions
      draft Aug. 3 morning presentation
Aug. 3
morning - presentations of results from the working groups.
Agenda
from
townhall
meeting
(Aug. 07)

---
Outline of White Paper
Physics
  - prioritized and realistic, as much as possible
UCN Source
  - proposed intensity at TRIUMF
  - world context and relevance
Required Infrastructure
  - floorspace, shielding
  - duty cycle
  - He liquefier
Required funding
  - CFI and collaboration, and international