Canadian Spallation Ultracold Neutron Source
Jeff Martin (U. Winnipeg)
Collaborators: J.D. Bowman, J. Birchall, L. Buchmann, L. Clarke, C. Davis, B.W. Filippone,
M. Gericke, R. Golub, K. Hatanaka, M. Hayden, T.M. Ito, S. Jeong, I. Kato, S. Komamiya,
E. Korobkina, E. Korkmaz, L. Lee, Y. Masuda, K. Matsuta, A. Micherdzinska, W.D. Ramsay,
S.A. Page, B. Plaster, I. Tanihata, W.T.H. van Oers, Y. Watanabe, S. Yamashita, T. Yoshioka
(Winnipeg, Manitoba, ORNL, TRIUMF, NCSU, Caltech, RCNP, SFU, LANL, KEK, Tokyo, UNBC, Osaka, Kentucky)
CANADA’S NATIONAL LABORATORY FOR PARTICLE AND NUCLEAR PHYSICS
Owned and operated as a joint venture by a consortium of Canadian universities via a contribution through the National Research Council Canada
LABORATOIRE NATIONAL CANADIEN POUR LA RECHERCHE EN PHYSIQUE NUCLÉAIRE ET EN PHYSIQUE DES PARTICULES
Propriété d’un consortium d’universités canadiennes, géré en co-entreprise à partir d’une contribution administrée par le Conseil national de recherches Canada

---
Summary
We propose to construct the world's highest-density source of UCN at TRIUMF
The source will be used carry out fundamental and applied research
Experiments:
  - gravity levels
  - n-lifetime
  - surface science
  - n-EDM
near term
longer term

---
How we will succeed
Huge commitment from expert Japanese group (Masuda) on UCN source project.
The TRIUMF high-intensity 500 MeV proton beam is required to reach high UCN density.
Canadian university-group expertise in fundamental neutron physics.
Exciting UCN physics experiments supported internationally (Japan, USA, Canada)

---
Ultracold Neutrons
Ultracold Neutrons
UCN are neutrons that are moving so slowly that they are totally reflected from surfaces of materials.
So, they can be confined in material bottles for long periods of time.
Typical parameters:
  - velocity < 8 m/s
  - temperature < 4 mK
  - kinetic energy < 300 neV
Interactions:
  - gravity: V=mgh (h < 3 m)
  - weak interaction (allows UCN to decay)
  - magnetic fields: V=-B (100% polarization)
  - strong interaction
Experiments at UCN sources are chronically limited by UCN density. TRIUMF can provide the world's largest density.

---
How to make UCN
Liberate neutrons by proton-induced spallation.
Moderate (thermalize) in cold (20 K) D2O.
Cold neutrons then “downscatter” to near zero energy (4 mK) in superfluid helium through phonon production.
Unique to TRIUMF! Most others use SD2

---
RCNP UCN Source (Masuda, et al)
1 a protons at 400 MeV
        → 10 UCN/cm3 to experiment.
Already has external users!
- e.g. Golub, Korobkina, Young (NCSU)

---
Gain Factors for TRIUMF
O
Future Upgrade: D2O ice → LD2 : x5

---
1-5 x 104
*

---
Experiments
n-lifetime
gravity levels
surface science
n-EDM
near term
longer term

---
Neutron Lifetime
Physics interest:
  - BBN
  - Vud
Currently a 6.5 sigma discrepancy between n-lifetime experiments

---
Neutron Lifetime
New efforts to trap UCN magnetically
marginally trapped orbits
NEED MORE UCN!!!
Basic experiment: trap UCN for varying amounts of time
All previous precise experiments used material traps
Wall effects give dominant systematic effects
<- Gravitrap
Permanent magnet trap
        ->
(both at ILL)

---
Magneto-Gravitational Trap for Neutron Lifetime (Bowman et al)
beta detectors
betas spiral around
guide field lines
0.5 m
Shallow Halbach array + gravity for trap
Guide field for decay betas
Marginally trapped neutrons experience chaotic orbits and are ejected rapidly
Goal precision n ~ 0.1 s
Requirements: Efficient trap loading, effective n-“cleaning”, high UCN density
loading through
trap door

---
N-lifetime Plans for TRIUMF
Theoretical work on trap dynamics completed at LANL (some remaining issues with trap loading)
Prototype under construction at LANL
Goal is for test experiment at LANL UCN source
TRIUMF experiment would build on preliminary work done at LANL
Candidate for a first physics experiment using the TRIUMF UCN source
Current common collaborators:
  - J.D. Bowman, B. Filippone, T. Ito, B. Plaster

---
UCN Quantum States in Gravity
Confine UCN in 1D by gravity
Experimental results have been used to place limits on
10 um scale modifications to gravity
extra dimensions
axions
V(z)
g.s.
V(z)=mngz
1.4 peV
Classical expectation
10 m
z
data +
quantum fit
Quantized energy
levels!
Further experiments:
Bottle the UCN to increase time the UCN is contact with the mirror.
Excite resonant transitions between quantum states.
Increase purity of states by preselection.
Goal: improve precision on energy of state and hence increase sensitivity to modifications to gravity.

---
Concept for Improved Experiment (Komamiya group)
UCN in
Features:
  - glass rod “magnifier”
  - Li-coated CCD readout

---
Plans for TRIUMF
Experiment would be initiated and led by Japanese groups (S. Komamiya, et al).
Because development work is already underway, this is a good candidate for a first experiment (along with n-lifetime).

---
Neutron Electric Dipole Moment (EDM)
Neutron Electric Dipole Moment (n-EDM)
Existence of EDM implies violation of Time Reversal Invariance
CPT Theorem then implies violation of CP conservation
t rightarrow -t
-
Present Exp. Limit < 3x10-26 e-cm
Standard Model value: 10-31 e-cm
Supersymmetry or Multi-Higgs models can give 105xSM
Significant discovery potential with new high sensitivity n-EDM experiment
±E
B

J
h%nu=2%mu_{n}B+-2d_{e}E
size 12{ { vec {J}}} {}
+
-
size 12{ { vec {J}}} {}
+
-

---
n-EDM Systematics
magnetic field variations
leakage currents
geometric phase effect
  - false EDM arising from field inhomogeneity and E x v.
(co)magnetometry
comagnetometry
false EDM (GP) effect

---
Past and Future n-EDM efforts
Oxford-ILL expt. (dn < 3⨯10-26 e-cm)
  - 0.7 UCN/cc, room temp, in vacuo
CryoEDM (ILL, Sussex, RAL)
  - 1000 UCN/cc, in superfluid 4He
SNS
  - 430 UCN/cc, in superfluid 4He
PSI
  - 1000 UCN/cc, in vacuo
TRIUMF: 5 x 104 UCN/cc

---
Plans for TRIUMF
Begin with modified ILL, SNS, or PSI setup
  - higher UCN density allows smaller cell size
    - smaller GP effect
  - development of magnetometers, Ramsey-resonance technique (Masuda)
proposal ~ 2011
expect number of EDM-experienced collaborators to grow if UCN source is approved:
  - B. Filippone, R. Golub, T. Ito, E. Korobkina, M. Hayden, B. Plaster

---
Surface Physics
Use UCN to study 10 nm thin surface films
  - e.g. our application: “inelastic scattering reflectometry” (UCN ISR), sensitive to low-energy excitations, particularly of hydrogen-containing materials
  - compare two methods of inelastic scattering detection:
    - UCN loss measurements
    - detect upscattered neutrons
High intensity UCN source is needed for this new field to be opened up.

---
Application of UCN ISR:
Artificial Molecular Rotors
“low-energy excitations”
=
rotations and vibrations
of big molecules
“Smart surfaces” research – surfaces that change their properties when subjected to external stimuli (drug delivery example)

---
Basic Apparatus
Simultaneous measurement of UCN loss rate and converter gammas isolates UCN ISR from e.g. (n,gamma) losses.

---
UCN ISR apparatus for TRIUMF
Design of cryostat and first proof-of-principle experiments have been carried out. (Hahn-Meitner Inst., ILL)
Need higher UCN flux.
R. Golub, E. Korobkina, L. Clarke (NCSU)
Potentially large user-base in “smart surfaces” community

---
UCN Overall timeline
Before 2012 – develop UCN source in Japan
2012-3 – Install, commission at TRIUMF
First experiments (n-lifetime, gravity, surface physics) 2012-2015
longer term: EDM, 2014 and beyond

---
Implementation at TRIUMF
Meson Hall option
Beamline design (J. Doornbos, G. Clark)
Kicker feasibility, design (M. Barnes)
Shielding estimates (A. Trudel)
Layout (above) (S. Austen, C. Davis)
Cost/Sched/Manpower (V. Verma, W.D. Ramsay, C. Davis)
...and many useful discussions with E. Blackmore, R. Baartman, ...

---
Preparations for CFI NIF request
Request through The University of Winnipeg (top project selected by university committee – NOI in prep.)
Overall cost ~$10M
CFI NIF provides 40% of total cost.
Proposed cost breakdown (rough numbers)
    - CFI NIF	$4M
    - Japanese collaborators	$4M
    - TRIUMF	$2M
Detailed cost+manpower breakdown, discussion provided in draft proposal.
Canadian university cosignatories: J. Martin (Winnipeg), M. Hayden (SFU),
E. Korkmaz (UNBC), J. Birchall, M. Gericke, S. Page, W. van Oers (Manitoba)

---
Conclusion
Canada has an opportunity to construct a world-leading UCN facility at TRIUMF.
Proposal to CFI NIF in preparation through U. Winnipeg. Matching supplied by TRIUMF and Japan.
Detailed cost/sched/manpower estimates, and more detailed design, underway.

---
Why UCN density
is the most important factor
UCN guides
Superfluid He
Experiment
UCN behave like an ideal gas
As long as the experiment volume is much less than the total volume, UCN density is the most important factor.
This is the case for every experiment we are pursuing for TRIUMF.

---
UCN Source Design
and How We Would Achieve the World's Highest UCN Density
Most other proposed sources use solid deuterium (ortho) at ~4K
  - ice quality
  - Fermi potential
  - para fraction, H-contamination
We would use superfluid He-II (Masuda et al PRL)
  - lower specific production
  - NO loss mechanisms.

---
Budget and Manpower Summary
from Proposal (Current Version)
equipment
person-years