Neutron Electric Dipole Moment Search with a Spallation Ultracold Neutron Source at TRIUMF
Spokespeople: Y. Masuda (KEK), J.W. Martin (Winnipeg)
Collaborators: T. Adachi, K. Asahi, M. Barnes, C. Bidinosti, J. Birchall, L. Buchmann, C. Davis,
T. Dawson, J. Doornbos, W. Falk, M. Gericke, R. Golub, K. Hatanaka, S. Jeong,
S. Kawasaki, A. Konaka, E. Korkmaz, E. Korobkina, L. Lee, R. Mastumiya, K. Matsuta, M. Mihara,
A. Miller, T. Momose, W.D. Ramsay, S.A. Page, H. Takahashi, K. Tanaka, I. Tanihata,
W.T.H. van Oers, Y. Watanabe
(KEK, Titech, Winnipeg, Manitoba, TRIUMF, NCSU,
RCNP, UNBC, UBC, Osaka)

---
Ultracold Neutrons (UCN)
- UCN are neutrons that are moving so slowly that they are totally reflected from a variety of materials.
- So, they can be confined in material bottles for long periods of time.
- Typical parameters:
  - velocity < 8 m/s = 30 km/h = 20 mph
  - temperature < 4 mK
  - kinetic energy < 300 neV
- Interactions:
  - Gravity:	V=mgh	mg = 100 neV/m
  - Magnetic:	V=-B	= 60 neV/T
  - Strong:	V=Veff	Veff < 335 neV
  - Weak:	 = 885.7 s = 15 mins

---
Physics Experiments for the TRIUMF UCN Source
- neutron EDM
- gravity levels
- neutron -decay
- nn-oscillations
- Free n target
near term
dreams
All ideas / letters / proposals welcome

---
Neutron Electric Dipole Moment (EDM)
Neutron Electric Dipole Moment
(n-EDM, dn)
d_n drarrow T drarrow CP
t rightarrow -t
New sources of CP violation are required to explain the baryon asymmetry of the universe.
Complementary to Rn-EDM, Fr-EDM @ ISAC.
-
±E
B
Experimental technique:
 - put UCN in a bottle with E-, B-fields
 - search for a change in spin precession
     frequency upon E reversal.

J
h%nu=2%mu_{n}B+-2d_{e}E
size 12{ { vec {J}}} {}
+
-
size 12{ { vec {J}}} {}
+
-

---
EDM's and SUSY
Scale of EDM's for quarks in SUSY:
d_{q} sim %alpha over %pi times {m_q over %LAMBDA_{SUSY}^2} times sin %theta_{CP}
from P. Harris, Sussex
For “reasonable” values of new parameters:
d_{q} sim 3 times 10^{-24} e cdot cm
According to neutron EDM measurements:
d_{u} < 2 times 10^{-25} e cdot cm ~~~~~d_{d} < 5 times 10^{-26} e cdot cm
- Unattractive solution:
  - SUSY > 2 TeV and/or CP < 0.01
  - “SUSY CP problem”

---
EDMs, the SM, and beyond
A. Ritz, M. Pospelov, et al
SUSY M = 1 TeV, tan = 3
Current
precision
Goal
precision
J.M. Pendlebury, E. Hinds
Note: universality assumptions are now even being tested
Ultimate goal: reach the SM limit (still 5 orders of magnitude to go)

---
Testing Universality in MSSM
Li, Profumo, Ramsey-Musolf JHEP 1008, 062 (2010)
- Open up to full MSSM parameter space.
- Scan parameters obeying neutron, Tl, Hg limits.

---
Past and Future n-EDM efforts
- Sussex-RAL-ILL expt. (dn < 3⨯10-26 e-cm)
  - 0.7 UCN/cc, room temp, in vacuo
- New experiments:
  - CryoEDM (Sussex-RAL-ILL)
  - SNS
  - PSI
  - Japan-Canada (us)
- Different superthermal sources
- Various approaches for EDM
Sussex-RAL-ILL experiment

---
New method to make UCN
- Liberate neutrons by proton-induced spallation.
- Moderate (thermalize) in cold (20 K) D2O.
- Cold neutrons then “downscatter” to near zero energy (4 mK) in superfluid helium through phonon production.

---
KEK UCN Source (Masuda, et al)
At RCNP, Osaka,
1 a protons at 390 MeV
        → 19 UCN/cm3 to UCN detector.
Now accepting proposals for experiments.
e.g. R. Golub, et al.

---
New UCN Cryostat (KEK)
Design & Construction underway!

---
CANADA’S NATIONAL LABORATORY FOR PARTICLE AND NUCLEAR PHYSICS
Owned and operated as a joint venture by a consortium of Canadian universities via a contribution through the National Research Council Canada
- Gain Factors (40 mA @ 500 MeV):
  - Beam energy, power	x 70
  - Production volume	x 1.5
  - Storage lifetime	x 2.5
  - Transport eff	x 2
  - Ec3/2 (from 90 to 210 neV)	x 3.5
- Goal: 5000 UCN/cm3 in EDM cell.
- Lumi upgrade at RCNP to 10 mA allows tests thru summer 2014.
- Longer running time at TRIUMF (8 months/yr vs few weeks)

---
Location at
TRIUMF
UCN
Approx 20 x 20 m2 box
Pi-e-nu completion 2011

---
Layout in Meson Hall
n-EDM
experiment
Cryo
plant
radiation
shielding
Spallation
target +
UCN source
bender
kicker
septum

---
Layout and Overview
Kicker off
usual delivery
to SR
EDM
Experiment
area
W target
UCN Source
proton beam
from TRIUMF
cyclotron
quads/SM
bender
120 uA
kicker
septum

---
Layout and Overview
Kicker on
simultaneous delivery
to UCN and SR,
UCN density buildup
W target
UCN Source
40 uA
proton beam
from TRIUMF
cyclotron
quads/SM
bender
80 uA
kicker
septum

---
Layout and Overview
Kicker off
UCN diffuse out to
EDM experiment,
usual delivery to SR
UCN out
to EDM
Experiment
area
W target
UCN Source
proton beam
from TRIUMF
cyclotron
quads/SM
bender
120 uA
kicker
septum

---
Kicker
- Redirect 1A beam into UCN line on kHz timescale using existing TRIUMF beam structure.
- Integrated 7% to UCN, 93% to CMMS users.
- TRIUMF/CERN design
  - HV SS switches
  - Fast dipole magnet
- Engineering design.
M. Barnes

---
UCN beam line magnets
kicker
- Septum/bender magnets to be contributed by KEK
  - Lambertson design for septum
  - Sector design for bender (design completed by KEK almost ready for bids)

---
Other Technical Progress
at TRIUMF
- Target and Remote Handling
  - Conceptual design, RCNP / TRIUMF collaboration
- Radiation Shielding conceptual design, cost
- Cryo Plant
  - Leveraged by cash & in-kind contributions from KEK
- Project Management, Cost, Schedule, Human resources, Gantt charts, MOU's, etc.

---
n-EDM development in Japan
- Development of:
  - Comagnetometers
  - Ramsey resonance
  - New B-field geometry
  - HV, EDM cell
Masuda, et al. Beam tests July, December 2009, April 2010, early 2011.

---
Resonance Results
Ramsey Resonance Results
Dec. 2009, achieved:
T2 ~ 300 ms
April 2010, achieved:
T2 > 30 s !!!
becoming competitive with ILL,
where T2 = 120 s (typ.)
(stat)
Nearing state-of-the-art in low-field NMR!
Successful demonstration of technique behind precision EDM measurements.
Improve field homogeneity, profile, magnitude, shielding for longer T2, Jan 2011.

---
n-EDM Systematics
- magnetic field variations
- leakage currents
- geometric phase effect
  - false EDM arising from B-field inhomogeneity and E x v.
(co)magnetometry
comagnetometry
false EDM (GP) effect

---
Xe-129 buffer-gas nuclear spin comagnetometer
- Masuda-san's idea: leak polarized Xe-129 into the EDM cell with the neutrons and watch spins precess.
- Xe-129 pressure must be large
  - Xe-Xe Collisions -> small MFP -> small GPE.
  - Ring-down signal picked up by SQUID.
- Xe-129 pressure must be small
  - Electrical breakdown at higher pressures.
  - UCN absorption by Xe-129.
- There is a range of pressures in mTorr range that seems to work! Other idea: optical pickup (Chupp).

---
Complementarity
Project	H0 field	magnetometer	EDM cell	magnetic shielding
KEK / RCNP / TRIUMF	spherical / coil	129Xe buffer gas / co-magnetometer	small / T = 300 K	finemet/ / superconductor
Sussex / / RAL / ILL	solenoid	n at E = 0 / magnetometer	large / T ~ 0.5 K	μ metal / superconductor
SNS	cosθ coil	3He / co-magnetometer	large / T ~ 0.5 K	μ metal / superconductor
PSI	cosθ coil	Cs multi- / magnetometer	large / T = 300 K	μ metal
Another major difference: our UCN source is totally different.

---
Schedule and Goals
Phase	Goals	Year
RCNP	T2 to 130 s, HV	2011
	New source, improved UCN density	2011-12
	Horizontal EDM experiment, improvement of UCN density in EDM cell to 900 UCN/cm3, SC polarizer, precision Xe comagnetometry	2012-13
	In 20 days production running, dn < 1 x 10-26 e-cm	2013-14
TRIUMF	Commissioning and first experiment with same setup.	2015-16
	Further improvements to magnetic shielding, (co)magnetometry, EDM cell, detectors, dn < 1 x 10-27 e-cm	2016-17
	Improvements to cold moderator, magnetic shielding, beam current, targetry, remote handling, cryogenics, (co)magnetometry, dn < 1 x 10-28 e-cm	2018-

---
Project Status Report
- International Expert Review held at TRIUMF Sept 20-21, 2010, quote from committee report:
  “The committee strongly endorses the program and finds excellent potential for the group to contribute on a significant and competitive level to the worldwide efforts. The committee was impressed by the effort and creativity within the collaboration. The Japan-Canada UCN project has to be considered as an important research opportunity for KEK, RCNP, and TRIUMF, as well as for university collaborators to take on a leadership role in an exciting research field.”
- Top priority is to sign MOU (KEK-TRIUMF-RCNP-Winnipeg); it is required to release any CFI, MB, Winnipeg funds in Canada.

---
Summary
- Neutron EDM experiment and UCN source have developed in Japan, transported to Canada 2014.
  Goals: 10-26 -> 10-27 -> 10-28 e-cm.
- UCN source would be world-class facility for experiments beyond EDM: e.g. Neutron lifetime, Neutron Gravity levels experiment, Neutron beta-decay, nn oscillation search, neutron-ion interactions.

---
Thank you!
Osaka, July 2009.

---
Funding Status
- UCN source installation infrastructure
  - Support in Canada from CFI (Winnipeg), TRIUMF, Acsion Industries, MB Gov't.
  - Japan JSPS (Y. Masuda), plus additional KEK internal funds, RCNP Osaka internal funds.
- EDM experiment
  - Support in Japan by same + additional JSPS support to be sought.
  - Some CFI support received (Winnipeg).
  - Further NSERC/CFI/other support to be sought.

---
Funding Status
- HQP + Travel
  - NSERC support ramping FY2010-2013.
  - Supplementary support for new collaborators is being sought FY2011-2013.
  - Support through Winnipeg CFI matching
- General status
  - International Review of Program at TRIUMF Sept. 20-21, 2010.
  - Need signed MOU (KEK-RCNP-TRIUMF-Wpg)

---
Advantages of our UCN approach
- Liquid (superfluid) converter technology
  - Strong against thermal and radiation stresses
- Order of magnitude lower beam current
  - Less instantaneous radiation, heat, shielding
- Unique opportunity!
  - TRIUMF has ideal infrastructure
  - Able to develop new UCN source technology unique to all others
  - Opportunity for world's best in the future.

---
Advantages of our EDM approach
- Use established methods at room temperature.
- Smaller EDM cell and new DC coil geometry exploiting higher UCN density to suppress systematics.
- New Xe buffer-gas comagnetometer idea to further suppress systematics.
- Availability of new UCN source.