TECHNICAL REVIEW REPORT FOR AN ACCURATE MEASUREMENT

OF THE NEUTRON SPIN - ELECTRON

ANGULAR CORRELATION

IN POLARIZED NEUTRON BETA DECAY

WITH ULTRA-COLD NEUTRONS

UPDATED 4/11/00

California Institute of Technology

R. Carr, B. Filippone, T. M. Ito, C. Jones,

J.W. Martin, R. McKeown, B. Tipton, J. Yuan

Institut Laue-Langevin

P. Geltenbort

### Japan Atomic Energy Research Institute

K. Soyama

Los Alamos National Laboratory

T. Bowles (co-PI), M. Fowler, R. Hill, A. Hime, G. Hogan,

K. Kirch, S. Lamoreaux, C. Morris, A. Pichlmaeir, A. Saunders,

S. Seestrom, P. Walstrom, J. Wilhelmy

Petersburg Nuclear Physics Institute

A. Alduschenkov, A. Kharitonov, M. Lassakov

Yu. Rudnev, A. Serebrov, A. Vasilev

Princeton University

S. Hoedl, C-Y. Liu, D. Smith, A.R. Young (co-PI)

Tohoku University

T. Kitagaki

Tokyo Institute of Technology

K. Asahi

University of Kyoto

M. Hino, T. Kawai, M. Utsuro

University of Tokyo

T. Miyachi

# Virginia Polytechnic Institute and State University

M. Makela, M. Pitt, R.B. Vogelaar

TABLE OF CONTENTS

Section	Page

Title page	1

Table of contents	2

List of figures	6

Technical Overview

Executive Summary	8

UCN Source	10

Design of the Beta Asymmetry Experiment	11

Signals and Background Rates	13

Calibration	13

Systematic Effects	14

Cost Estimates	15

Schedule	16

Other Possible Future Experiments	17

Conclusion	18

Appendices

A1.  Scientific Justification

A1.1	Background Information	25

A1.2	Scientific Justification	25

A1.3	Theoretical Description of Polarized Neutron Beta Decay	26

A1.4	Weak Magnetism	28

A2.  Recent Reactor Measurements of the Beta Asymmetry

A2.1	Previous Status	30

A2.2	Perkeo	30

A2.3	IAE-PNPI	31

A2.4	ILL-TPC	31

A2.5	Perkeo II	32

A3.  Theoretical Implications

A3.1	Comparison of Experimental Results	37

A3.2	Comparison with 0+ ( 0+  Nuclear Beta Decay	37

A3.3	Unitarity of the CKM Matrix Comparison	37

A3.4	Theoretical Implications - Right-Handed Currents	38

A4.  Advantages of UCN Measurements of

Neutron Beta Decay Angular Correlations	46

Table of Contents (con’t)

Section	Page

A5.  The Prototype Solid Deuterium UCN Source

A5.1	Introduction	47

A5.2	The MLNSC Rotor Source	47

A5.3	The Prototype SD2 Source in the Blue Room at WNR	48

A5.3.1.  The Prototype SD2 Source	48

A5.3.2.  UCN Production in a Normal Para-ortho SD2 Source	49

A5.3.3.  UCN Production in an Ortho Deuterium SD2 Source	51

A5.3.4.  Loss Lifetimes in SD2	51

A5.3.5.  Measurements with an Ortho Deuterium SD2 Source	52

A6.  A Dedicated SD2 Source in Area B

A6.1	Introduction	68

A6.2	Improvements to the Existing Source	69

A6.3.	Signal Rates and Polarizations in the Beta Asymmetry	70

Experiment with an SD2 Source

A6.4.	Operational Issues of a Dedicated SD2 Source

A6.4.1.  Construction of a Dedicated SD2 Source	71

A6.4.2.  Beam Heating Issues	73

A6.4.2.  ES&H/Nuclear Facility Issues	75

A7.  Design of the Beta Asymmetry Experiment

A7.1	Experiment Layout	88

A7.2	Polarization of UCN	89

A7.3	Spin Flipping	89

A7.4	Depolarization of UCN	90

A7.5	Spectrometer

A7.5.1	Overview	93

A7.5.2	Magnetic Field Configuration	93

A7.5.3	UCN Beta Decay Trap	94

A7.5.4	Detector Systems	96

A7.5.5	Electronics	99

A7.5.6	DAQ	100

A8.  Expected Backgrounds

A8.1	Requirements	108

A8.2	Background Measurements	108

A8.3	Types of Backgrounds

A8.3.1	Spallation Source Backgrounds	110

A8.3.2	Natural Radioactivity - Room Backgrounds	110

A8.3.3	Natural Radioactivity - Spectrometer Backgrounds	111

A8.3.4	Cosmogenic Activities	111

A8.3.5	UCN-Related Backgrounds	111

Table of Contents (con’t)

Section	Page

A8.4	Expected Background Rate	112

A9.  Expected Count Rates and Statistical Accuracy

A9.1	Expected Signal Rate	115

A9.2	Monte Carlo Optimization of UCN Beta Decay Trap	115

A9.3	Statistical Accuracy	116

A9.4	Running Time Required	116

A10.  Calibration

A10.1	Conversion Line Sources	119

A10.2	Accelerator Sources	120

A11.  Systematic Effects

A11.1	Overview	125

A11.2	Neutron Polarization	126

A11.3	Depolarization	127

A11.4	Neutron Spin Alignment	127

A11.5	Variations in UCN Density

A11.5.1.  Spatial Variations in the UCN Density	128

A11.5.2.  Time Variations in the UCN Flux	129

A11.6	Backscattered Betas	130

A11.7	Scattered Betas	131

A11.8	Field Nonuniformities	132

A11.9	Magnetic Mirror Effect in the Field Expansion Region	133

A11.10	Fiducial Volume Definition	134

A11.11	Detector Inefficiencies	134

A11.12	Detector Resolution Function	135

A11.13	Detector Nonlinearity	135

A11.14	Detector Backgrounds	136

A11.15	Summary of Systematic Uncertainties	137

A11.16	Data Analysis	138

A12.  Calculation of Upscattering Rate in Para Deuterium	140

A13.  Detailed Cost Estimate

A12.1		SD2 Source	144

A12.2		Beta Asymmetry Schedule	146

A14.  Schedules

A14.1		SD2 Source Schedule	149

A14.2		Beta Asymmetry Schedule	150

Table of Contents (con’t)

Section	Page

A15.  Other Possible Future Experiments	151

A16.  Collaboration Responsibilities	154

A17.  Brief Biographies of the Collaboration Members	156

A18.  References		164

LIST OF FIGURES

Figure	Page

1	Results of beta asymmetry experiments (1999)	19

2	Sensitivity of proposed beta asymmetry experiment	20

3	Schematic view of the UCN solid deuterium source at LANSCE	21

4	Top view of the beta asymmetry spectrometer	22

5	Beta asymmetry spectrometer detectors	23

6	Plan view of Area B at LANSCE 	24

A2.1	Perkeo layout	33

A2.2	Neutron beta spectrum from Perkeo	34

A2.3	Beta decay asymmetry from Perkeo	34

A2.4	IAE - PNPI detector layout	35

A2.5	ILL - TPC layout	35

A2.6	Perkeo II layout	36

A3.1	Determination of GA vs. GV plot	40

A3.2	Results for GA vs. GV from beta asymmetry experiments (1999)	41

A3.3	Sensitivity of proposed beta asymmetry experiment	42

A3.4	Determination of Vud from neutron experiments	43

A3.5	Right-handed current exclusion plot for neutron data	44

A3.6	Sensitivity to right-handed currents of the proposed A experiment	45

A5.1.  Schematic view of the UCN rotor source at the MLNSC.	57

A5.2	Schematic view of the proposed dedicated SD2 source	58	A5.3	Schematic view of the SD2 prototype source	59

A5.4	Loss lifetimes in SD2 for a 0.8% HD	60

A5.5	Loss lifetimes in SD2 for a 0.2% HD	60

A5.6	Measured and calculated temperature dependence of UCN yield	61

A5.7	Measured and calculated time-of-arrival spectra at 8 K	61

A5.8	Detected neutron rates as a function of 3He pressure	62

A5.9	Layout of the experimental setup used in Line B	63

A5.10  Raman spectrum for D2.	64

A5.11	Measured temperature dependence of the UCN production rate	65

A5.12	Time spectrum of UCN bottle run	65

A5.13	Effect of para fraction on UCN production rate	66

A5.14	Measured volume dependence in the March run	66

A5.15	Time spectrum of an UCN bottle run with multiple beam pulses	67

A5.16  Dependence of UCN production rate on total proton charge	67

A6.1	Plan view of Area B at LANSCE	78

A6.2	Preengineering view of the SD2 source and storage bottle	79

A6.3	Schematic view of the proposed UCN storage arrangement	80

List of Figures (con’t)

A6.4	UCN production rate vs. target diameter	81

A6.5	UCN production rate vs. target length	81

A6.6	UCN densities for various moderator configurations	82

A6.7	Cold neutron spectra for various moderator configurations	82

A6.8	Stored UCN density vs. SD2 volume	83

A6.9	Scaled beta decay rate vs. SD2 volume	83

A6.10	UCN density vs. time after a proton pulse	84

A6.11	Initial ramp up to equilibrium in the UCN storage bottle	84

A6.12	Calculated temperature rise in the SD2 after a proton pulse	85

A6.13	Line B/C/switchyard  layout	86

A6.14	Line B layout	87

A7.1	Schematic view of the UCN polarizer/spin flipper	101

A7.2	Schematic view of the depolarization test system used at the ILL	102

A7.3	Top view of the beta asymmetry spectrometer	103

A7.4	Detector systems for the beta asymmetry spectrometer	104

A7.5	Cross-sectional view of the superconducting solenoid	105

A7.6	Schematic of the scintillator electronics	106

A7.7	Schematic of the wire chamber electronics	107

A8.1	Measured background spectrum w/o timing cut	113

A8.2	Measured background spectrum w timing cut	114

A9.1	UCN retention times for traps of various lengths	118

A9.2	Relative beta decay rates for different UCN traps	118

A10.1	Schematic view of the JPL electron dynamitron	122

A10.2	Scintillator energy spectra at the JPL dynamitron	123

A10.3	Si detector energy spectra at the JPL dynamitron	124

A11.1	Missed backscatter fraction for different B fields and foils	139

A14.1	SD2 source schedule	149

A14.2	Beta asymmetry schedule	150

1.  	EXECUTIVE SUMMARY

In the last several years, four measurements have been carried out using cold neutron beams at reactors of the angular correlation between the neutron spin and the direction of emission of the electron in polarized neutron beta decay, characterized by the coefficient A (and usually referred to as the beta asymmetry).  A measurement of the beta asymmetry involves a determination of the forward-backward asymmetry of the beta with respect to the direction of the neutron polarization.  A measurement of A, when combined with results from the neutron lifetime, provides a determination of the fundamental vector and axial vector weak coupling constants GA and GV.  The value of GV determined from neutron beta decay can also be compared with that determined from measurements of superallowed 0+ ( 0+ nuclear beta decay and with that determined by requiring that the Cabibbo-Kobayashi-Maskawi (CKM) matrix (which describes the mixing between quarks) be unitary.  This provides a sensitive means to search for new Physics beyond the Standard Model (such as right-handed currents), phenomena that are predicted to occur in a number of Grand Unified Field Theories (GUTs).  (A detailed scientific justification is given in Appendix 1.)

The recent four measurements of A using cold neutron beams at reactors all quote a combined statistical and systematic uncertainty of about 1% in the determination of A.  Unfortunately, the agreement between these four A measurements is poor and the results are also in disagreement with both the 0+ ( 0+ beta decay and the CKM unitarity results, as shown in Figure 1.  (Details of the four recent measurements of A can be found in Appendix 2.)  It may be that the differences are real and are due to the existence of new physics.  (Detailed descriptions of possible theoretical explanations can be found in Appendix 3.)  Of course, it may also be due to the existence of systematic problems in the different experiments.  In order to understand the origin of the discrepancies, it is obviously essential to carry out new measurements with very different systematic effects than those in the reactor experiments.  It is also equally important to improve the accuracy of these experiments in order to search for new physics with increased sensitivity.  The goals of the research described here are to address these issues with a measurement of the beta asymmetry with substantially improved accuracy.

A measurement of the beta asymmetry using Ultra-Cold Neutrons (UCN) provides significant advantages over reactor beam experiments.  As UCN can be transported through bent guide tubes, it is possible to place the experiment at a position distant (of order 10 m) from any neutron beam.  In addition, at a Short-Pulse Spallation Source (SPSS), one can suppress backgrounds significantly by using timing information so that data are excluded during the period just after the proton pulse strikes the spallation target.  It is also possible to polarize UCN to nearly 100% by passage through a magnetic field gradient with a maximum field of 7 Tesla.  Depolarization effects have been measured to be very small ( < 9 x 10-4), thus a UCN source with essentially 100% polarization can be constructed.

In this proposal, we lay out the essential elements of our plans to carry out a beta asymmetry experiment using a dedicated solid deuterium UCN source that we propose to construct in Area B at the Los Alamos Neutron Science Center (LANSCE).  Our goal is an initial measurement with an accuracy of about 0.2% of A (which has a value of approximately -0.114).  The precision of such a measurement, coupled with the most recent values (reported, but unpublished) of the neutron lifetime and reactor beta asymmetry measurements, is shown in Figure 2 for comparison.  The count rate expected in the proposed experiment of ≥ 100 Hz will allow a determination at this statistical accuracy level in a running time of one month.  Including setup time, systeamtic studies, and beam availability, we expect the experiment to take one year of calendar time to reach or exceed an accuracy of 0.2%.  It is important to note that the systematic effects in an experiment with UCN will be very different and much smaller (by an order of magnitude) than those in the reactor experiments.  Our estimates indicate that the total systematic uncertainty will be at the ( 4.2 x 10-4 level.  (We note that even if we did not make any corrections for systematic effects, the systematic uncertainty would still be below the 1.7 x 10-3 level and thus our result would still have an accuracy substantially better than in the previous experiments.)  With such accuracy, one could address the issues of the discrepancy between the 0+ ( 0+ decays and the unitarity of the CKM matrix.  With possible increases in the UCN source intensity and a better understanding of systematic effects, we ultimately expect to be able to improve the accuracy beyond that of existing experiments by an order of magnitude or better.  This would provide unprecedented sensitivity in the search for new Physics Beyond the Standard Model.

All of the technical requirements for the experiment are in hand and do not require any new, untested techniques.  Pending available funding, we expect to complete construction of a dedicated SD2 source in Area B and of the beta asymmetry experiment by the end of CY01.  We would then anticipate having a result at the 0.2% accuracy level by the end of CY02.  What is required to carry this out is capital equipment funds of about $1.52M.  Of this total, $155K has already been provided by the NSF through a MRI to Princeton University.  Of the remainder, $840K is being requested from the DOE and $525K from the NSF (through a MRI to Cal Tech).  We note that Los Alamos National Laboratory, Princeton University, the California Institute of Technology, Virginia Polytechnic, and the University of Kyoto are providing substantial support for this effort (a total of $1090K) and that a large amount of equipment already exists.

Our long-term goal (which is beyond the scope of this proposal) is to carry out a set of measurements of the allowed angular correlations in neutron beta decay (the correlation between the directions of emission of the electron and the recoil proton (the a coefficient), the beta asymmetry discussed above, the correlation between the neutron spin and the direction of emission of the recoil proton (the B coefficient), and of the neutron lifetime with an accuracy of 0.1% or better.  This would allow a determination of GA and GV solely within the neutron system with an accuracy better than any other technique.  In particular, this would avoid the problems associated with Coulomb effects and radiative corrections that must be applied to the 0+ ( 0+ nuclear beta decays to extract GV.  Such a precision would also allow a comparison with the CKM results, which would provide a means of searching for new Physics Beyond the Standard Model with a sensitivity comparable to what is expected to be achieved at high energy accelerators.

2.	UCN SOURCE

Ultra-Cold Neutrons are neutrons whose wavelengths are sufficiently long (typically greater than 500 Angstroms, which corresponds to 8 m/s neutron velocity) that they can undergo total external reflection at all angles from the surfaces of a variety of materials.  This leads to the possibility that ultra-cold neutrons can be totally confined within a bottle for periods in excess of 100 seconds, making a compact source of stored neutrons for use in measurements of fundamental physics.

There are two significant advantages that UCN offer compared to experiments done in-beam:  polarization and background.  It is possible to produce 100% polarization of UCN by passing the UCN through a strong magnetic field gradient.  In practice, passage through a field of 7 Tesla is sufficient to polarize 100% of the UCN.  This is due to the fact that the kinetic energy of an UCN is so small that UCN of one spin state cannot overcome the potential barrier due to the .B interaction of the neutron spin with the magnetic field.  Secondly, as the UCN can be piped out to a spectrometer located 10 m or more away from the primary neutron beam, it is possible to provide 100% coverage of the shielding and to have a background which is close to the intrinsic background of the spectrometer.  (A detailed discussion of the advantages of a UCN measurement of neutron beta decay angular correlations is found in Appendix 4.)

Until recently, the only existing sources have been at the Institute Laue-Langevin (ILL) reactor in Grenoble and at the Gatchina reactor in St. Petersburg.  In 1996 we constructed an UCN source on Flight Path 11B at the Manuel Lujan Neutron Scattering Center (MLNSC). This source makes use of the cold neutron beam produced by a LH2 moderator at the MLNSC.  The cold neutrons impinge on a set of moving mica crystals.  The cold neutrons Bragg scatter from the mica crystals and, as the mica crystals are moving away from the cold neutron beam, are Doppler shifted into the UCN regime.  This production mechanism for UCN is employed at the MLNSC at a position about 8 m from the LH2 moderator.  At that location a 6 cm x 6 cm mica crystal moving away from the neutron pulse at a velocity of 200 m/s has been installed on the end of a rotor that rotates in synchronism with the beam pulse rate. During each beam pulse, a puff of UCN is produced at the rotor.  The puff of UCN then expands outward and some fraction enters an UCN guide tube through which they are transported to the experimental area.  In 1997 this source reached a measured rate of 650 UCN/s at the end of a 3-m long 8-cm ID UCN guide.  In 1998 both the cold neutron source at the MLNSC and the rotor source were upgraded and we anticipate a flux in excess of 5,000 UCN/s from the source when beam becomes available again at the MLNSC in the spring of 2000.  However, as is explained below, we now plan to use this source only as an UCN test beam in developing equipment for use in the beta asymmetry experiment.

At the same time that we were working on the FP11B source, we also pursued the development (together with Prof. Serebrov’s group at the Petersburg Nuclear Physics Institute (PNPI)) of a solid deuterium (SD2) UCN source (as shown in Figure 3).  Initial results from PNPI were very encouraging and so in 1998-99 we constructed and tested the performance of a prototype SD2 source at LANSCE.  In this source, the 800 MeV proton beam from the LANSCE accelerator impinges on a stopping-length tungsten target where it produces about 18 neutrons per incident proton.  These spallation neutrons are reflected back by blocks of Be cooled to liquid nitrogen (LN) temperature.  They are then moderated to about 40 K by a set of polyethylene moderators that are at either LN or liquid helium (LHe) temperature.  In the center of the moderators is an 8-cm ID UCN guide tube coated with 58Ni in which up to 1 liter of solid deuterium can be condensed.  The cold neutrons produced in the polyethylene moderator can be downscattered into the UCN regime in the solid deuterium and are then trapped within the walls of the UCN guide holding the solid deuterium.  The UCN can exit only up the guide to an UCN storage bottle.  The source operates in a quasi-continuous mode: the full proton beam (1 mA peak current) impinges on the tungsten target for about 200 ms (4 macropulses) and is then switched off.  The UCN produced during this beam pulse fill the UCN storage bottle in about one second, after which time an UCN valve between the SD2 source and the UCN storage bottle is closed.  The UCN are filtered in the storage bottle for about one second (in order to ensure that any neutrons with a velocity higher than the critical velocity (8 m/s) of the 58Ni walls of the UCN storage bottle escape the bottle).  The valve between the UCN storage bottle and the guide to the beta asymmetry experiment is then opened. This cycle is repeated every 10 seconds.  Within 10 cycles an equilibrium density of 385 UCN/cm3 is established in the UCN storage bottle and a relatively constant flux of UCN is provided to the beta asymmetry experiment.  This quasi-continuous operation results in a time-averaged proton beam current of 4 A, a limit that is set by the requirement that the activation of the tungsten target does not exceed the threshold at which the UCN source would become a nuclear facility.  This type of operation also allows takes advantage of the low duty cycle of the proton beam (2%) so that we can take data only when there is no proton beam present.  This results in a substantial reduction in background while maintaining a high signal rate and only a small loss of counting time.

Our progress with this prototype source has been so rapid that we have now shifted all of our source work to focus on a dedicated SD2 source for use in the beta asymmetry experiment.  Thus, we are proposing to construct a dedicated SD2 UCN source in Area B at LANSCE as part of this proposal.  Our measurements indicate that using an optimized version of the prototype SD2 source with 4 A (time-averaged) beam on target we can exceed the beta decay rate that we expected with a fully upgraded rotor source by a factor of more than five.  (Details of the measurements made with the UCN source are given in Appendix 5.)  In addition, the characteristics of the SD2 source allow us to optimize the design of the beta asymmetry spectrometer and thus to further reduce systematic effects.  We expect that an optimized source can achieve beta decay rates in the beta asymmetry experiment in excess of 100 Hz with a first-generation SD2 source.

The UCN density anticipated in the SD2 source UCN bottle at LANSCE of 385 UCN/cm3 can be compared to the best existing UCN source in the world (at the ILL reactor) of 41 UCN/cm3 stored in a bottle directly attached to the source.  Thus, the first generation dedicated SD2 source at LANSCE will be the most intense UCN source in the world and is certainly sufficient to carry out a first-generation measurement of the beta asymmetry with an accuracy of 0.2%.

3.	DESIGN OF THE BETA ASYMMETRY EXPERIMENT

A 4 x 4 cm diamond-coated UCN guide tube will transport UCN from the SD2 source to the beta asymmetry spectrometer (located in the Area B hall at a distance of about 10 m from the UCN source).  The UCN will be 100% polarized by passage through a 7 T superconducting solenoid. The UCN will then pass through an Adiabatic Fast Passage (AFP) resonator that will allow rapid spin flipping of the UCN.  In our geometry, the adiabatic condition for spin flipping should be well satisfied and under less favorable conditions, experiments at SLAC achieved AFP spin-flip efficiencies of > 99.9%.  The UCN will then be fed to the center of the beta asymmetry spectrometer, as shown in Fig. 4.  (A detailed description can be found in Appendix 7.)

The spectrometer consists of a 3-m long, 10-cm diameter UCN open-ended trap that defines a decay volume for the UCN, as shown in Fig. 4.  A suitable wall material is diamond film, made by laser ablation from graphite, deposited onto the inner surface of a quartz tube.  Such a surface has a rather high effective potential (with a cutoff velocity of 6.95 m/s) and a loss rate corresponding to a lifetime of about 50 seconds at room temperature.  Furthermore, the depolarization time for such a surface would be extremely long.  Data from the ILL Electric Dipole Moment (EDM) experiment already provide a lower lifetime of 1000 s for the spin relaxation time.

A highly-uniform ( < 10-3 variation) strong (1.0 T) magnetic field is generated along the axis of the UCN trap by a superconducting solenoid. At the ends of the bottle, the magnetic field is expanded in the region before the detector.  The strong magnetic field in the solenoid is used to determine the neutron spin direction and is used to guide the betas from neutron decay in the bottle to the detectors, as shown in Figure 5.  Two detector systems will be used to measure the energy of the betas: Scintillator and Si-strip detectors.  The Si-strip detectors will provide an important systematic check on the performance and calibration of the spectrometer.  In the principal detector configuration the betas are detected in a Multi-Wire Proportional Chamber (MWPC) - scintillator system at the ends of the spectrometer in the expanded field region. This detector system allows both position information from the multi-wire proportional counters (MWPC), total energy information (from the scintillator), and some information on the pitch angle of the electron (from the dE/dx measurement in the MWPC).  The pitch angle of the betas decreases as the beta moves from the high field to the low field region, which reduces the backscattering amplitude of electrons from the MWPC windows and the scintillator, thus substantially reducing one of the largest systematic effects in measuring the beta asymmetry.  This geometry strongly suppresses backscattering effects by mirroring the backscattered betas back into the detector.  The spectrometer is shielded against both neutron and gamma backgrounds.  The overall layout of the UCN source and beta asymmetry spectrometer is shown in Figure 6.

The UCN exiting the decay tube are monitored in an array of UCN detectors (surface barrier detectors with a thin 6LiF layer plated onto them), are transported down a diamond-coated UCN guide to a 3He detector, or are captured on 6LiH surfaces in the region between the decay tube and the detectors.  Thus, the UCN are effectively pumped away at the ends of the decay tube, thereby strongly reducing the number of neutron decays in the field expansion region.  This arrangement  provides the means to monitor both the total number of UCN exiting the trap (using the 6LiF surface barrier detectors) as well as the number of UCN in the field expansion region.

We will be able to measure the depolarization of the UCN in situ by using the 7 T superconducting solenoid as both a polarizer and an analyzer.  This is done by polarizing the UCN when filling the UCN trap, closing off the trap for some time, then emptying the trap through the 7 T solenoid (now acting as an analyzer) and finally counting any wrong spin state neutrons left in the UCN trap.  By also installing additional UCN valves at the inlet of the polarizer, one can also search for depolarization effects due to multiple passes of the UCN through the AFP and polarizer.

4.	SIGNAL AND BACKGROUND RATES

We have carried out Monte Carlo calculations of the holding time integrated UCN density of UCN in the spectrometer, resulting in a bottle lifetime of 4.7 seconds, which results in a total decay rate in the bottle, based on the expected UCN production rate discussed above, of 116 Hz.

There are two features of the A experiment as designed that are central to achieving a high signal-to-background ratio (of order 200/1 with a threshold of 50 keV or lower):  the use of a strong magnetic guide field that allows 4 collection efficiency of the betas in a relatively small detector, and the use of a coincidence requirement between the proportional counter and scintillator.

Measurements were made during the UCN running period of July 1997 with plastic scintillators and wire chambers to determine the backgrounds that exist.  Differential shielding measurements were also carried out during that period to determine the amount of shielding that will be required for the A experiment.  We observed a background rate that has a fast component (due to prompt fast neutrons from the source after the proton pulse strikes the spallation target) which decays away with a time constant of a few milliseconds.  By gating out the the proton pulse and the first 5 ms following the pulse, we expect a background rate in the detectors of 0.5 Hz total rate from about 50 keV to 1.1 MeV.  (A detailed discussion of the expected backgrounds is given in Appendix 8.)

In order to achieve a given statistical accuracy , we expect that  = 2.7 / (N. We expect a total decay rate in the UCN bottle of 116 Hz.  (A detailed discussion of the expected signal rate is given in Appendix 9.)  We assume total detection efficiency of 98%, a fiducial volume cut of 69%, and a timing cut efficiency of 98%, which results in a counting rate after all cuts of 77 Hz.  We expect to acquire statistical data for 90 days (which results in 60 days of data acquisition, as discussed in Appendix 9.4), during which time we will observe 4.0 x 108 decays (we require only 1.4 x 108 decays to achieve a statistical accuracy of 2 x 10-3).  Thus, we can easily achieve a statistical accuracy of /A = 2.0 x 10-3.  We note the important fact that the signal to background will be about 220/1.

5.	CALIBRATION

Full calibration of the energy resolution function of the spectrometer is of paramount importance for a beta asymmetry experiment.  In the previous reactor experiments, this has been done using thin film conversion line sources such as 109Cd and 207Bi.  While we will certainly calibrate the spectrometer using this type of source introduced at the center of the spectrometer, it would be advantageous to have a source which filled the spectrometer active volume in the same manner as the UCN. At least one such a source does exist - several isotopes of Xe decay by internal conversion or by beta decay with energies up to a few hundred keV.  In addition to filling the UCN bottle region fully, such a source is massless and thus does not have the scattering tails typical of conversion line sources deposited on thin films.  The Xe isotopes can be easily produced in mCi quantities in one day of irradiation in a thermal reactor.  The lifetimes of the isotopes are relatively short (a few days to a few weeks), but enough of the Xe isotopes can be produced in a single irradiation to provide a useful source for 1 - 2 months.

It is also clear that in order to decrease detector systematic effects, it will be necessary to fully characterize the detector response using a high-resolution, variable-energy electron source.  We have carried out preliminary studies using a dynamitron at the Jet Propulsion Laboratory (JPL) in Pasadena that is capable of producing very low intensities of electrons that can be varied continuously in energy from 150 keV to 1.5 MeV.  A 5-150 keV electrostatic source has also been built at Cal Tech.  A simple double focusing spectrometer that has a measured resolution of E/E = 0.3% has also been built.  When used in conjunction with the two electron sources, it is possible to carry out extremely precise calibrations of the detector response from 5 keV to 1 MeV.  This will provide a full characterization of the detector systems on line and provide a check of our Monte Carlo simulations of the detector response.  (A more detailed discussion is given in Appendix 10.)

6.	SYSTEMATIC EFFECTS

| Systematic Effect | A/A | A /A |
| --- | --- | --- |
| Polarization (including neutron spin flipping) | ( 1 x 10-3 | ( 1 x 10-4 |
| Depolarization | < 9 x 10-4 | ( 1 x 10-4 |
| Spatial variations in UCN density | < 5 x 10-5 | < 5 x 10-5 |
| Temporal variations in UCN density | 2 x 10-5 | 2 x 10-5 |
| Neutron spin alignment | 1 x 10-4 | 1 x 10-4 |
| Subtotal UCN Systematic Effects | 1.4 x 10-3 | 2.1 x 10-4 |
| Backscattered betas | 1 x 10-3 | ( 2 x 10-4 |
| Scattered betas - residual gas contribution | < 1 x 10-5 | < 1 x 10-5 |
| Scattered betas - wall contribution | < 3 x 10-6 | < 3 x 10-6 |
| Field nonuniformities | 1 x 10-4 | 2 x 10-5 |
| Magnetic mirror effect | < 8 x 10-6 | < 8 x 10-6 |
| Fiducial volume definition | < 3 x 10-6 | < 3 x 10-6 |
| Subtotal Electron Collection | 1.0 x 10-3 | 2.0 x 10-4 |
| Detector inefficiencies | < 5 x 10-6 | < 5 x 10-6 |
| Detector resolution function | 3 x 10-4 | 3 x 10-4 |
| Detector nonlinearity | 6 x 10-5 | 6 x 10-5 |
| Detector backgrounds - room | ( 1 x 10-6 | ( 1 x 10-6 |
| Detector backgrounds - beam associated | < 1 x 10-7 | < 1 x 10-7 |
| Detector backgrounds - UCN related | < 4 x 10-6 | < 4 x 10-6 |
| Subtotal Detector Effects | 3.0 x 10-4 | 3.0 x 10-4 |
| TOTAL | 1.7 x 10-3 | 4.2 x 10-4 |

Table 1.  Systematic effects and uncertainties.  A/A is the size of the systematic effect relative to A (which has a value of -0.114) and A /A is the size of the systematic uncertainty relative to A.

A central issue in accurately determining the beta asymmetry is the systematic uncertainties in the measurement.  As noted above, UCN offer significant reductions in the major systematic effects in a measurement of the beta asymmetry.  The systematic uncertainties can be broadly divided into three categories: those concerning knowledge of the A) neutron spin-dependent effects, B) electron collection, and C) detector-related effects.  (A detailed discussion is given in Appendix 11.)

The uncertainty in each of the systematic effects is summarized in Table 1.  The total systematic uncertainty is determined by adding the individual systematic uncertainties in quadrature.  We expect that the total systematic uncertainty will be A /A  ( 4.2 x 10-4.  Just as important, the total correction due to systematic effects (A/A) is less than 1.7 x 10-3.  For comparison, the total systematic uncertainty in PERKEO II was 6 x 10-3.  Thus, even if we did not make any corrections for systematic effects, our systematic uncertainty would still be a factor of three better than that quoted by the best experiment to date.

7.	COST ESTIMATES

7.1.	SD2 SOURCE COST ESTIMATE

| Item | Collaboration | DOE TO LANL |
| --- | --- | --- |
|  | Cost ($K) | Cost ($K) |
| Line B |  | 64.2 |
| Area B Cave |  | 51.2 |
| Tungsten Target |  | 116.8 |
| SD2 Moderator | 39.3 | 72 |
| UCN Storage Bottle | 19.3 | 57.7 |
| UCN Guide | 18.5 | 84.5 |
| Subtotal | 77.1 | 446.4 |
| Contingency (17%) |  | 78.0 |
| Subtotal w Contingency | 77.1 | 524.4 |
| MAT Tax (3.25%) |  | 17.0 |
| G&A Taxes (31%) |  | 167.9 |
| Total | 77.1 | 709.3 |

Table 2.  Summary of the cost estimates for construction of the SD2 UCN source.  All costs are in FY00 dollars.

A summary of the costs of the equipment required for the SD2 UCN source is given in Table 2 and a summary of the costs of the beta asymmetry experiment is given in Table 3.  We note that the cost estimates given above are the costs for purchase requests issued. A total of $1090K of the equipment listed above is available or will be purchased from funds from within the collaboration.  The request to the Department of Energy is for a total of $840K for the dedicated SD2 source and beta asymmetry spectrometer including contingency and LANL taxes.  The request to NSF is for $680K including contingency (no taxes), of which $155K has already been provided to Princeton University.  (A detailed breakdown of costs is given in Appendix 13.)

7.2.  BETA ASYMMETRY EXPERIMENT COST ESTIMATE

| Item | Collaboration | DOE To LANL | NSF To Princeton | NSF To Cal Tech |
| --- | --- | --- | --- | --- |
|  | Cost ($K) | Cost ($K) |  | Cost ($K) |
| UCN Rotor Test Source | 655.0 |  |  |  |
| Superconducting Solenoid |  |  |  | 467.0 |
| Resistive Coils | 15.0 |  |  | 33.0 |
| AFP/Polarizer | 22.2 |  | 155.0 |  |
| UCN Beta Decay Trap |  | 59.7 |  |  |
| Vacuum Systems | 47.5 |  |  |  |
| UCN Detectors | 74.4 |  |  |  |
| Beta Detectors | 204.0 |  |  |  |
| Shielding |  | 13.5 |  |  |
| Enclosure |  | 7.2 |  |  |
| Calibration | 40.0 |  |  | 15.0 |
| Subtotal | 1058.1 | 80.4 | 155.0 | 515.0 |
| Contingency (16%) | 30 | 15.0 |  | 10.0 |
| Subtotal w Contingency | 1088.7 | 95.4 | 155.0 | 525.0 |
| MAT Tax (3.25%) |  | 3.1 |  |  |
| G&A Taxes (31%) |  | 30.5 |  |  |
| Total | 1088.1 | 129.0 | 155.0 | 525.0 |

Table 3.  Summary of the cost estimates for construction of the beta asymmetry experiment.  All costs are in FY00 dollars.

8.	SCHEDULE

A more detailed schedule is laid out in Appendix 14.  Basically we plan to complete the SD2 source development runs in the spring of 2000 and start final design of the dedicated SD2 source after that.  We will work on reinstalling Line B while the source is being designed and be ready for installation of the source by the fall of 2000.  It will take approximately 9 months to construct and install the SD2 source and 3 months to commission it.  Thus, by the fall of 2001 we expect to have a dedicated SD2 source on line and operational.

The beta asymmetry equipment consists of three primary parts: the polarizer/spin flipper, the detectors, and the spectrometer.  Work on all three of these components will start in the summer of 2000.  We expect to complete the spin flipper by the fall of 2000 and have the detectors and spectrometer ready by early summer of 2001. We also expect to complete construction of the beta spectrometer by the summer of 2001.  It will take about 6 months to commission the experiment and carry out calibrations.  Thus, we expect to start data acquisition at the start of CY20002.

The LANSCE accelerator is expected to provide beam nine months out of each calendar year.  The normal cycle is expected to be three months of beam followed by one month of beam off.  We estimate that approximately 2 months of time will be required in initial operation and debugging.  Given an overall duty factor of 67% (as discussed in Appendix 9), this corresponds to three months of data acquisition. We then plan five months of systematic studies (one month of beam off followed by three months of beam on followed by one month of beam off).  In the third beam cycle, we plan for three months of data acquisition (60 days of actual data).  Thus, we anticipate that the experiment will require 12 calendar months of operation in CY 2002.  This allows a factor of 500% contingency in running time.  With this very conservative schedule, we feel confident we can reach the quoted accuracy within the schedule we have laid out.

9.	OTHER POSSIBLE FUTURE EXPERIMENTS

While this proposal has dealt specifically with a beta asymmetry measurement, we plan to carry out other neutron beta decay experiments using a modified spectrometer.  Specifically, by incorporating the ability to detect the recoil protons into the spectrometer, we will be able to directly measure the electron-neutrino (a) and neutron spin-neutrino (B) angular correlations.  While we have not yet studied the systematic effects in either the a or B experiments, scaling from our estimates of the systematics in the beta asymmetry experiment, we believe that measurements of the a and B correlations could be made with accuracies improved by an order of magnitude or more over present experiments.  The count rates should also be sufficiently high and the backgrounds sufficiently low to allow an accurate measurement of weak magnetism with a SD2 source.  The possibility of measuring the time-reversal violating correlation D also looks promising with a SD2 source and initial estimates indicate it may be possible to improve the sensitivity by two orders of magnitude over the currently published limits.  We would also pursue an accurate measurement of weak magnetism which would provide a strong test of the Conserved Vector Current Theory.  (Additional information on other possible experiments is given in Appendix 15.)

The recoil protons can be detected by accelerating them to about 35 keV through a thin entrance window of a Multi-Step Avalanche Counters (MSACs). These are counters in which the E / p (electric field to pressure) ratio is so high that multiplication occurs in the gas throughout the volume of the detector.  A very high signal to background ratio in MSACs can be achieved for the recoil protons.  We would anticipate installing these counters in the spectrometer following completion of the beta asymmetry experiment to start a and B correlation experiments.

We also plan to investigate the possibility of using Time Projection Chambers (TPCs) for tracking of the betas.  It would then be possible to track in three dimensions the betas from neutron beta decay.  By placing the TPC in a strong magnetic field it would be possible to measure the radius of curvature of the tracks.  This would represent a significant improvement in the beta energy resolution over that possible with a scintillator.  Just as important, the tracking information would provide directly the emission angle of the beta with an angular resolution of a few degrees.  This would provide two additional benefits:  1)  instead of averaging over the 2 solid angle (with its resultant loss of sensitivity of a factor of 2), one could directly fit the entire cos distribution, and 2)  the increased ability to study systematic effects in detail.  In addition, the statistical power of the data would increase, as the factor of 2.0 reduction in statistical significance (see section A9.3) would go to unity if we could reconstruct the angular information in the decay with perfect precision.

We are also investigating the use of Time Projection Chambers (TPCs), Si(Li), Si, other tracking devices, and electrostatic and magnetic spectrometers, with the goal of carrying out high-resolution, low-background measurements of the beta and recoil proton spectra and correlations in polarized and unpolarized neutron beta decay.

Thus, a continuing program of precision measurements of UCN beta decay is envisaged using various modifications of the beta asymmetry spectrometer.  These measurements will provide unparalleled sensitivity to new physics.

10.	CONCLUSION

The total uncertainty in our measurement of the beta asymmetry is obtained by adding the expected statistical and systematic uncertainties in quadrature resulting in an expected total uncertainty in A of 2 x 10-3, an improvement by a factor of five over the best reactor experiment.  We expect to achieve this level of accuracy by the end of CY 2002.  This would allow us to address the important physics issues of the disagreement between the 0+ ( 0+ beta decays and the unitarity of the CKM matrix.  The impact in the science community of this result would be far beyond that of simply determining the value of  and providing a resolution of the current experimental situation.

All of the major issues in the experiment have been dealt with and shown to be tractable at the < 2 x 10-3 level.  No new technology is required and this proposal requests only capital equipment funds.  The experiment can produce a result within three years with an accuracy substantially better than any other experiment to date or any that are planned.  A continuing research program in neutron beta decay is envisioned following completion of the initial beta asymmetry experiment.

Figure 1.  Results for the neutron decay beta asymmetry measurements as of 1999, and the values of GV determined from 0+ ( 0+ superallowed beta decay and from requiring unitarity of the CKM matrix.

Figure 2.  Projected sensitivity for GV and GA for the proposed beta asymmetry experiment and results for the most recent neutron lifetime experiments as of 1999 showing the sensitivity of our proposed beta asymmetry measurement.  The central value for our proposed measurement has been arbitrarily set to coincide with the value of GV determined by requiring unitarity of the CKM matrix.

Figure 3.  Schematic view of the proposed SD2 source.  The aluminum window shown on the drawing was removed after the first set of runs with the prototype source.

Figure 4.  Top view of the beta asymmetry spectrometer

Figure 5.  View of the detector system for the beta asymmetry spectrometer.

Figure 6.  Plan view of Area B at LANSCE.  The dedicated SD2 source would be located in the cave marked LD2 target.  The UCN beta asymmetry experiment would be located in the Area B Hall (close to where the old MRS spectrometer is shown).

APPENDIX 1

SCIENTIFIC JUSTIFICATION

A1.1.  	BACKGROUND INFORMATION

Ultra-Cold Neutrons are neutrons whose wavelengths are sufficiently long (typically greater than 500 Angstroms) that they can undergo total external reflection at all angles from the surfaces of a variety of materials.  This leads to the possibility that ultra-cold neutrons can be totally confined within a bottle for periods in excess of 100 seconds, making a compact source of stored neutrons for use in measurements of fundamental physics.

The only existing sources have been at the ILL reactor in Grenoble and at the Gatchina reactor in St. Petersburg.  UCN research at these facilities has resulted in the most sensitive measurements to date in the search for an electric dipole moment (EDM) of the neutron 1-2) and in the highest precision measurements of the lifetime of the neutron. 3-6)  Both of these measurements are of great fundamental interest;  the neutron EDM in trying to elucidate the origin of CP violation, and the neutron lifetime in determining the weak axial vector coupling constant and in a number of astrophysical applications, such as determining the number of light neutrino species in Big Bang nucleosynthesis.

The benefit of using UCN in fundamental physics was recognized in the Long Range Plan formulated by the Nuclear Science Advisory Committee (NSAC) in 1989 in which it was stated "A facility judged to be of major importance to this field (precision tests of fundamental interactions) is a source of cold and ultra-cold neutrons.  The lack of first-rate sources in the US. is limiting basic experiments on parity violation, time-reversal violation, and the lifetime, electric dipole moment, and beta decay angular correlation of the free neutron."

A1.2.	SCIENTIFIC JUSTIFICATION

Our current understanding of the physical world is embedded in the Standard Model, which describes the structure of the strong, electromagnetic, and weak forces as:

SU(3)C  SU(2)L  U(1)EM.

The Weinberg-Salam-Glashow (W-S-G) model of the electroweak interactions is contained within this and provides us with a pure left-handed (V-A) interaction.  While this of course reproduces the observed state in nature, the Standard Model does not provide any underlying reason for this structure, it is not able to predict the observed mass spectrum of quarks and leptons, it does not reduce the number of coupling constants of the interactions, nor does it include gravity.  While the Standard Model is in spectacular agreement with all experimental data, it is assumed that it is only part of a larger model.  It is this belief that has motivated the formulation of Grand Unified field Theories (GUTs), SUperSYmmetric (SUSY) theories, and String Theories.  All of these theories attempt to unify the weak nuclear, electromagnetic, and strong nuclear forces in a single, comprehensive theory.  They generally predict that a range of new phenomena beyond the Standard Model should exist, including proton decay, non zero neutrino masses and mixing, right-handed currents, and new particles. In the past two decades, much effort has been expended in searching for new physics beyond the Standard Model.  One area in which the Standard Model can be probed is neutron beta decay.  In particular, measurements of angular correlations in neutron beta decay can place constraints on the existence of right-handed currents, the presence of scalar and tensor terms in the weak interaction, and for evidence of Time Reversal Violation, which is expected from the observed violation of CP invariance in kaon decay.

In order to search for new physics beyond the Standard Model, one possible strategy is to measure known quantities with ever increasing accuracy and precision and hope to find a difference between the Standard Model predictions and the measurements.  Another possible strategy is to probe for effects that are not included in the Standard Model, but are predicted by the Grand Unified field Theories.  Angular correlation measurements in neutron beta decay provide a means to pursue both strategies.  By accurately and precisely measuring the coefficients of the allowed angular correlations (electron-neutrino, spin-electron, and spin-neutrino) one can search for the presence of right-handed currents and scalar and tensor terms in the weak interaction.  All of these correlations are non-zero with a value precisely defined in the Standard Model.  By searching for a time-reversal-violating correlation coefficient (which is expected to be zero in the Standard Model), one can test for the existence of Time Reversal Violation.  Thus, the need for experiments with ever increasing accuracy and precision in neutron beta decay is clear.

A1.3.  	THEORETICAL DESCRIPTION OF POLARIZED NEUTRON BETA DECAY

One can write the Hamiltonian which provides the most complete description of neutron beta decay as 7) :

Hint = i (p i n)[e (Ci i +C i' Gi5)]  +  h.c.

where p, n, e,  are the spinor wavefunctions of the proton, neutron, electron, and antineutrino, respectively, h.c. is the Hermitean conjugate, and

i = 1, /√2, i5, 5

expressed in terms of the usual Pauli matrices.  Under the most general assumptions that allow possible time reversal violation and both right- and left-handed currents, there are 19 real free parameters.  If one places the condition of time reversal invariance on the Hamiltonian, then there are still 10 arbitrary constants.  The matrix element M for neutron beta decay can then be written using this Hamiltonian in a current-current formulation as 8) :

M = (2)4 (G/√2) jl jn

where G is the Fermi coupling constant, and

jl = -i ue  (1 + 5)  ue 

where ue and ue are the electron and spinor wave functions, and

jn = jV + jA

where

jV = i  up  GV - (GM - GV) q / 2mn - i Gs q / 2mn  un 

jA = i  up  GA - GII q / 2mn - i Gp q / 2mn  un 

and the form factors describe the vector (GV), axial vector (GA), induced pseudotensor (GM - GV), induced tensor (GII), induced scalar (Gs), and induced pseudoscalar (Gp) interactions.

The differential probability that a polarized neutron will decay with the emission of an electron and an antineutrino in specified directions is given by 8) :

d3W(pe, p) = dW(pe)ded [ 1 + a pe . p /EeE

+  . (A pe/Ee + B p/E  + D pe x p/EeE) ]

where Ee and Eare the full energies of the electron and anti-neutrino, de and d are the elements of solid angle for the electron and neutrino respectively, is the neutron spin, and pe and p are the electron and anti-neutrino vector momenta respectively.  The coefficients correspond to the electron-neutrino (a), neutron spin-electron (A), neutron spin-neutrino (B), and time reversal violating (D) correlations, respectively.  We note that if time reversal is a valid symmetry (which is only approximately true) that D would vanish.

It is possible to write the correlation coefficients in terms of the ratio of the axial vector (GA) and vector (GV) coupling constants as 8) :

a = (GV2 - GA2) / (GV2 + 3 GA2)

A = -2 (GAGV cos+ GA2) / (GV2 + 3GA2)

B = 2 (GA2 - GVGAcos) / (GV2 + 3GA2)

D = 2 GAGV sin / (GV2 + 3GA2)

Ftn = constant / (GV2 + 3GA2)

where  is the phase angle between the vector and axial vector couplings (we note that  = 180o if time reversal invariance holds).

These equations are often expressed in terms of the ratio of GA and GV where

 = GA / GV  = exp (i).

In terms of , the correlation coefficients can be written as:

a = (1 - 2) / (1 + 32)

A = -2 (2 + cos) / (1 + 32)

B = -2 (2 - cos) / (1 + 32)

D = 2  sin / (1 + 32)

Ftn = constant  / [ GV2 (1 + 32)}

In the above definitions of the correlation coefficients, we have not included the possibility of scalar and tensor terms or of right-handed currents.  These can easily be included in a rather more complicated definition.9-10)  For the sake of simplicity, the more complicated expressions are not given here.

From the above equations, one can see that measurements of the neutron lifetime and a decay correlation can be combined to determine the value of GV . A difference between the value of  GV from neutron experiments and that  from the purely  vector decay of complex nuclei (super-allowed  decays) would be an indication of physics beyond the Standard Model.

A1.4.	WEAK MAGNETISM

The magnitude of weak magnetism is predicted by the Conserved Vector Current (CVC) theorem, which relates the weak magnetism form factor to the anomalous magnetic moments of the neutron and proton.  Previous tests 11-13) of CVC in masses 8, 12, and 20 have resulted in accuracies of only about 10-15%, and concern about the precision in some of the measurements due to possible systematic effects has been raised.  Thus, it is quite important to provide an accurate and precise test of CVC.  In principle, the beta decay of the neutron offers an ideal place for such a test. In addition, the Conserved Vector Current hypothesis can be used to relate GV to the muon-decay coupling constant GF, by the relation , where  is the first element of the CKM matrix and fcorr  is the radiative correction.  The comparison of GV from neutron decay experiments with GF from muon decay can be used to extract Vud and hence to perform a test of the unitarity of the CKM matrix.

The effect of weak magnetism is to produce an energy dependent term in the decay amplitude:

W(Ee, ) = (allowed spectrum) x {(1 + awmE) + n . pe/E (A + a'wmE)} dE d

where awm and a'wm are the amplitudes of the weak magnetism form factors, which are predicted by CVC to be 8) :

awm = 3.4 x 10-3/MeV and a'wm = 2.1 x 10-3/MeV.

Thus, the measurement of the weak magnetism form factor a'wm requires an accurate determination of the energy dependence of A.  Due to the small effects in the energy dependence that must be measured accurately to provide an interesting test of CVC, backgrounds have to date presented an insurmountable obstacle in trying to measure weak magnetism.  A measurement with UCN may provide a means of substantially reducing backgrounds and thus providing the ability to measure weak magnetism in the neutron.

#### APPENDIX 2

RECENT REACTOR MEASUREMENTS OF THE BETA ASYMMETRY

A2.1.	PREVIOUS STATUS

Prior to 1990, essentially all of the measurements of angular correlations in neutron beta decay agreed well with each other and arrived at a common value of .  A combined analysis of the data (together with measurements of the neutron half-life and 0  0 nuclear beta decay) yielded 14) :

 = -1.261  0.004	(from correlation measurements)

while

 = - 1.267  0.007	(from neutron lifetime measurements)

indicating good agreement between the different techniques of determining .  An analysis 9) for the possible presence of scalar, tensor, or right-handed components of the weak interactions indicated that the data were consistent with a pure V - A interaction and set limits on the possible contributions of either pure scalar or pure tensor at about the 10-15% level, and a limit on possible V + A contributions at about the 10% level.  Possible combinations of scalar plus tensor contributions could not be ruled out at less than about the 40% from neutron beta decay measurements alone.

Since 1985, four measurements of the beta asymmetry have been carried out.  We now go on to discuss each of the four experiments.

A2.2.	PERKEO

A precise measurement 15-17) was made at ILL using the PERKEO spectrometer, which is shown in Fig. A2.1.  In this experiment, a beam of cold neutrons are polarized by a supermirror polarizer, strongly collimated to restrict the beam divergence, and then pass through the bore of a 2-m-long superconducting magnet.  A small fraction (( 10-6) of the neutrons decay within the solenoid.  The betas spiral along the field lines and are deflected out of the beam at the ends of the solenoid by a set of transverse field coils.  The betas are then detected in plastic scintillators at the two ends of the solenoid.  In this apparatus the signal-to-noise was improved by enhancing the signal by collecting all the electrons from a large decay volume.  Another advantage to this scheme is that any betas which backscatter from the scintillators either are reflected back into the scintillator by the magnetic mirror effect, or are detected a few tens of ns later in the scintillator at the other end.  Timing information allows one to determine which scintillator was hit first, thus largely eliminating effects due to backscattering.

The PERKEO experiment determined the value of A to be:

A0 = -0.1146 ± 0.0019.

resulting in a determination of  of

 = - 1.262 ± 0.005

The subscript 0 on A0 indicates that the measured asymmetry A has been modified to incorporate radiative corrections that must be applied in order to derive the correct value of .  Figs. A2.2 and A2.3 show the neutron beta decay spectrum and experimental asymmetry respectively measured with the Perkeo spectrometer.

The experiment was limited predominantly by systematic effects associated with the transverse magnetic fields at the ends of the solenoid, differences in the backgrounds in the two detectors, and the determination of the absolute neutron polarization.

A2.3.	IAE - PNPI

A measurement in which the recoil proton was measured in coincidence with the beta was carried by the Institute for Atomic Energy (IAE) and the Petersburg Nuclear Physics Institute (PNPI) at the Gatchina reactor as shown in Fig. A2.4. 18)  The experiment did not use a supermirror polarizer and thus had relatively low polarization (( 76%).

The IAE experiment determined the value of A to be:

A0 = -0.1116 ± 0.0014,

resulting in a determination of of

 = - 1.2544 ± 0.0037

The largest systematic effect in this experiment was the large correction required for the low polarization.

A claim has been made recently that the technique used to correct for the polarization in this experiment was in error.  19)   The magnitude of this effect is such as to reduce the value of Ao and thus for GV.  The revised correction has now been submitted for publication 20) and results in a new value of A of:

A0 = -0.1135 ± 0.0014.

Thus, the corrected result will move the deduced value of GV to be in closer agreement with the value quoted by the PERKEO I measurement.

A2.4.	ILL - TPC

This measurement was carried out at the Grenoble reactor at the Institute Laue-Langevin and involved having a cold neutron beam pass through a Time Projection Chamber (TPC), as shown in Fig. A2.5.  The direction of the track was reconstructed with crude angular information using the TPC information. The result of the ILL - TPC measurement was  21) :

A0 = -0.1160 ± 0.0015

resulting in a determination of f

= - 1.266 ± 0.0040

The primary systematic problem in this experiment was the background that resulted in 0.8% uncertainty in the background subtraction.  In addition the angular dependence of the asymmetry was measured in this experiment, however the results were not in agreement with expectations. Due to this difficulty, the angular information was integrated over to obtain the final results.

A2.5.	PERKEO II

An improved version of the PERKEO spectrometer, called PERKEO II, has provided new results.  The primary difference is that instead of a superconducting solenoid, the experiment used a completely transverse magnetic field produced by a set of superconducting coils, as shown in Fig. A2.6.  This effectively reduces the systematic uncertainty due to magnetic mirror effects.  The value of A measured in Perkeo II was 22) :

A0 = -0.1189 ± 0.0012

resulting in a determination of f

= - 1.2738 ± 0.0033

The remaining dominant limitations to the precision of a new measurement with PERKEO II are due to the precision with which the absolute value of the polarization can be measured and the backgrounds associated with the cold neutron beam from the reactor.  The systematic uncertainty associated with the polarization measurement was primarily due to possible depolarization caused by the chopper wheel (which proved to be slightly magnetic) used to measure the wavelength dependence of the polarization.  This problem has been addressed in a second set of measurements carried out at the ILL.  The results from the improved PERKEO II run resulted in a value of:

A0 = -0.1189 ± 0.0008

resulting in a determination off

= - 1.2740 ± 0.0021

Thus, the central value basically did not change but the uncertainty was reduced by 33%.  The latest PERKEO II result is shown in Figure 2 which graphically shows that the disagreement between the four existing reactor measurements of the beta asymmetry has become even worse with the latest PERKEO II result.

Figure A2.1.  Perkeo layout

Figure A2.2.  Neutron beta decay spectrum measured by Perkeo.

Figure A2.3.  Polarized neutron beta decay asymmetry measured by Perkeo.

Figure A2.4.  IAE - PNPI detector layout.

Figure A2.5.  ILL-TPC layout.

Figure A2.6.  Perkeo II layout.

APPENDIX 3

THEORETICAL IMPLICATIONS

A3.1.	COMPARISON OF EXPERIMENTAL RESULTS

The four measurements of the A coefficient within the last ten years all claim to have a combined uncertainty of the statistical and systematic uncertainties of order 1%.  When combined with measurements of the neutron lifetime and 0+ ( 0+ nuclear beta decay, it is possible to uniquely define the quadrant of the GA vs. GV plot, as shown in Figure A3.1.  Unfortunately, the agreement of the experimental results is poor, as shown in Figure A3.2 (which shows a blow-up of Figure A3.1 of the intersection region of the values of GV and GA determined from the neutron lifetime, neutron beta asymmetry, 0+ ( 0+ beta decay, and unitarity of the CKM matrix).  Figure A3.2 shows the status as of 1997, based on the published results of the neutron lifetime 28) and the published values of the beta asymmetry from the four reactor measurements (as discussed in Appendix 2).   A partial resolution of this discrepancy is shown in Figure A3.3 in which the newly-reported corrected value of the IAE result is shown,20) together an improved determination of the neutron lifetime which has been reported by the PNPI group at the ILL reactor.29)  For comparison, the accuracy of the proposed beta asymmetry experiment is shown in Fig. A3.4 in which the most recent lifetime measurements are included and the central value of GV as determined in the proposed beta asymmetry experiment has been arbitrarily set to agree with the value of GV as determined by requiring unitarity of the CKM matrix.

A3.2.	COMPARISON WITH 0+ ( 0+  NUCLEAR BETA DECAY

The value of GV can be determined from 0+ ( 0+ superallowed nuclear beta decay.  To date, this decay rate has been measured in nine nuclei.  The experimentally measured quantity of interest is the Ft value for these decays.  From the average Ft value of these decays, one can deduce the value of GV after applying corrections for the finite nuclear size Coulomb and radiative effects.  The size of these corrections is similar in magnitude to the quoted accuracy deduced for GV.  A systematic analysis was made  of these corrections and it was deduced that in order to get agreement between all of the superallowed 0+ ( 0+  beta decays that one had to include additional ad hoc corrections due to Coulomb effects. 24,25) Although recent experimental results on 10C do not seem to indicate any need for such additional effects, 26,27) this situation has led one to question the validity of extracting GV with the quoted precision from 0+ ( 0+ superallowed nuclear beta decay.

A3.3.	UNITARITY OF THE CABIBB0-KOBAYASHI-MASKAWA MATRIX COMPARISON

In the Standard Weinberg-Salam-Glashow electroweak model, there are only three generations of quarks.  The mixing between the quarks is described by the CKM matrix.  If the Standard Model assumption of only three generations is correct, then the CKM matrix is required to be unitary.  From measurements of various hadronic and meson decays, measurements of all of the important (i.e., large mixing) matrix elements of the CKM matrix have been made.  One thus has an overdetermined system and by using the values of all of the CKM matrix elements except Vud (the mixing matrix element between the up and down quarks) and requiring unitarity of the CKM matrix, one can deduce the value of Vud.  GV and GA are related to Vud by the expressions

GV = GF Vud

and

GA = GF Vud 

where GF is the Fermi coupling constant and  = GA/GV.  A measurement of the beta asymmetry in neutron beta decay and a measurement of the neutron lifetime provides a measurement of GA and GV.  GF is known from muon decay, and so solving for Vud results in the value shown in Fig. A3.5, which is in disagreement with the value of Vud deduced from 0+ ( 0+ superallowed nuclear beta decay as well as being in disagreement with the beta asymmetry results.

A chief theoretical impetus for improved measurements of Vud is that one possible source of a violation of CKM unitarity is the assumption of only three generations. While three generations of leptons have been precisely confirmed at e+ e-  colliders, this result is valid only for light neutrino species [m < M(Z/2)]. A violation of unitarity of the CKM matrix would thus have profound implications for our understanding of elementary particles.

Precision measurements of Vud that confirm unitarity are also very important. In fact, with an order-of-magnitude improvement in the neutron asymmetry A and a factor of 2 - 4 improvement in measurements of the neutron lifetime, the neutron could provide the best measurements of Vus. This occurs by assuming unitarity and then due to the smallness of Vud  we have V2us =  1 - V2ud. This parameter is a key component of the ``Unitarity Triangle'' that allows Standard Model predictions of CKM induced CP-violation in the B meson system.

A3.4.	Possible theoretical Implications - Right-Handed Currents

If one formulates the weak interactions in a left-right symmetric model, the presence of right-handed currents corresponds to the existence of a right-handed gauge boson WR in addition to the conventional left-handed gauge boson WL.  WL and WR are combinations of two mass eigenstates W1 and W2 with masses m1 and m2.  Thus,

WL = cos   W1 + sin   W2

WR = -sin  W1 + cos  W2

where  is a mixing angle.  One can then express the correlation coefficients in terms of WL and WR ( or equally well in terms of W1 and W2) and plot the allowed regions in terms of the ratio of masses squared  = (m1 / m2)2  and the mixing angle 

The allowed regions using values of the spin-electron correlation A coefficient which include the weighted average of the Perkeo I and IAE measurements are shown in Fig. A3.6.  We take this plot to be representative of the possible sensitivity to right-handed currents.  As the current experimental state is unclear, the region of parameter space that may or may not be allowed is in question.  Thus, one sees that the conclusion one draws depends entirely on which measurements of A are used.  Taken together with the measured value of the spin-electron angular correlation in 19Ne, the IAE measurement shows about a 2  discrepancy with the Standard Model.23)  However, one also finds that the analysis of measurements in muon decay in terms of right-handed currents disagrees with the new IAE and 19Ne results.  While it is possible to derive models which would predict right-handed contributions in the semileptonic sector but not in the purely leptonic sector, it is perhaps more plausible that one or more of the measurements is in error.  For comparison, the sensitivity of the proposed beta asymmetry measurement to right-handed currents is shown in Fig A3.7 in which the central value of A has been arbitrarily chosen to agree with the Standard Electroweak Model. The results shown include the Particle Data Group compilation (1996) 28) and thus does not include the Perkeo II result or the revised value of the IAE - PNPI measurement.  The 19Ne result shown is from the most recent 19Ne experiment carried out at Princeton University (1998).  One observes that the proposed beta asymmetry measurement will provide a very high sensitivity to the possible existence of right-handed currents.

Figure A3.1.  Determination of GA and GV from measurements of the neutron lifetime and neutron beta asymmetry.

Figure A3.2.  Results for the neutron decay correlation coefficients as in 1997 (based on reported but unpublished new results), and the values of GV determined from 0+ ( 0+ superallowed beta decay and from requiring unitarity of the CKM matrix.

Figure A3.3.  Projected sensitivity for GV and GA for the proposed beta asymmetry experiment and for the most recent neutron lifetime experiments.  Also shown are the most recent results determined from the reactor measurements, including the updated Perkeo II result from 1998.  The neutron lifetime has been taken from the analysis of all of the recent lifetime measurements as compiled by Jules Deutsch in 1998.  The central value for the beta asymmetry has been arbitrarily set to coincide with the value of GV determined by requiring unitarity of the CKM matrix.

Figure A3.4.  Comparison of Vud determined from 0+ ( 0+ nuclear beta decay, the unitarity of the CKM matrix, and the value determined from the latest beta asymmetry measurement of by Perkeo II and that assigned by the Particle Data Group to the average value of the beta asymmetry measurements.

Figure A3.5.  Allowed regions (inside the solid lines) at the 90% CL in the (,) region if one uses the weighted average of the Perkeo I and the initial IAE measurements of A.

Figure A3.6.  Projected sensitivity for right-handed currents for the proposed beta asymmetry experiment.  The neutron present limits are taken from the Particle Data Group compilation and the 19Ne result is the most recent Princeton measurement.

APPENDIX 4

ADVANTAGES OF UCN MEASUREMENTS OF

NEUTRON BETA DECAY ANGULAR CORRELATIONS.

There are two significant advantages that UCN offer compared to experiments done in-beam:  polarization and background.

In-beam experiments typically produce polarized neutron beams using supermirror polarizers.  These consist of many parallel plates of thin glass bent at a large radius which are installed in a Soller collimator.  Each plate is covered with alternating layers of Co and Ti with a layer of Gd underneath the layers.  The assembly is placed inside a permanent magnet, thus magnetizing the layers of Co and Ti on the glass plates.  Neutrons must interact with the surface films of the glass plates at least once in passing through the polarizer.  Neutrons in one spin state undergo coherent scattering from the films and are transported through the supermirror.  Neutrons in the other spin state are scattered into 4 and are captured in the Gd where an average of 4 gammas are produced for each neutron captured.  The great advantage of the supermirror polarizers is that they can achieve very high polarization (typically 98%) over a broad range of neutron energies (typically from about 4 to 10 Angstroms).  However, the disadvantage is that the beam polarization is not completely uniform over the entire beam, the beam divergence is increased by a factor of two, and an intense gamma background is created.  In all of the experiments done to date, the uncertainty in the neutron beam polarization has been one of the limiting systematics.

In-beam experiments also have detectors typically located relatively close to the neutron beam.  Great care must be taken to control the halo around the neutron beam.  In the beam experiments, typically only about 10-6 of the neutrons passing through the detector beta decay within the detector active volume.  Thus, one must take great care in dealing with beam halos and the dumping of the primary neutron beam.  The beam-associated background has been one of the most important systematic concerns in all of the beta asymmetry experiments carried out at reactors to date.

In contrast, it is possible to produce 100% polarization of UCN by passing the UCN through a strong magnetic field gradient.  In practice, passage through a field of 6 Tesla is sufficient to polarize 100% of the UCN.  This is due to the fact that the kinetic energy of an UCN is so small that UCN of one spin state cannot overcome the potential barrier due to the .B interaction of the neutron spin with the magnetic field.  Secondly, as the UCN can be piped out to a spectrometer located 10 m or more away from the primary neutron beam, it is possible to provide 100% coverage of the shielding and to have a background which is close to the intrinsic background of the spectrometer.

APPENDIX 5

THE PROTOTYPE SD2 UCN SOURCE

A5.1.	INTRODUCTION

The considerations for UCN production at a spallation source are quite different from a reactor. At a reactor, the production has been done best by converting cold neutrons into UCN by multiple reflection from the rapidly moving blades of a turbine.  Such a device has produced an (extrapolated) UCN source density of 87 UCN/cm3 at the ILL reactor, a world record.30)  This technique involves Doppler shifting 40-50 m/s neutrons down into the UCN regime (< 8 m/s) and makes effective use of the high cold neutron flux from cold moderators at reactors to provide continuous UCN beams.  In a spallation source, a proton beam strikes a high-Z target in which approximately 1 neutron per 30 MeV of beam power (compared to about 180 MeV for a reactor) is produced.31)  These fast neutrons are thermalized and cooled in a variety of moderators. In a Short Pulse Spallation Source (SPSS), the proton pulse on the spallation target is typically a few s or less in duration.  At the MLNSC SPSS the proton pulse is 270 ns long.  In this case, the pulse width of cold neutrons is determined by the moderator that provides a pulse width of about 100 s.

A5.2.  THE MLNSC UCN ROTOR SOURCE

At a SPSS, the high-energy spallation neutrons are not fully moderated and at present, the time-averaged flux is at least an order of magnitude less than that at the ILL reactor.  However, one can take advantage of the pulsed nature of the source to produce and store UCN at the peak intensities available, which are comparable to or can exceed that at a reactor.  A technique for doing this was demonstrated many years ago at the ZING-P' source at Argonne National Laboratory and at a test setup at LAMPF.32)

This technique involves Doppler-shifted Bragg scattering of neutrons to convert 400-m/s neutrons down into the UCN regime.  A rotor carrying a mica scattering crystal moves away from the neutron pulse from the liquid hydrogen moderator at one half of the velocity of the neutrons that will be converted into the UCN regime.  The rotor velocity required is determined by the Bragg scattering condition associated with the lattice spacing of the crystal.  For mica, one converts 395 m/s neutrons.  In the center of mass frame, the incident neutrons are reflected back from the crystal with the same velocity at which they impinge on the crystal.  In the laboratory frame, the 395 m/s neutrons are stopped.  Thus, a puff of UCN is produced which then begins to expand.  Some fraction of the UCN cloud will drift into a guide tube placed close to the position at which the rotor intersects the neutron beam.  A shutter at the entrance to the guide tube opens while the puff is expanding and closes after a few ms.  Thus, it is possible to bottle the UCN at the peak flux rather than the average flux.  The penalty paid is that the filling time will be longer at a SPSS than at a reactor.  However, for a rather wide range of experiments, this is not a serious concern.

At Los Alamos, we have installed such a rotor converter on the existing LANSCE cold moderator. The moderator is viewed by a 58Ni-lined guide tube with a cross-section of 6 cm x 6 cm.  At a position about 8 m from the moderator a 6 cm x 6 cm mica crystal moving away from the neutron pulse at a velocity of 200 m/s has been installed on the end of a rotor that rotates in synchronism with the beam pulse rate.  A schematic view of the UCN source at LANSCE is shown in Figure A5.1.

A program of UCN measurements was carried out in 1996 and 1997 with the purpose of characterizing the performance of the UCN source, identifying possible areas in which improvements might be possible, and measuring the bottle lifetime of a prototype UCN bottle.  We typically detected 650 UCN/s at the end of a 3-m long, 8 cm diameter guide.  Correcting for the UCN guide solid angle (16%), the guide transmission (82% for 3 meters of guide), the detector window transmission efficiency (90%), and the detector efficiency (95%), we arrive at a UCN production rate at the source of about 5300 UCN/s.  Translating this production rate measured in the UCN detector to an UCN density at the source results in a value of the UCN source density of about 0.8 UCN/cm3.  We also measured a lifetime of 25 seconds for UCN stored in a 58Ni bottle, in agreement with the value expected.

We have upgraded the UCN rotor source in a number of ways.  The LRIP upgrade at LANSCE will increase the proton beam current in 1998 from the current 70 A to 100 A (and to 200 A in 2001).  A new moderator has been installed on FP11B, which is a partially-coupled liquid hydrogen moderator.  Measurements of the cold neutron flux show that the increased brightness of this moderator (running at 100 A) results in a gain in UCN production of a factor of 4.  Samples of crystals (fluorophlogopite) with substantially better reflectivity and lower absorption have been obtained and have been installed in place of the existing crystal package.  Measurements of the reflectivity indicate the new crystals should provide a factor of about 3 increase in the UCN production rate.  Taken together, these improvements will increase the UCN density to about 30 UCN/cm3 with a UCN flux of about 8,000 UCN/s at the end of a 1-m long, 7.6 cm ID UCN guide.  Since the prototype solid deuterium source is already capable of providing a much more intense source of UCN, we plan to use the solid deuterium source for the beta asymmetry experiment.  We do plan to use the rotor source as a test beam for testing apparatus to be used in the beta asymmetry experiment.

A5.3.  THE PROTOTYPE SD2 SOURCE IN THE BLUE ROOM AT WNR

A5.3.1.	THE PROTOTYPE SD2 SOURCE

The conceptual design of a SD2 UCN source is shown in Figure A5.2.  This is a variation (put forward by S. Lamoreaux) of the UCN factory concept originated by Serebrov et al.  Basically, the 800 MeV beam from the LANSCE accelerator would be directed onto a spallation target for a duration of less than one second.  The spallation neutrons would be moderated in a cold (5 K) CH2 moderator surrounded by a Be reflector at LN temperature.  Within the cold CH2 moderator is a SD2 moderator held at 5 K.  The walls of the SD2 moderator are stainless steel coated with 58Ni on the walls and bottom.  Originally a thin aluminum window was placed above the SD2 in the guide in order to confine the D2 gas to the cold region while making the SD2.  It was later removed as we learned more about the performance of the source.  The walls of the SD2 moderator form an UCN bottle that is connected at the top to an UCN guide tube leading to an UCN storage bottle. While the proton beam strikes the spallation target an intense pulse of UCN will be created and diffuse out of the solid deuterium moderator into the UCN guide.  After the beam pulse is shut off, an UCN shutter in the guide tube between the SD2 moderator and the UCN storage bottle would be closed so that capture on the solid deuterium will not occur.  While the proton beam is on target, the SD2 will be heated by gammas, fast neutrons, and charged particles and will rise in temperature.  However, at the beam currents we plan to operate at, this temperature rise is only a fraction of a degree.  Thus, a pulse of UCN would be trapped during each proton beam pulse inside the UCN storage bottle from which they could be bled off into UCN guides and transported to a variety of experiments.  By pulsing the source for 1 second once ever 10 seconds, one can provide a high-intensity, continuous source of UCN.

A5.3.2.	UCN PRODUCTION IN A NORMAL PARA-ORTHO SD2 SOURCE

The initial runs from the fall of 1998 through the summer of 1999 were carried out using the prototype SD2 UCN source with a normal (room temperature) mixture of 67% ortho deuterium and 33% para deuterium.  During these runs we consistently observed the following: 1) the UCN production rate was below that calculated using a simple Debye model,  2) there was not the expected temperature dependence of UCN production rate, 3) the volume dependence was consistent with a mean free path of a few cm, and 4) the measured UCN rate did not show any significant difference that depended on how the SD2 was formed.

We did make a number of improvements to the UCN source during this period in order to try to determine the cause of the lower-than-expected UCN production rates and the lack of a temperature dependence to the UCN production rate.  The geometry that was used in these experiments is shown in Figure A5.3.

The September 1998 measurements used a Fomblin-coated UCN bottle and suffered from a number of technical problems (condensation on the Al window in the guide, detector backgrounds, microphonics).  While we did observe a flux of very cold neutrons, we did not observe any measurable number of UCN.

For the January 1999 run, we removed the thin aluminum window that was located in the UCN guide just above the SD2 as this acted as a cryopump for residual gas and thus reduced the UCN transmission.  We also improved the detector shielding and used purer D2 gas.  After this modification we observed a significant UCN production rate.

For the July 1999 run, we installed a shorter LHe cryostat so that only a limited amount of surface of the UCN guide is at LHe temperature and thus reduced the amount of wall surface that acted as a cryopump for residual gases.

We also installed a palladium leak in the system through which only hydrogen isotopes can pass in order to ensure that air and water vapor could not be condensed onto the cryostat walls.  This was done at the same time as installation of the shorter LHe crysotat and thus it is not possible to separate the effect of these two changes.  However, we can state that reducing wall contamination resulted in an increase in UCN production rate.

Finally, we installed a flapper valve with a 1-inch diameter aperture just in front of the UCN detector (or just in front of the 3He cell when it was used).  The purpose of the flapper valve was to turn the guide system into a quasi-bottle permitting measurements that would be more sensitive to the loss lifetime in the SD2.

Analysis of the flapper valve data indicated that the lifetime of UCN in the SD2 was consistent with a lifetime of UCN in the SD2 of only a few ms and a mean free path of a few cm. The UCN production rate was also observed to be a factor of about 7 below that we calculated using our Debye model of UCN production.

We determined the contribution of wall losses in the UCN guides by measuring the UCN production rate using pure solid hydrogen (SH2).  While the rate is substantially decreased in SH2, the production rate can be predicted quite well and thus any reduction below that predicted provides a measures a combination of the guide losses and detector inefficiencies.

While some losses in the measured UCN production rate can be attributed to wall losses in the guides, the very low lifetime of UCN in the SD2 indicated there was clearly a problem with unexpected losses in the SD2.  There are several ways that the lifetime in the SD2 could be shorter: 1) the solid is warmer than 10 K, 2) there are additional impurities (and therefore losses) in the SD2, and / or 3) there are significant losses in the para deuterium fraction of the SD2.

Following the July 1999 run, we made off-line measurements of the temperature uniformity in the SD2 with thermometers placed directly inside the source volume.  These measurements revealed the presence of significant temperature gradients and even hot spots of over 20 K (liquid temperatures) within the source volume.  The most likely cause is that as the SD2 is cooled down it contracts and no longer makes good thermal contact with the walls of the LHe dewar around the SD2 region.  There is infrared (IR) radiation that is transported (with relatively high efficiency 33)) down the UCN guide from the room temperature part of the guide system.  The combination of the poor contact with the LHe dewar and the incident IR radiation resulted in very large (> 15 K) temperature differences being observed between the center of the SD2 and surface of the SD2.  In order to provide better thermal contact, we introduced a very low pressure (60 milliTorr) of 4He into the UCN guide.  The 4He gas in the SD2 source region acts as a strong thermal link between the SD2 and the LHe dewar.  We also installed a LN temperature baffle above the SD2 in order to reduce the IR heating.  With these changes, we no longer observed large temperature variations in the SD2.

We also produced SD2 by two methods:  1)  first liquefying the D2 and then freezing it and 2) condensing SD2 directly from the gas phase.  The SD2 produced from the gas phase (called lake ice) was optically much clearer compared to that produced by first liquefying the D2 gas (called river ice).

In the August 1999 run, we ran with the LN temperature baffle in place and used a small pressure of 4He gas in the guides.  While we now had confidence that our measurements of the SD2 temperature were fairly accurate, no large differences in the UCN production rate between the two types (river and lake ice) of SD2 were observed.  Again, we failed to see the expected temperature dependence.

Analysis of the measurements made in August, 1999, showed that the best fits to the data were obtained by a model for the SD2 that had a loss lifetime of 2-3 ms and a mean-free-path for elastic scattering of about 8 cm.

Thus, we explored the two remaining possibilities for the reduced UCN production rates:  additional impurities and losses in para deuterium.

In order to check the possibility of contamination of the D2 gas, we had mass spectrometer measurements made of impurities in the D2 gas after it had been frozen into SD2 and then warmed back up to room temperature.  The measurements indicated that there were very low levels of N2 (30 ppm), O2 (5 ppm), CO2 (2 ppm), and H2O (50 ppm).  Such impurity levels are not sufficient to cause any significant reduction in the UCN production rate.  However, the measurements did indicate that while the D2 gas direct from the factory had a total H contamination of 0.1% (as advertised), the D2 gas after being run through our gas handling system showed an HD contamination of 0.8%.  This limits the lifetime in the SD2 to about 20 ms.  As the data indicate a lifetime of a few ms, this contamination of HD is also not sufficient to explain our measurements.

Thus, it appeared that losses in para deuterium might be a likely candidate to explain the short lifetime observed for UCN in SD2.  The evidence for this is discussed in the following two sections.

A5.3.3.  	UCN PRODUCTION IN	AN ORTHO DEUTERIUM SD2 SOURCE

Deuterium gas at room temperature is 33% para deuterium (which has a total nuclear spin = 1 and rotational angular momentum =1) and 67% ortho deuterium (which is the ground state and has total nuclear spin = 0 or 2 and rotational angular momentum = 0).  When deuterium gas is cooled to liquid helium temperature it relaxes to the ground state with a relaxation time on the order of a month.  Thus, the solid deuterium used in the test runs is likely to have approximately the same para deuterium fraction (33%) as at room temperature.

We have (for the first time anywhere) calculated the upscattering rate from para deuterium and found that it corresponds to a 1.5 ms lifetime in pure para D2.  (See Appendix 12 for the paper of Liu, Young, and Lamoreaux for the calculation of the upscattering rate in para D2.)

Thus, we expect that the dominant limitation in UCN production is the para fraction in the SD2. This model of a near room temperature spin state equilibrium in the D2 would explain one of the most prominent and persistent features of our measurements; viz., the almost complete lack of temperature dependence in the UCN yields.

Thus, we can now derive a complete physics model of the UCN production process that incorporates all of the important possible loss mechanisms.

A5.3.4.	LOSS LIFETIMES IN SD2

The inverse of the loss lifetime  is the sum of the inverse lifetime components for temperature independent absorption in H2 and D2, upscattering in para D2, and for the temperature dependent upscattering in H2 (assumed to be para) and ortho D2.  If the fraction of H2 in the source is FH and the fraction of para D2 is FP,  then:

 =

FH 4830 s-1 	(absorption in H2)

+ (1- FH) 6.86 s-1 	(absorption in D2)

+ (1- FH) FP 995 s-1 	(upscattering in para D2)

+ FH uH (T) 	(upscattering in H2)

+ (1- FH) (1- FP) uP(T) 	(upscattering in ortho D2)

The functions uH (T) and uP(T) describe the temperature dependence of the upscattering rates in H2 and ortho D2, respectively.  The function uH (T) varies from 3 to 510 s-1 as T goes from 4 to 18 K and the function uP(T) varies from 9 to 3960 s-1 as T goes from 4 to 18 K.

These lifetimes are shown plotted in Figure A5.4 as a function of temperature for various values of FP when FH = 0.004 (corresponding to the 0.8% HD measured in the D2 gas used in the October run, as is discussed in the Section A5.3.4.  For comparison, we also show the lifetimes in Figure A5.5 when F H = 0.0001, which corresponds to the isotopic purity (99.9%) of the D2 gas as provided from Isotec.

As can be seen in Figure A5.5, for a room temperature equilibrium para fraction of 0.33, the lifetime varies only between 1.5 and 1.9 ms as the temperature varies between 18 and 4 K. Whereas for pure ortho D2 (with 0.1% hydrogen) the lifetime varies from 2.9 to 68 ms over the same temperature interval.

A5.3.5.	MEASUREMENTS WITH AN ORTHO DEUTERIUM SD2 SOURCE

It is possible to drive SD2 into the ortho ground state by cooling it to very low termperatures in the presence of a magnetic material that will induce the spin flip from the para to the ortho state.  The transition energy is about 7 meV (= 80 K), so it is necessary to do the conversion around the triple point (19 K) in order to have a high conversion efficiency while maintaining a finite vapor pressure.  We constructed such a converter cell and carried out measurements to verify that the para deuterium fraction was the dominant limiting factor in UCN production in SD2.

For the October 1999 run, we installed a short gas cell just in front of the UCN detector that could be filled with 3He gas at low pressures.  Since the absorption cross section in 3He is large and scales as 1/v, by increasing the 3He gas pressure the slower UCN are preferentially attenuated.  By running the cell at a number of different gas pressures, it is possible to determine the velocity spectrum of the UCN incident on the UCN detector.  The flapper cell was also used for the October run and was placed just in front of the 3He gas cell.

The principal goal of the October measurements was to determine the effects of a lower para fraction on the temperature dependence of UCN yield.  Off-line tests made in September of a para to ortho D2 converter developed for this purpose showed that the converter could reduce the para fraction of the D2 to about 5 % (as determined using thermal conductivity measurements of the D2 gas).  The para to ortho D2 converter was installed for the runs of October 6 and 7, 1999.

The SD2 source used in the October 1999 runs used a low pressure (tens of milliTorr) of 4He gas in the guide.  As our offline measurements indicated that the temperature of the SD2 was within one degree of the temperature of the LHe bath when the 4He exchange gas was used, we did not install the thermal baffle for the October run. The simulation geometry was modified to include the 3He spectrometer and also to include (for the first time) a 26 mm gap between the detector window and the first wire plane of the detector.

The temperature dependence of the UCN yield from 150 cc of SD2 is shown in red in Figure A5.6, as measured on October 6, 1999.  The dependence is fit very well by simulations that model the SD2 as containing a 4% para fraction with 0.8 % HD and an 8 cm elastic mfp.  There are no free parameters in the model calculations.  The results of the calculations are plotted using a normalization factor of 0.75.  Thus, our model predicts to within 25% the absolute UCN production rate that we observe.

A comparison of the calculated and measured time-of-arrival spectra for the coldest point on the 150 cc curve is shown in Figure A5.7.  The 4% para model, which at 8 K corresponds to an 11.5 ms lifetime, fits the measured data with a P(2) of 37%.

The 3He spectrometer was used to measure the velocity distribution of the neutrons arriving at the detector.  The measured values of the detected UCN rate as the pressure of the 3He in the 33 mm gap was varied are shown in red in Figure A5.8.  The slope of the measured curve corresponds to an average neutron velocity of 8.4 m/s.  The slope of the simulated curve corresponds to an average neutron velocity of 7.4 m/s, in agreement with the observations within the measurement errors.  These simulations used the 4% para model for the SD2 at 5 K and show good agreement with the shape of the measured curve after renormalizing by a factor of 0.75.

Thus, an increase in UCN yield of a factor of 2.8 was observed in the runs of October 6, 1999, as the SD2 temperature was decreased from 13.6 to 7.9 K.  This increase as a function of temperature is fit extremely well by simulations that model the SD2 as having a 4% para fraction, a 0.8% HD contamination, and only incoherent elastic scattering.  The absolute values of the measurements are reproduced to within 25% in the calculations with no free parameters.  The 4% para fraction is consistent with off-line measurements of the para to ortho conversion efficiency of the converter that was installed for the October runs.  Analysis of the 3He spectrometer (velocity) measurements made with a time cut of 0.8 s show that all of the neutrons detected are true UCN.

In November 1999 we shipped all of our UCN guides, 3He gas cell, the flapper valve, and our UCN detector to the ILL along with a stainless steel UCN bottle that was fabricated from a section of polished SS guide tube that had close-fitting flapper valves at the ends of the tube.  We carried out a series of measurements there that allowed us to separately measure the transmission through the UCN guides, the 3He gas cell + the flapper valve, and the UCN detector efficiency.  We also measured the UCN bottle lifetime to be about 8 seconds (consistent with that from expected wall losses in the guide and leakage through the gaps of the flapper valves).

With independent information about the guide transmission, detector efficiency, para deuterium fraction, temperature, HD contamination, and transmission through the flapper valve and 3He spectrometer cell, we can now make model predictions of the UCN source performance that have no free parameters.

In the March-April 2000 run, we moved the source to the Line B tunnel (due to unavailability of beam at WNR).  The source was set up at the junction of the Line B and C tunnels.  The configuration used is shown in Figure A5.9.  For this run we implemented an improved para to ortho converter cell, improved thermal conductivity cell, a Raman spectroscopy system, and improved gas handling system.

The new para to ortho converter cell has an improved cryogenic design that allows operation at 17K (instead of converting at 22K as was done in the October 6, 1999 run).  We have routinely achieved a 1.5-2.0% para deuterium fraction with the new converter cell.  We have also constructed two new systems to provide accurate measurements of the residual para D2 fraction in the D2 gas.  The first employs Raman spectroscopy to measure the absolute value of the residual para deuterium fraction.  The performance of the Raman spectrometer was improved by installing filters to reduce the scattered light.  This enables us to measure the para fraction with an accuracy of about 0.2%.  It also enables us to measure the HD fraction directly in the gas samples. Figure A5.10 shows the Raman spectrum from a D2 gas sample that was converted to 98.5% ortho deuterium at 17 K.  This figure also shows the sensitivity to the presence of HD.  It is clear that we can measure both the HD and para deuterium fractions with a sensitivity of 0.2%.  The second system uses an improved thermal conductivity cell at LN temperature.  This provides on-line measurements but with reduced accuracy.  One section of the cell contains a normal (33% para D2) sample of D2 gas while the other cell contains the D2 gas that has passed through the converter cell.  Since the relaxation time is so long, the normal sample retains the 33% para D2 fraction without any measurable change for at least several hours, which is the time it takes to convert enough D2 to form up to 200 cc of SD2.

We were able to reduce the HD contamination in the March 2000 run.  There was a measured 0.8% HD impurity in the October 1999 that limits the lifetime in the SD2 to 20 ms.  As we expect to achieve lifetimes of >30 ms due to residual para D2, keeping the HD contamination level at the 0.2% level (as delivered from Isotec) is sufficient.  The measured purity level of 0.8% HD in the October run is due to contamination from four sources: the D2 gas storage tank, the palladium leak, the para to ortho converter cell, and surface contamination in the gas handling system.  We have pumped and baked out the storage tank, flushed the palladium leak and converter cell with large amounts of D2, and constructed a new and cleaner gas handling system.  This has resulted in measured values of HD (0.2%) in the source for the March 2000 run that is consistent with that coming directly from the gas cylinder.

We were also able to run at lower temperatures in the SD2 in the March 2000 run than in October 1999.  The thermal mass of the source (mostly the Be and W target) is very large and it takes 3-4 days for the source to reach LN temperature.  During the October 6, 1999 run, we had only 2 days to precool the source (due to the limited time allowed for setup in the Blue Room) and thus the source was not in thermal equilibrium for that run.  From Figure A5.4, we see there is a potential gain factor of 60% in going from 8K to 4K (for 98% ortho D2).

The primary goals of this run were to demonstrate that we understand the physics model for our SD2 source and to bottle UCN at a high density.  The first is required in order to have confidence in the expected performance of a dedicated UCN source in Area B and the second is required in order for LANSCE management to agree to the use of Area B for a dedicated SD2 source.

We measured the temperature dependence of the UCN production, as shown in Figure A5.11.  The data agree quite well with the predictions for the temperature dependence.  The absolute value for the UCN production rate agrees with the Monte Carlo predictions to within 30% with no free paramaters.  Incorporating the 25% reduction factor that was empirically determined in the October 1999 run, we get agreement to within 5% for the absolute production rate.

We bottled UCN during the March and April  runs.  The bottle used was the 3.6 liter stainless steel bottle with butterfly valves that was taken to the ILL in November 1999 to have its performance measured.  The bottle lifetime is only about 6 seconds, due mainly to gaps around the edges of the butterfly valves and a hole in the guide where the shaft that turns the butterfly valves enters.  We ran in the mode where the exit valve of the bottle was closed, a proton pulse was put on target, and the entrance valve to the bottle was closed after a short period.  Measurements showed that the highest UCN density could be achieved when the entrance valve was closed 0.5 seconds after the proton pulse, in agreement with expectation.  After some period of time (called the holding time) the exit valve was opened and the UCN were detected in the 3He counter.  Figure A5.12 shows the time spectrum from one of the bottling runs carried out with a single pulse of 3 C of protons on target.  The entrance valve was closed at t = 0.5 seconds after the proton pulse.  The initial decay curve (before 4 seconds) is due to leakage of UCN from the source through the exit valve of the bottle into the detector.  At t = 4 seconds, the exit valve was opened and the UCN were detected in the 3He detector.  The integrated number of UCN measured results in an extrapolated UCN bottle density (at t = 0 seconds) of about 3.4 UCN/cm3.

We carried out measurements of the UCN production rate as a function of the para deuterium fraction.  This was done with 40 cm3 of SD2 at 5 K in bottling runs in which the UCN were held for 4 seconds before being counted.  We varied the para fraction from 2% to 4% to 33% (normal room temperature fraction) and observed the expected dependence on the para fraction.  Figure A5.13 shows in a graphic manner the effect of varying the para fraction.

We also measured the volume dependence of the UCN production rate.  This agreed generally quite well with expectations.  However, due to a systematic problem associated with the pressure (17 mbar) at which the SD2 production was carried out, there were fairly large uncertainties in the volume of SD2 that was produced.  However, we determined that the UCN production rate reached a maximum somewhere in the 120-200 cm3 region, in agreement with our predictions.  Figure A5.14 shows the volume dependences measured in the August 99 run (with normal 33% para deuterium fraction), October 1999 run (with 4% para deuterium fraction) and March 2000 run (with 2% para deuterium).  The effect of reducting the para deuterium fraction is once again very obvious from the data.

We also made measurements of the bottle UCN density with multiple beam pulses on target.  By increasing the charge in each proton pulse, we were able to study the effects of possible beam heating of the SD2.  In addition, we were able to achieve significant densities of UCN in the bottle.  Figure A5.15 shows the time spectrum of counts in the UCN detector when 8 beam pulses, spaced 0.5 seconds apart, were put on target.  Each of the spikes resulting from the beam pulses can be seen in Figure A5.15 at 0.5 second intervals.  The entrance valve to the bottle was closed at t = 3.5 seconds and the exit valve was opened at t =4.0 seconds.  In this run, the total charge in the beam pulses was about 24 C, corresponding to about 3 C per pulse.  This resulted in a measured bottle density of 19.3 UCN/cm3 at the time that the exit valve was opened.  We carried out similar measurements with different amounts of charge per pulse, ranging from 0.25 C per pulse to 3 C per pulse.  The results are shown in Figure A5.16 in which it is clear that the UCN production rate tracks linearly with the total proton charge up to the maximum of 24 C delivered on target.

Figure A5.1.  Schematic view of the UCN rotor source at the MLNSC.

Figure A5.2.  Schematic view of the proposed dedicated SD2 source.  The aluminum window shown on the drawing was removed after the first set of runs with the prototype source.

Figure A5.3.	Schematic view of the SD2 prototype source.

Figure A5.4.  Loss lifetimes in SD2 for a 0.8% HD contamination level  (0.4% total H contamination), as was used in the October 1999 run.

Figure A5.5.  Loss lifetimes in SD2 for a 0.2% HD contamination level  (0.1% total H contamination).

Figure A5.6.  Measured and calculated temperature dependence of UCN yield from a 150 cc SD2 source.  The temperature measurements plotted are taken from the diode thermometers on the UCN source.  The calculations are plotted using a normalization factor of 0.75.

Figure A5.7.  Measured and calculated time-of-arrival spectra at 8 K.

Figure A5.8.  Detected neutron rates as a function of 3He pressure in the spectrometer in the October 1999 run.

Figure A5.9.  Layout of the experimental setup used in the March 2000 run in Line B.  The UCN bottle is located in the top horizontal section of the UCN guide system.

Figure A5.10.  Raman spectrum for D2.  The top figure shows D2 converted to 98.5% ortho with gas from a storage cylinder that was contaminated with 1.3% HD.  The bottom figure shows D2 converted directly from the factory gas cylinder for two different conversion rates (23 K and 17 K).

Figure A5.11.  Measured temperature dependence of the UCN production rate in the March run.

Figure A5.12.  Time spectrum showing the initial leakthrough of UCN from the bottle and the UCN observed when the bottle was emptied at 4 seconds.  The proton beam pulse was 3 C.  (March 2000 run)

Figure A 5.13.  Effect of para fraction on UCN production rate.

Figure A5.14.  Measured volume dependence in the March run.

Figure A5.15.  Time spectrum of an UCN bottle run showing the initial ramp up of UCN following 8 pulses of protons followed by opening the bottle at t = 4.0 s.  (April 2000 run)

Figure A5.16.  The dependence of the UCN production rate on total proton charge delivered on the tungsten spallation target.

APPENDIX 6

A DEDICATED SD2 SOURCE IN AREA B

A6.1.  INTRODUCTION

The performance of the prototype SD2 source is already sufficiently good that we can design a first-generation dedicated SD2 source that would be installed on Line B at LANSCE.  In fact, the prototype source, based on its measured performance, could be used to carry out the beta asymmetry experiment with at least the same accuracy as that originally proposed using the UCN rotor source at the MLNSC.  Of course, we plan to optimize the design for a dedicated source based on our understanding of the physics involved in UCN production in SD2.

A schematic view of the source is shown in Figure A5.2.  The 800 MeV proton beam from the LANSCE accelerator impinges on a stopping-length tungsten spallation target.  The MeV spallation neutrons are reflected back in a flux trap consisting of a LN-temperature Be reflector.  Within the Be reflector is a LN-temperature polyethylene premoderator that surrounds a UCN guide tube that contains a few hundred cm3 of SD2.  The proton beam is on target for less than 1 second and is turned off after 40 microCoulombs of charge (4 macropulses) have been delivered.  The UCN produced in the SD2 move up into the UCN storage bottle where they are filtered for 1 second to remove any neutrons above the critical velocity of the bottle.  The exit valve on the bottle is then opened and the UCN flow out to the experiment.  This cycle is repeated every 10 seconds.  This results in a time-averaged beam current on target of 4 A.  Eventually (after about 10 beam cycles) an equilibrium density of UCN is produced in the storage bottle.  The beta asymmetry experiment sees essentially a constant flow of UCN.  The UCN source would be located at the site of the existing LD2 target in Area B (see Figure A6.1) and the beta asymmetry spectrometer would be located in the large experimental hall in Area B.

A more detailed view of the source arrangement is shown in Figure A6.2.  The SD2 source would be coupled by an input guide to an UCN storage bottle that has a vacuum pumping port rising out of the top of the storage bottle.  There is also a horizontal guide that transports UCN to the beta decay spectrometer.

The four components of the storage volume are shown colored in blue in Figure A6.3.  The input guide (that contains the SD2) is a 1-m high 20-cm diameter specular reflection 58Ni-coated PNPI zirconium guide.  The use of zirconium minimizes both cold neutron absorption in the source and activation of the guide tube.  The UCN storage bottle is a 20-cm diameter x 20 cm high diffuse surface 58Ni-coated double-walled aluminum cylinder that contains LN in the region between the walls.  The bottle is pumped out through a 3.3 m high vertical pumping port consists of 4 sections of standard 8-cm diameter 58Ni-coated PNPI zirconium guide.  The height is chosen so that UCN with V < 8 m/s are gravitationally confined and cannot reach the top of the guide tube.  Neutron absorbers at the top of the guide absorb neutrons with V > 8 m/s.  This vertical extension also provides a pumping port and vacuum instrumentation for the source.

The UCN storage bottle is joined to a long horizontal section that feeds the UCN to the beta asymmetry spectrometer.  The first horizontal section is an 9.5-m long, 4 cm x 4 cm square 58Ni-coated guide that penetrates the 4 m-thick shielding surrounding the target position.  This guide transitions to a 2-m long, 4 cm x 4 cm square diamond-coated UCN guide in the region of the polarizer and AFP spin flipper.  (This region must be electrically nonconducting since to allow RF spin flipping of the UCN.)  After passage through the AFP spin flipper, the horizontal guide transitions to a 50-cm long, 2-cm diameter diamond-coated UCN guide that is required for injection of the UCN into the beta decay trap through the 3-cm diameter warm bore penetration through the side of the superconducting solenoid.  The 58Ni-coated guides are assumed to have a loss factor of f = 0.0005 (the measured value for the PNPI guide tubes) while the diamond-coated guides are taken to have a loss factor of f = 0.001.  The horizontal guide also contains an UCN switch and a set of UCN valves (as shown in Figure A7.3) that allow depolarization measurements (as discussed in section A7.4.  The horizontal UCN guides are at room temperature and they transition to LN temperature at the UCN storage bottle and the beta decay trap.

A6.2. IMPROVEMENTS TO THE EXISTING SOURCE.

It is possible to further increase the UCN production rate by optimizing the geometry of the SD2 source.  The prototype UCN source geometry was dictated by the need to use existing equipment in order to bring the source on line quickly and at minimal cost.  In particular, the diameter of the SD2 was fixed to be 7.8 cm since we used a standard PNPI guide for the UCN source.

There are two considerations that determine the optimal geometry.  First, we have carried out optimization studies of the tungsten target.  The goal in this design study was to reduce the mass of the tungsten target as much as possible without substantially affecting the neutron production rate.  This is largely an ES&H issue as thermal neutron capture on 186W produces 187W (with a 25 hour half-life).  187W is one of the primary activities that determines how much beam current we can take on target before we exceed the activation level at which we become a Category 3 nuclear facility operation.  The neutron yield vs. diameter and length of the W target are shown in Figures A6.4 and A6.5, respectively.   From these figures, we see that we lose only 6% in UCN production rate by decreasing the W target from 5 x 10 x 20 cm (the size in the prototype UCN source) to 2 cm diameter x 12 cm long.  Thus, we have set the W target size to be 2 cm in diameter x 12 cm long as a reasonable compromise between performance and activation of the source.

Second, since the length of the tungsten target is 12 cm long, to first order an optimized UCN source would most likely have a larger diameter than the prototype source.  We have carried out a Monte Carlo study to determine the optimal size of the SD2.  As is shown in Figure A6.5, for a given source thickness, a 20 cm-diameter SD2 source provides about 30% higher UCN production rate than a 16 cm diameter source.

We also considered the possibility of improving the cold neutron flux in the region of the SD2 by studying different moderator configurations.  The results for moderators comprised of polyethylene, ortho hydrogen, and ortho deuterium are shown in Figure A6.6.  We observe that polyethylene is just as effective a moderator as liquid hydrogen or liquid deuterium.  This is due to the fact that, while liquid hydrogen is a very effective moderator, it has very low density and this requires that the SD2 be moved further away from the W target, thus reducing the cold neutron flux incident on the SD2.  Thus, given equal performance, we select polyethylene as the moderator of choice due to the much greater simplicity of construction and operation.  The cold neutron spectra associated with different thicknesses of polyethylene moderators is shown in Figure A6.7.

Finally, since the best fit to the mean free path is about 8 cm,one would expect the thickness of the SD2 should be of order 8 cm.  As can be seen from Figures A6.8 and A6.9, the optimal volume from a 15.8-cm diameter source is 1000 - 1200 cm3.  This corresponds to a thickness of 5-6 cm.  The optimal thickness should be independent of the source diameter and thus we expect that a 6-cm thickness for the 20-cm diameter SD2 source should also be optimal.

We have carried out Monte Carlo studies that explored the use of different materials for the storage volume and were led to the conclusion that to maximize the rate and polarization using a 7 T polarizing field, the junction box should be 100% diffuse 58Ni.  In further Monte Carlo studies the volume of the junction box, the cross-sectional area of the horizontal section and the specularity of the vertical and horizontal surfaces were varied in order to determine the optimum configuration.

A6.3.  SIGNAL RATES AND POLARIZATIONS IN THE BETA ASYMMETRY

EXPERIMENT WITH AN SD2 UCN SOURCE

The UCN bottle storage density and signal rate in the beta asymmetry experiment are derived from the peak pulse neutron density, 0, and the lifetime in the storage volume, B that are provided by the simulations.  If the proton pulse producing the neutrons has a length of P and this pulse is repeated with a repetition rate of R, the equilibrium neutron density in the bottle is given by:

The time distribution of the neutrons emerging from the outlet follows the bottle density, so the equilibrium current of neutrons emerging from the outlet is given by:

.

If the lifetime of these neutrons in the A experiment storage trap is T and the lifetime against beta decay is n  , the equilibrium beta decay rate in the trap will be:

.

Previous simulations for a 3m long 10 cm dia storage trap for the beta asymmetry experiment with a 2 cm dia input guide have shown that T = 4.74 seconds. n is, of course, 887 seconds.

The simulations used in this study were all done with a maximum initial neutron velocity in the SD2 of 30 m/s with a 10 A average current delivered as a 100 C pulse within 1 s repeated every 10 s.  The input valve to the storage system is closed 1 s after the beginning of the pulse and the exit valve is opened at the same time.  The best choice over the range of 6 liter to 30 liter box volumes studied was a 10 liter, 25x20x20 cm (HxWxL) junction box and a 4x4 cm cross-section horizontal section. The total volume of the entire system (UCN storage bottle + pumping guide + horizontal guides) is 41 liters.  The entire system has a calculated lifetime of 19 seconds, which is dominated by the UCN exiting the horizontal guides into the beta asymmetry spectrometer.  Both the vertical and horizontal sections are specular while the walls of the UCN storage bottle are completely diffuse in order to quickly filter out any false UCN (i.e., UCN with v > 8 m/s).

The transport model used in the analysis of the October data was derived from fits to SH2 measurements made in July, 1999, that models the guides as 96% specular with a loss factor of f=0.0005.  (This is in agreement with the direct measurements of the guide tube transmission made at the ILL in November 1999.)  This model for the guides was used to calculate the performance of the storage arrangement shown in Figure A6.3, except that the transport model assumed the 1 m input guide section from the SD2 source to be 99% specular with f=0.0005.  The storage volume surfaces were also assumed to have f=0.0005 but with completely diffuse reflectance.  Since the peak yields observed during the October measurements were from 150 cc of SD2 at 8 K, this study was done assuming a 150 cc source at 8 K.

The neutron density averaged over the storage volume as a function of time following a single proton pulse is shown in Figure A6.10.  The simulations were carried out with Vmax = 8,16, and 30 m/s.  The 16 and 30 m/s results are essentially indistinguishable after about 0.6 s so most of the very cold neutron (VCN) filtering is done by then. Simulations using Vmax =8 m/s appear to underestimate the actual densities at t < 3 seconds (due to the presence of VCN) but the fits that determine 0 and B are not that effected.  The ramp up to an equilibrium density of 385 UCN/cm3 is shown in Figure A6.11.  In this case, 40 C of charge is delivered on target within 1 second and the beam cycle is repeated once every 10 seconds, resulting in a time-averaged beam current of 4 A.

The optimum performance (that can be realized in practice) is for a source with a 20-cm diameter SD2 volume that is 6 cm thick and SD2 at 5K with a 0.2% HD concentration and 98% ortho fraction.  As will be discussed in the following section, we are limited to an average beam current of 4 A in order to avoid becoming a Category 3 nuclear facility.  With that beam current, from Table A6.1, we see that we should be able to achieve an UCN density in the storage bottle of 385 UCN/cm3, a flux into the beta decay spectrometer of about 40,000 UCN/s with essentially 100% polarization, and a beta decay rate of 116 Hz.  This exceeds by an order of magnitude the performance that could be achieved using the ILL UCN source.  As we have a high degree of confidence in the physics model on which these estimates are made, we will assume this level of source performance in the rest of this proposal.

A6.4.	OPERATIONAL ISSUES OF A DEDICATED SD2 SOURCE

A6.4.1.	CONSTRUCTION OF A DEDICATED SD2 SOURCE

There are a number of important issues that must be addressed in providing a safe, reliable, and easily maintainable dedicated SD2 source in Area B.  In this section we detail the operational plan for installing and maintaining a dedicated SD2 source.

The first component in the system is a fast kicker magnet located in the switchyard of the LANSCE accelerator, as is shown in Figure A6.13.  This kicker magnet allows one to take single H- macropulses on a per demand basis and inject the beam into Line B/C.  This magnet is required in order that the Lujan Center neutron scattering program and the nuclear physics program at WNR can both run at the same time as beam is being delivered to Areas B and C.  This fast kicker magnet has been designed primarily to allow the Proton Radiography (PRAD) program to be able to take beam on a demand basis for weapons physics measurements in Area C.  However, the technical characteristics of the fast kicker magnet are such that it can run at any repetition rate up to 120 Hz (i.e., taking every macropulse from the LANSCE accelerator).  Thus, it is also ideally suited to provide full intensity macropulses (10 C per pulse) to line B at a rate of 10 Hz.  This is the maximum amount of beam that Line B can accept with the current amounts of shielding that are installed in Line B.

The fast kicker magnet is being funded by Defense Programs for use in the PRAD program but will be made available to us for use in Line B as well.  The schedule for construction, installation, and commissioning of the fast kicker magnet is that it is expected to be available for regular use in the beginning on CY2002.  Thus, we do not anticipate that availability of the fast kicker magnet will impact our proposed schedule and there is no extra cost to the UCN program for the fast kicker magnet.

PRAD plans an operating schedule of working in Area C on a normal 40-hour work week and taking beam for detector development and high explosives shots on an average use basis of about 2 days per week.  However, beam is generally only required for periods of a few hours at a time and as beam can be switched between Line B and C in a period of an hour or less, we do not anticipate any major down time for UCN running due to PRAD activities.  In order to take this into account in our beam schedule, we allot a very generous 10% dead time for use of the beam by PRAD.

In order that beam delivery to UCN in Area B does not impact access of the PRAD personnel to Area C, we will have to construct a shield wall with a dogleg entry at the junction between Line B and Line C.  Such a wall used to exist before PRAD began operations and it is our plan to reinstall the shield wall in essentially the same place as it previously occupied.  Due to HVAC considerations of the flow of beam halo activated air in the beam tunnels, we will also have to hermetically seal Line B from Line C at the shield wall.  The entries into Line B and Line C are already a part of the Personnel Security System (PSS) that forms the normal ES&H controls that regulate entry into beam areas at LANSCE.

Second, the Line B beam line must be reinstalled.  Parts of this beam line were removed when the Accelerator Production of Tritium (APT) program carried out some tests in Line B in 1998.  Our plan is to reconstitute Line B as per the design when it was decommissioned in 1996, as is shown in Figure A6.13.  We have taken an inventory of parts for the vacuum and magnetic components in Line B and have either located every original item or an acceptable substitute.  There is one magnet power supply that must be repaired, but otherwise all the components are operable.  Thus, we do not anticipate any unexpected problems with beam transport, safety, and operations as we are simply returning to the running mode previously used in Line B.

Third, the Area B cave containing the LD2 target must be emptied of the existing beam line components and magnets.  This will require that the roof (which consists of 3’ wide x 19’ long x 12” thick steel plates and large concrete shielding blocks) be removed.  This is required at any rate in order to modify the steel shielding in the roof so that the SD2 source can be installed and removed for maintenance.  After almost 20 years of beam delivery to this cave, the residual activation is less than 40 mR/hr (in isolated areas – primarily the beam collection magnets), so personnel access for limited periods is permissible while removing the magnets with the 30-ton overhead bridge crane.  The steel roof shielding plates will be cut using a propane and oxygen torch so that access for installing the SD2 source is provided.  We will also core a 6” penetration through the shielding wall between the Area B cave and the Area B experimental hall.  This penetration is 1 m above the proton beam height and provides a port for the UCN guide to be inserted.  Finally, the MRS spectrometer must be disassembled and removed from Area B.  The overall floor layout (as it currently exists) is shown in Figure A6.1.  Funding to carry out this task is being provided by the Laboratory out of funds set aside for dealing with legacy issues.

Fourth, we will install the water-cooled tungsten target and the Be reflector below it on a permanently mounted stand in the Area B cave.  We will also install a permanent water-cooled carbon beam dump just downstream of the tungsten target.  We will then lower the cryogenic parts of the SD2 source and the UCN bottle that sits on top of the source down onto the tungsten target.  This allows complete physical separation of the tungsten target from the cryogenics of the UCN source, thus facilitating removal and replacement of the tungsten target when required.  The UCN guide, which sits on a rail system, will then be slid into the source and the vacuum chamber around the guide can be connected to the source vacuum chamber by remotely coupled clamps.  The design of the components of the SD2 source is shown schematically in Figure A6.2.  The vertical extension of the UCN storage bottle will be installed and serves as a pumping port, a port through which we can view the SD2, and a gravitational velocity filter.  Finally the overhead shielding above the SD2 source will be installed and the water lines, cryogenic transfer lines, power and instrumentation cables will be connected.  The water cooling system for the tungsten target and carbon beam stop is mounted on two skids that have dual water pumps and redundant failure controls for cooling the target and beam stop.  The cooling system is virtually identical in design to the cooling water system that has been used successfully for Target 4 at WNR with up to 8 A of beam for more than 10 years.  The cooling systems and catch basins beneath them (required for containment of the activated water in the case of a water leak in the system) will be located in an existing pit on the roof above the Area B cave.

The SD2 target is then ready for beam.  A number of monitoring instruments will be connected to the source for temperature monitoring of all of the different components, status monitors for the UCN valves, vacuum instrumentation, radiation monitors, and beam control monitors.  Here we will draw on the extensive experience of the LANSCE operations team that has designed, installed, and successfully operated the tungsten spallation source at the Lujan Center and the beamline components for the 1L target that runs 100 A of beam.

A6.4.2.	BEAM HEATING ISSUES

A serious concern in designing a dedicated SD2 UCN source is that of beam heating.  When the proton beam strikes the spallation target, a substantial amount of heat is deposited in the tungsten target and cryogenic source.  The breakdown of the heat load is 984 watts in the tungsten source, 872 watts in the LN-temperature components, 22 watts in the LHe-temperature components (other than SD2), and 5.8 watts in the SD2.

The tungsten target has an average heat load of about 984 watts.  During a beam pulse of 40 C, the front section of the tungsten target (which has the highest energy deposition per unit mass) will rise in temperature to about 530 K.  This is still far below the melting temperature of tungsten (3683 K).  The tungsten target is continuously cooled by chilled water and since the time constant for removing the heat load from the beam pulse is of order 0.5 seconds, the maximum temperature of the tungsten will not exceed 600 K.  The temperature of the tungsten target will be constantly monitored in order to ensure that beam delivery is stopped in the event of any unexpected temperature increase in the source.  We note that the 1L tungsten target at the Lujan Center is water cooled and runs at a time-averaged current of 100 A (compared to our time-averaged beam current of 4 A).  Thus, based on the operational experience at the Lujan Center, we do not expect any problems with the operation of the tungsten target for the SD2 UCN source in Area B.

The second aspect of beam heating that must be considered is that due to heating of the cryogenic components of the UCN source.  We have carried out detailed heat load calculations (using the LAHET and MCNP computer codes).  The results show that the average heat load on the entire LHe-temperature cryogenic systems is 28 watts.  Of that, about 50% is due to prompt heating associated with direct particles from the beam interacting with the source and 50% is due to the thermalization and capture of neutrons in the LHe-temperature parts of the UCN source.  This is a heat load that can readily be handled and thus we do not expect any problems with maintaining the source at LHe temperature.

The third aspect of beam heating that must be considered is that due to heating of the SD2 itself.  Since the UCN production rate is temperature dependent, an increase of the SD2 temperature could potentially lead to large UCN losses.  We have calculated the heating load on the SD2 and found that the expected temperature rise from a 10 C pulse is only 2.3 K in the worst case and only 1.6 K on the average, as is shown inf Figure A6.12.  Such a temperature rise would result in a reduction in the UCN production rate of about 11%.  However, one must ensure that the heat from a single beam pulse is removed before another beam pulse is put on target.  We note that the thermal conductivity of ortho D2 is quite high (0.14 W/cm/K at 5 K).  We estimate that the thermal time constant of the SD2 is less than 100 ms and since we will pulse the source at 10 Hz, we do not expect the SD2 temperatures to increase much above that during which occurs from a single beam pulse.  In the worst case (assuming a single 40 C pulse, the average temperature rise in the SD2 would be about 4 K, resulting in a loss in the UCN production rate of about 60%.  We also note that experimental evidence from the PNPI indicates that intense irradiation drives the deuterium into the (ortho) ground state.  We thus expect that in normal operation the ortho purity will increase over the course of several days to reach at least 99%.  Such an increase would result in an increase in the UCN production rate of 40%, thus offsetting any effect due to beam heating of the SD2.

We have taken data to study the issue of beam heating, as was discussed in section A5.3.5.  During a run in early April 2000, we ran the source in Line B with 100 cm3 of 98% ortho deuterium at 5 K.  We measured the UCN production rate as a function of beam current.  The proton beam was run at 2 Hz with a total of 8 beam pulses striking the tungsten target in a period of 4 seconds.  The charge per beam pulse was increased from about 0.25 C per pulse to 3 C per pulse.  The UCN production rate was observed to be quite linear over this range, as was shown in Figure A5.17.  Thus, with a total charge of 24 C put on target over a 4 second period, we observed no effects due to beam heating of the SD2.  As this is within a factor of 2 of the 40 C we expect to put on target in normal operation, we do not expect any substantial UCN losses due to beam heating of the SD2.  Thus, we assume in estimating the performance of a dedicated SD2 source that beam heating of the SD2 will not result in any noticeable loss in the UCN production rate.

A6.4.3.	ES&H / NUCLEAR FACILITY ISSUES

The primary restriction on the beam current that we can use with the SD2 target is determined by the requirement (by LANSCE) that it not become a nuclear facility.  The primary deciding factor is the level of accumulated radioisotopes in the tungsten target.  The proton beam activates the target and produces a large number of fairly short-lived activities with half-lives in the range of a few hours to few days.  This activity builds up to an equilibrium level within a week of startup of operations and consists primarily of 186W that is produced by thermal neutron capture on 185W.  The primary long-lived activites produced in the tungsten are 125I (t1/2 = 60 days) and 148Gd (t1/2 = 74.6 years).  Extensive calculations and measurements have been carried out by LANSCE-12 with the result that an accurate activation curve for the tungsten target has been determined.  The normal operating cycle at LANSCE will be beam on for three months followed by beam off for one month for maintenance.  The activation of the SD2 tungsten target for this type of beam cycle and 4 A of average beam current is shown in Table A6.1.  The units in the table are such that a value of 1.0 indicates the threshold for accumulated activation at which point the source becomes a Category 3 nuclear facility.  The values shown assume that beam availability to Line B is 90% (allowing for 10% of the time for PRAD running) and beam availability from the accelerator is also 90% (based on LANSCE projections) resulting in a total beam duty factor of 81% for Line B UCN operations. Thus, by running at only 4 A, we still have a safety factor of 18% after three beam cycles.  The estimated uncertainty in the Cat 3 calculations is about 10%, thus running at only 4 A provides a safety factor of almost 2 .  In fact, this is conservative since no allowance has been included for any down time in the experiment.  We will continuously monitor the total recorded beam current on target and recalculate the activation periodically in order to ensure that we remain safely below the Category 3 limit.  Thus, in order to remain a nonnuclear facility, we will operate the source at 4 A and remove and dispose of the tungsten target once a year.  This operating mode means that we do not have to replace any part of the source during the course of the beta asymmetry experiment.

The physical layout that allows removal and replacement of the source is shown in Figure A 6.2.  In order to remove the source, we will first remove all of the water from the tungsten target water cooling lines.  We will then remove the target hatch from the roof shielding.  The tungsten target is mounted on a horizontal rail system that allows the target assembly to be moved horizontally remotely using a mechanical drive.  The water lines connected to the source are soft aluminum close to the source and then transition to flexible stainless steel bellows lines.  Once we are ready to remove the target assembly, we will remotely raise into postion a mechanical crimping/cutting system around the soft aluminum water lines.  The aluminum lines are remotely crimped in two places about 3 inches apart.  We will then remotely shear the water lines between the two crimps.  The flexible water lines (with the remaining sealed section of aluminum line attached) can then be removed from the Line B cave.  The target assembly sits on rails and can then be remotely moved horizontally (using a mechanical drive screw assembly) to a position directly below the target hatch.  A remotely controlled hook on the crane can then be lowered and connected to the tungsten target assembly.  The tungsten target assembly can then be then be lifted up with the overhead crane into a cylindrical steel shield that is positioned on the target hatch.  The tungsten target assembly can then be held in place in the shield with pins and the crane hook can then be disconnected and lifted away.  The top of the shield can then be lowered onto the shield cylinder and bolted together manually.  The shield can then be lifted remotely with the crane up and lowered onto the base plate of the shield.  The base plate can then be bolted to the rest of the shield manually.  The entire shield assembly containing the tungsten target assembly can then be removed for permanent disposal.

Cumulative Time	Delta Time	Beam  Status	Cat3 Value

90 days	90 days	on	0.561

120 days	30 days	off	0.240

210 days		90 days	on	0.518

240 days		30 days	off	0.373

330 days		90 days	on	0.823

360 days		30 days	off	0.480

450 days		90 days	on	0.923

480 days		30 days	off	0.580

570 days		90 days	on	1.024

600 days		30 days	off	0.677

690 days		90 days	on	1.118

720 days		30 days	off	0.774

Table A6.1.  Buildup of activities in the SD2 source with 4 A average beam current.  Each beam cycle is assumed to be 90 days of beam on followed by 30 days of beam off.  The source becomes a Cat 3 facility when the Cat 3 value reaches 1.0.  The values given assume 90% beam availability in Line B and 90% accelerator beam availability for a total beam duty factor of 81%.

We note that the procedures listed described above follow very closely the procedures developed to remove and dispose of the 1L target at LANSCE.  As the 1L tungsten target is typically operated at a beam current of 100 A, its activation is approximately 25 times higher than our target.  Thus, we are confident that these procedures described above will prove adequate to handle our target assembly.

As discussed above, the target assembly must be removed and replaced once a year.  This would normally occur during the 30-day shutdown between beam cycles.  After three beam cycles (330 days), we would allow the target to cool for two weeks.  We would then remove the activated tungsten target assembly, which would take only one day.  To install a new tungsten target assembly, we would first disconnect the remaining crimped aluminum water lines from the flexible stainless steel bellows water lines.  A new target assembly would then be connected to the flexible stainless steel water lines.  The entire assembly would then be lowered onto the jack stand assembly on the rails in the Area B Cave.  The assembly would then be moved remotely into the the cryogenic source assembly.  The target hatch can be put in place and we are ready for beam.  We estimate that, apart from the two-week cooldown period, the replacement of the target assembly can be completed in two working days.  Thus, there is more than enough contingency time during a one-month shutdown to allow for replacement of the target assembly.  Of course, we will certainly test and debug our operations a number of times using nonactivated targets before beam is ever put on target in the Area B cave.  If any problems arise that require changes in our procedures, this will allow us an opportunity to resolve them during a period where we can still have physical access to all of the components inside the Area B cave.

We are designing the cryogenic target assembly to operate for several years without any regular maintenance.  Our general approach is that we do not plan to do any remote handling servicing of the source cryogenic assembly.  However, as a matter of prudence, we will design the source to be constructed primarily from materials (such as aluminum and zirconium) that will not become highly activated.  If the need arises to repair some component of the source, we would plan to remove the entire cyrogenic source assembly and replace it with a new one.  The cost to do this is not large as long as we can salvage the beryllium reflector assembly.  The cryogenic source assembly is being designed in such a way that this can be easily done with a minimum of exposure.

The general process for removing and installing a new cyrogenic source assembly is as follows.  First, the activated tungsten target assembly will be removed using the procedure discussed above. We will then uncouple (using remotely actuated clamps) and retract the UCN guide from the UCN storage bottle.  Then we will remove the roof shielding over the SD2 source and remove all of the vacuum pumps and instrumentation located within the concrete blockhouse on the Area B mezzanine.  We would then lift the UCN storage bottle and cryogenic parts of the SD2 up and store it in a roped-off area on the mezzanine.  Since we are designing virtually all of the components of the source to be from aluminum, zirconium, and beryllium, our estimates of the activation indicate this is an acceptable procedure.  The outer vacuum shell can then be decoupled and lifted off.  Similarly, the bottom plate of the LN shield can be decoupled from the rest of the LN shield.  The rest of the cryogenic assembly can then be lifted off as one piece, leaving the bottom plate of the LN shield (to which the beryllium is attached) behind.  The activated cryogenic source assembly can then be moved into a shielded transport container for proper disposal.  A new cryogenic assembly can then be lowered onto and attached to the Be and bottom LN shield plate.  The outer vacuum shell can then be lowered into place and connected to the rest of the assembly.  At that point, we will leak check the entire system.  After it has passed the leak check, we will pump the source down and can carry out cryogenic tests.  Once it passes the cryogenic tests, we will warm it up and vent it.  At that point, it can be installed into the Area B cave using the inverse of the procedure used to remove it.  We estimate that this operation will take about one week to accomplish.  Thus, if necessary we can completely replace the UCN source during one of the regular one-month-long maintenance shutdowns.

We note that the LHe refrigeration system that was used to provide cooling for the LD2 target still exists on the roof above the Area B cave.  Some minor refurbishing is required to make it operational, but it will provide sufficient cooling power for the SD2 source.  Vacuum insulated LN transfer lines also exist as do essentially all of the components for a He gas recovery system.  In addition, all of the personnel protection interlocks, fences, gates, etc. are either still in place or can be easily reinstalled.  We also note that Area B has about 600 square meters of floor space for experiments, a roof height of about 10 meters, a 30 ton bridge crane, a large roll-up door to bring equipment into the Area B experimental hall, adequate HVAC, large amounts of AC power and cooling water, and a well shielded cave for the SD2 source.  Thus, it is an ideal location in which to carry out UCN measurements.

Figure A6.1.  Plan view of Area B at LANSCE.  The dedicated SD2 source would be located in the cave marked LD2 target.  The UCN beta asymmetry experiment would be located in the Area B Hall (close to where the old MRS spectrometer is shown).

Figure A6.2.  Preengineering view of the SD2 source and storage bottle.

Figure A6.3.  Schematic of the UCN storage arrangement for a Line B source.

Figure A6.4.  UCN production rate as a function of

tungsten  target diameter.

Figure A6.5.  UCN production rate for W and Pb targets as a function of target length for two different source geometries (15.8 and 19.8 cm diameter SD2 sources).

Figure A6.6.  UCN density achievable with different moderators as a function of moderator thickness.

Figure A6.7.  Cold neutron energy spectrum as a function of the polyethylene moderator thickness.

Figure A6.8.   Stored UCN density as a function of the SD2 volume.

Figure A6.9.  Scaled UCN decay rate in the beta asymmetry experiment as a function of SD2 volume.

Figure A6.10.  Neutron densities in the storage volume as a function of time after the proton pulse.

Figure A6.11.  Initial ramp up to equilibrium density using the measured UCN flux from the prototype source for proton pulses of 1 second duration every repeated every 10 seconds.

Figure A6.12.  The expected instantaneous temperature rise in the SD2 for a 10 C pulse as a function of distance in the SD2 above the bottom of the source.

Figure A6.13.  Line B /C and the switchyard section of the LANSCE accelerator.  The fast kicker magnet will be located at the position marked Beam Switchyard.

Figure A6.14.  Line B layout.  The beam line between the elements labeled LB-BM-02 and LB-PO-02 is extant while we need to replace the section of Line B between the elements marked LB-PM-01 and LB-ST-01.

APPENDIX 7

DESIGN OF THE BETA ASYMMETRY EXPERIMENT

A7.1.	EXPERIMENT LAYOUT

The SD2 source will be used to provide UCN to the beta asymmetry spectrometer.  A 4 x 4 cm  diamond-coated UCN guide tube will transport UCN from the SD2 source (located in the Area B LD2 cave) to the spectrometer (located in the Area B experimental hall).  The UCN will be polarized by passage through a 7 T superconducting solenoid. The UCN will then pass through an Adiabatic Fast Passage (AFP) coil that will allow rapid spin flipping of the UCN.  The magnetic field in the AFP solenoid at the spin-flip point is chosen to be the same as the field strength in the UCN bottle solenoid.  Thus, it is possible to move the UCN into a high magnetic field region without a substantial change in the velocity distribution of the UCN while at the same time polarizing and spin flipping the UCN.

The UCN are injected into the spectrometer through a 2-cm ID diamond-coated guide that penetrates through a specially-designed aperature in the side of the superconducting solenoid.  The spectrometer consists of a 3-m-long UCN guide tube which define a decay volume for the UCN. A 1.0 T magnetic field is generated along the axis of the UCN guide tube by a superconducting solenoid.  At the ends of the decay tube, the magnetic field is expanded in the region before the detector.  The strong magnetic field is used to determine the neutron spin direction and to guide the electrons from neutron decay out of the apparatus into a position-sensitive electron detector.  As a neutron passes through a spatially varying magnetic field, the projection of the neutron spin (and the degree of neutron polarization) is an adiabatic invariant. The electrons from neutron decay spiral around the magnetic field lines.  The experiment takes advantage of the adiabatic invariants of the electron motion to transform perpendicular momentum into longitudinal momentum and “bury” the electron in the detector, thus reducing backscatter.  The position-sensitive electron detector will be used to identify the location of the neutron decay within the decay volume.  The betas will be stopped and their energy measured in a plastic scintillator.  The spectrometer is shielded against both neutron and gamma backgrounds.

The UCN exiting the decay tube are monitored in an array of UCN detectors (surface barrier detectors with a thin 6LiF layer plated onto them), are transported down a diamond-coated UCN guide to a 3He detector, or are captured on 6LiH surfaces in the region between the decay tube and the detectors.  Thus, the UCN are effectively pumped away at the ends of the decay tube, thus strongly reducing the number of neutron decays in the field expansion region.

We will be able to measure the depolarization of the UCN in situ by using the 7 T superconducting solenoid as both a polarizer and an analyzer.  This is done by polarizing the UCN when filling the UCN bottle, closing off the bottle for some time, then emptying the bottle first through the 7 T solenoid (now acting as an analyzer) and then finally counting any wrong spin state neutrons left in the UCN bottle.  By also installing UCN valves at the inlet of the polarizer, one can also search for depolarization effects due to multiple passes of the UCN through the AFP and polarizer.

A7.2.	POLARIZATION OF UCN

There are methods to substantially improve the knowledge of the neutron beam polarization using bottled UCN. This can be done because of the ability to obtain a 100% polarization using a magnetic field gradient.  The kinetic energy of the UCN is so small that UCN of one spin state cannot overcome the potential barrier due to the .B interaction of the neutron spin with the magnetic field.  For a critical velocity cutoff of the guide of 7 m/s (e.g., for diamond), a field of ≥ 6 Tesla is sufficient to provide 100% polarization of the UCN.  The use of magnetic fields has a secondary advantage of reducing the backgrounds compared to those generated when supermirrors are used to polarize the neutron beam. The collaboration has already secured funding for an integrated spin-flipper/polarizer which incorporates a strong field polarizer (B = 7 T).

A7.3.	SPIN FLIPPING

In order to measure the beta decay asymmetry using super-ratios of count rates in the detectors (a procedure that cancels out many potential systematic problems) one is required to flip the direction of the neutron polarization.  This poses several challenges to the experimenter.  The most straightforward method to perform this operation is to reverse the direction of the solenoidal polarizing field and the holding field in the observation geometry.  This will lead to the polarization vector pointing the opposite direction.  Reversing the magnetic field has two important limitations.  It must be done slowly, precluding spin-flip sequences performed on time scales comparable to the projected holding time for UCN in our observation guide (5 s).  Also, the magnetic field is directly coupled to the observation geometry, since electrons are guided along the field lines into the detector faces.  In order to use this method, great care must be taken to ensure that no artificial asymmetries are introduced due to the field reversal.  While we believe this may be possible, we would certainly prefer not to rely on this as our only means of spin flipping.

These limitations can be overcome using adiabatic fast passage (AFP) to flip the spins of the 100% polarized UCN leaving the polarizer solenoid.  The polarizer / AFP unit we are constructing consists of a superconducting solenoid magnet 17.5 cm in diameter and 1.5 meters long (see Figure A7.1) which integrates a 7 T polarizing field with an AFP geometry following the strong polarizer fields. After being polarized by passage through the 7 T superconducting solenoid, the UCN are directed into an AFP solenoid with a central field at 1.0 T.  AFP occurs in a region with a very small gradient along the magnetic field direction superimposed on a very homogenous field (0.006 T/m over a 30-cm region).  The field in the AFP solenoid is tapered so that the UCN first see a field of 2.0 T followed by a field with a central value of 1.0 T which has a small constant gradient with a field homogeneity of better than 10-3 over a 30 cm long region and a field at the exit end of the solenoid of 0.5 T.  This ensures a high degree of adiabaticity in the spin flip.  The RF frequency is chosen so that the spin flip occurs in a field Bspin flip which is equal the magnitude of the field in the UCN bottle from the solenoid Bsolenoid , i.e.,

Bspin flip    =  Bsolenoid

This condition ensures that the velocity distribution of the spin-flipped neutrons in the UCN bottle is similar to the velocity distribution of the non spin-flipped neutrons.

In the AFP region, a strong rf field (about 5 Gauss) is introduced, with a resonant frequency corresponding to 1.0 T (which requires an rf frequency of about 30 MHz).  The rf fields are introduced using a birdcage geometry, 34)  with the conductors flared to produce a gradual tapering of the rf field intensity away from the resonance region.  The end result is that the UCN sees a slowly varying field in its rest frame.  As long as the relative variations in the effective field (the vector sum of the holding field Ho and the rf field H1) are slow compared to the precession time, very little depolarization should result.  In our geometry, the adiabatic condition should be well satisfied, as 35)

(P/P = v( Ho / (He2 < v( Ho / (H12=10-3

Under worse conditions, experiments at SLAC achieved AFP efficiencies of 99.9% (.i.e. the depolarization experienced by 3He was smaller than 0.1% per AFP cycle). 36)

We have investigated the effect of depolarization due to the wall materials in the AFP apparatus and due to magnetic field inhomogeneities.  Depolarization due to wall materials is discussed in Section A7.4, and has been measured for several wall materials that were found to be acceptable.  We can also place an upper limit on the depolarization due to gradients using the equations of Gamblin and Carver. 37)  The depolarization rate due to inhomogeneities decreases very rapidly with increasing overall magnetic field strength; therefore, a conservative estimate of the depolarization rate must use the smallest effective field strength experienced by the UCN.  Using a field strength of only 5 Gauss and radial derivatives of a few Gauss/cm at the guide tube wall, one obtains depolarization rates below 10-4,  resulting in acceptable depolarization rates for the experiment as a whole.

Flipping the spins with AFP gives the experiment two independent methods of reversing the sign of the experimental effect, permitting one to independently assess the magnitude of more subtle spin dependent effects which depend on the alignment of the holding field in the observation guide (which should be small, but must be checked) and the effects of introducing large amplitude rf  fields (which may influence detector performance).  We also note that the efficiency for loading the observation volume with a particular spin state can influence the measured asymmetry by coupling to a rate dependent gain shift.  Our detector design should minimize the presence of these shifts, but having two separate methods for performing the spin flip provides an independent test for these effects as well.

A7.4.	DEPOLARIZATION OF UCN

Recent measurements 38) by members of our collaboration (led by Serebrov) have made the first quantitative assessment of depolarization of UCN in material traps.  This study introduced UCN to a trapping volume coated with beryllium, and then introduced various foils to measure changes in the depolarization rate.

The apparatus used for making these measurements is depicted in Figure A7.2.   A 100-liter Be-coated UCN bottle was filled to a density of about 6 UCN/cm3 from the turbine source at the ILL.  This bottle was connected to a similar UCN bottle by a UCN guide that passed through a 4.5T superconducting solenoid.  Valves at the entrance and exits could be opened and closed so that only UCN in one polarization state can enter the second bottle.  That bottle is then shut for a period of time (up to several hundred seconds) and then allowed to exit through the solenoid.  Any UCN that underwent a spin flip are then trapped in the second bottle.  The spin-flipped UCN are detected by opening a valve to a UCN detector on the second bottle.  It was possible to place thin sheets of other materials in the UCN bottle, thus providing a means to study depolarization from different materials.

|  | Probability of spin flip per collision (10-6) | Probability of losses per collision (10-5) |
| --- | --- | --- |
| 1. Be (trap) | 7.2±0.7 |  |
| 2. Be (trap+foils) | 7.7±0.7 | 7.1±1.1 |
| 3. SiO (guartz) | 14±1 | 59.8±6.0 |
| 4. BeO (before outgassing) | 48±5 | 168±15 |
| 5. BeO (after outgassing) | 44±4 | 74±7 |
| 6. Glass: SIO2 81% B2O2 13% Na2O+K2O 4% Al2O3 2% | 95±9 | 315±30 |
| 7. C (graphite) | 1.9(1.0 | 18.6±2.0 |
| 8. Brass (63% Cu, 37% Zu) | 1.1(1.0 | 19.3±2.0 |
| 9. Cu | -1.2(1.0 | 20.0±2.0 |
| 10. Teflon (CF4) | 1.8(1.0 | 23.5±2.0 |

Table A7.1.  The spin-flip probability and loss probability per surface collision for various materials.

The results are shown in Table A7.1.  The depolarization rates for C, brass, Cu, and teflon are all reasonably consistent with about 10-6 spin flip probability per collision, which meets the needs of our experiment.  The sensitivity of the measurement was limited by the use of Be (which turned out to have a rather high probability of spin flip) as the liner material for the UCN storage bottle.  We are now carrying out further depolarization measurements at the ILL using a Cu-coated UCN bottle.  At present, all available information indicates that carbon (in the form of a diamond-like coating) will make a good wall material for polarized UCN.

There is also data on the depolarization rate of UCN on diamond surfaces from the ILL EDM experiment. 39)  The EDM experiment uses a diamond-coated cell for holding the UCN while they spin precess.  Measurements with two size cells (50 and 100 liters) have been made and a lower limit on the depolarization rate of 1000 s has been set.  All of the evidence indicates that the depolarization time in the EDM cell is limited by magnetic field nonuniformities in the cell (mainly due to the UCN valve located at the entrance to the cell) and that the intrinsic relaxation rate is much longer than 1000 s.  Thus, experimental data provide a conservative limit of a depolarization of < 5 x 10-3 in a bottle with a holding time of 5 seconds.  Thus, all data and calculations indicates that the depolarization relaxation time is quite likely to be sufficiently long that depolarization in the UCN bottle in the beta asymmetry experiment will be negligible.

Using the data in Table A7.1, and assuming that graphite and diamond will have the same depolarization rate, we assign a spin-flip probability per wall collision of 1.9 x 10-6 (at the 1  level).  This results in a net depolarization of 7.3 x 10-4 for our bottle.  We plan to measure the depolarization rate more accurately with diamond films during our depolarization measurements at the ILL.

We will be able to measure the depolarization of the UCN in situ by using the 7 T superconducting solenoid as both a polarizer and an analyzer.  This is done by polarizing the UCN when filling the UCN bottle, closing off the bottle for some time, then emptying the bottle first through the 7 T solenoid (now acting as an analyzer) and then finally counting any wrong spin state neutrons left in the UCN bottle.  In practice, this is done as follows (refer to Fig. A7.3 for the shutter locations).  The shutters (marked 5 and 6) on the end of the bottle are closed and the UCN bottle is filled with UCN from the rotor source (the UCN switch is in the source position) which are polarized by passing through the 7 T superconducting solenoid.  Shutter #3 at the inlet to the UCN bottle is closed and the UCN are stored in the bottle for varying periods of time (tens to hundreds of seconds).  During this period, the UCN switch in front of the polarizing solenoid is moved to the UCN detector position.  Shutter #3 is then opened and the correct spin state neutrons flow back out through the polarizer (now used as an analyzer) to be counted in the UCN detector.  The polarizer acts as a magnetic shutter for an UCN which have undergone a spin flip while sitting in the UCN bottle.  After all of the correct spin state neutrons have flowed out of the bottle only the wrong spin state neutrons are left in the bottle. (We note that after opening shutter #3 it takes only 50 seconds for the correct spin state neutrons to be completely emptied out of the bottle at the 10-4 level.)  Shutter #4 is then opened and the wrong spin state neutrons are detected in a 3He UCN detector.  This measurement can also be made with the AFP on, giving a result which measures the combination of depolarization in the bottle and the AFP spin flip efficiency.

We estimate that this procedure will provide a sensitivity to depolarization at the 10-3 level in one cycle (which takes about two minutes to complete).  After 100 such cycles (taking about 3 hours), we can determine the depolarization with an accuracy of 10-4.  Thus, it is possible to measure the depolarization in situ regularly throughout the course of the experiment.

It is also possible to test for depolarization effects due to multiple passes of the UCN through the AFP and polarizer.  In the case of testing for depolarization in the AFP, this would be done by closing shutter #3, filling the AFP guide tube region with polarized UCN, closing shutter #2, moving the UCN switch to the detector position, opening shutter #2 and counting the correct spin state neutrons in the UCN detector, and then opening shutter #3 (with shutters 5 and 6 closed and shutter #4 open) to count the wrong-spin state neutrons.  Similarly, one can study depolarization effects in the combined polarizer - AFP system using the same sequence except replacing the use of shutter #2 with shutter #1.

Finally, we note that the spatial homogeneity conditions required on the magnetic field for an accurate beta asymmetry measurement are much more stringent than is required to maintain the UCN polarization.

A7.5.	SPECTROMETER

A7.5.1.	OVERVIEW

The correlation spectrometer consists of a long UCN guide tube (really an open-ended bottle) with a uniform magnetic field and an expanded field region at the ends of the UCN guide.  Detectors consisting of a scintillator - proportional counter combination are placed in the expanded field region.  This combination allows both position information from the multi-wire proportional counters (MWPC), total energy information (from the scintillator), and some information on the pitch angle of the electron (from the dE/dx measurement in the MWPC).  In the expanded field region, the pitch angle of electrons decreases as the electron moves the high field to the low field region.  This reduces the backscattering amplitude of electrons from the MWPC windows and from the scintillator.  In addition, if the backscattered electrons have deposited some energy in the scintillator, it is likely they will be reflected back into the scintillator due to the magnetic mirror effect.  The schematic design of the spectrometer is shown in Figure 4.

A7.5.2.	MAGNETIC FIELD CONFIGURATION

It is essential that the magnetic field over the entire decay region be uniform at approximately the same level as the asymmetry that accuracy of the result is desired.  Any field nonuniformity can result in electrons being reflected during to the magnetic mirror effect.  Thus, an electron starting off in one direction may be turned around and observed in the wrong detector, thus creating an artificial asymmetry.  Our specification for the magnetic field uniformity is that it be better than 5 x 10-4 over the fiducial volume of the UCN bottle.

At the two ends of the spectrometer there is a field expansion region inside a Pb shield lined with 6LiH-TPX.  The field will be expanded by 40% in this region so that the diameter from the entire UCN volume that is viewed is 10 cm in diameter.  Thus, the fiducial volume of the UCN bottle is 10 cm in diameter and this ensures that betas that may strike the wall cannot be viewed by the detector.  The pitch angle of the electrons as they move from a field of strength Bo into a field of strength B is given by:

sin  = (B / Bo)1/2 sin o

Thus, for a field expansion ratio of 0.6 the maximum angle of betas striking the detector is 51o from normal.  This forward peaking of the electron trajectories greatly reduces backscatter.  We plan to accurately map out the entire field region using triple-axis magnetometers and to monitor the magnetic field on-line continuously with several triple-axis magnetometers.43)  This geometry strongly suppresses backscattering effects by mirroring the backscattered betas back into the detector.  The spectrometer is shielded against both neutron and gamma backgrounds.

In order to have a large enough decay volume to achieve the desired counting rate, a decay region with a volume of a few tens of liters is required.  Given the constraint of keeping the detector small in order to keep backgrounds low, along with the requirement of a small enough diameter for the MWPC that the window can be kept thin, the diameter of the detector cannot exceed about 15 cm.  We use a field expansion ratio of 0.6 from the decay region to the detector.  We also require a fiducial volume cut of at least 1 Larmor diameter in the decay volume in order that electrons which interact with the wall are not accepted in the detector.  Assuming a 1.0 T field, the radius a 782 keV beta makes is 3.9 mm.  Thus, the decay region should have a diameter of approximately 10 cm.  To achieve a decay volume of 25 liters, the decay region must be about 3 m long.  Thus, we plan for an UCN bottle with an inner diameter of 10 cm and a length of 3.0 m resulting in a bottle volume of 24.5 liters.

The magnet providing the field in the UCN bottle is a 4.5-m long, 25-cm ID warm-bore superconducting solenoid as shown in Fig. A7.5.  The magnet is comprised of 17 individual coils in order to do the field shaping to the level required.  At the center of the magnet is a 3-cm ID aperture that penetrates through the side of the magnet into the central bore of the magnet.  To accommodate this warm-bore penetration requires a 7-cm gap in the coil windings in this region.  In the gap, the coil windings are first brought radially outward and then looped around in half-circle.  They windings then go radially back inward to the same radius as the rest of the coil windings.  This forms a “butterfly” pattern in which there are extra fields generated from the coils on both sides of the gap moving outward, then around in two half-circles, and then back inward.  One can show analytically that this sort of coil pattern generates an extra magnetic field that dies off as R5, where R is the radius of the coils of the butterfly pattern.  We and American Magnetics have both carried out detailed magnetic field calculations and find that it is possible to generate a magnetic field of 1 Tesla on the central axis of the solenoid that has a field uniformity of 1 x 10-4.  We have also calculated the magnetic field uniformity along a line which is 5 cm radially out from the central axis and in line with the two penetrations through the side of the magnet.  As expected, the field uniformity as one approaches the penetrations becomes worse, but in the worst position (at center of the solenoid 5 cm off axis in direct line with the penetration) the field uniformity is still good to 5 x 10-4.  This is more than adequate for the beta asymmetry experiment (as detailed in the discussion of systematics in Appendix 11).  The design of the solenoid along with the calculated field profiles is shown in Figure A7.5.

At the ends of the solenoid are two 50-cm diameter conventional resistive coils that are located at + and – 2.5 m from the center of the superconducting solenoid.   These coils provide for the field expansion region required to minimize backscattering with a field at the center of the coils of 0.6 Tesla.  They consist of 1-cm square hollow copper conductors wound in 10 layers deep x 10 layers long.  The coils are run at 830 A and consume 28 kW per coil.  The current density in the coils is limited to 1000 A/cm2, a value well within the normal operating range for conventional magnets.  The required power supplies are available from LAMPF surplus and adequate water cooling already exists in Area B.

There is a gap between the solenoid and the resistive coils to accommodate the beta detectors, as shown in Figure A7.4.

A7.5.3.	UCN BETA DECAY TRAP

UCN can undergo total external reflection from a variety of materials.  We are faced with the following set of problems:  1)  The UCN must be confined to a region of constant magnetic field and 2)  There can be no UCN containment windows that allow backscattering of beta decay electrons in the constant magnetic field region.  A solution to this problem is to use the slow diffusion of UCN in a non-specular guide as a confinement mechanism.

The beta decay trap consists of a 3-m long, 10-cm diameter, UCN diamond-coated guide coupled to the UCN source. UCN propagate diffusively in the trap, which is to say they undergo a random walk along the axial direction.  For a guide of radius R and length Z, the transmission probability through each end of the storage guide, assuming no losses on the guide walls, is W = 8R / 3Z = 0.112 for the proposed dimensions.  Since the UCN density falls off roughly exponentially along the guide, it is prudent to have some fraction of the length be made of specular guide, followed by diffusive sections at each end which serve to confine the UCN to the central region.  This would maximize the useful fiducial volume.  Monte Carlo simulations indicate that the highest beta decay rate is achieved with a central specular region that is 2 m in length with 0.5-m long diffuse sections at the ends of the trap.

It is important to ensure that the number of UCN that decay within the field expansion region is sufficiently small that those decays do not distort the measured asymmetry to any appreciable degree.  We plan to coat the inside of the field expansion region with a thin film of TPX (a material with a critical velocity of 0 m/s) containing a small amount of 6LiH (as shown in Figure A7.4).  The lifetime of UCN in this region should be of order the time it takes to transit the diameter of the bottle in that region.  For an UCN with a typical velocity of 5 m/s, the average transit time is about 50 ms, compared to the 5 seconds it spends in the decay tube.  However, it is only those UCN that decay within the region that can be viewed by the detector that can contribute to a false asymmetry.  That fraction is about 40% of the UCN of the UCN exit the decay tube.  Our Monte Carlo calculations indicate that approximately 60% of the UCN exit the decay tube from the ends.  Thus, the decay probability of an UCN in the field expansion region is the product of the relative time spent in the field expansion region viewed by the detectors and the relative UCN density in the field expansion region, or about 2.5 x 10-3.

A suitable wall material might be diamond film deposited onto the inner surface of a quartz tube.  Such a surface would likely have a UCN storage time of order 100 seconds, and a rather high effective potential.  Furthermore, the depolarization time for such a surface would be extremely long.  Sandia National Laboratory now can produce diamond films using laser ablation of graphite.  These films have a density of about 3.0 (compared to 3.2 for diamond), have a large number of diamond-like bonds, can be made self-supporting with thicknesses of a few microns, have optical-quality surface finish, and contain only 2 ppm hydrogen.  These films can be annealed and survive repeated temperature cycling.  Thus, they appear ideal for our applications.  We are now in the process of testing these films for UCN transmission and reflectivity.  UCN reflectometry measurements have already been made on samples and indicate a critical velocity of 6.95 m/s.  An alternative is diamond films made by high-temperature CVD from deuterated methane.  Films produced in this way have been used in the EDM experiment at the ILL and exhibit long lifetimes and small depolarization.  We plan to accurately measure (we have approved beam time in collaboration with Serebrov) the depolarization of UCN from these films at the ILL in the very near future.

The diffusive sections at each end could be easily made by either chemically etching or mechanically roughening the surfaces along a length at each end of the storage guide.

The fiducial volume of the bottle is taken to be the full length of the beta decay trap (3.0 m) and a cross-sectional area which excludes the region in which betas from UCN decay may strike the bottle ways before reaching the detectors.  The radius of gyration  of an electron in a magnetic field is given by:

 (mm) = 1.70 [(+2)]1/2 / B(Tesla)

where  is the electron energy in units of the rest mass of the electron.  For a magnetic field of 1.0 T, the maximum diameter of the betas at the neutron beta decay endpoint is 7.76 mm.  Allowing a safety factor of 10% results in a guard region of 8.54 mm.  This results in a usable diameter of 8.3 cm, giving a 69% fiducial volume.

A7.5.4.	DETECTOR SYSTEMS

For electron detection we propose to use two separate configurations.  In one, the energy of the electrons is measured with low resolution using fast plastic scintillators.  The fiducial volume of the detector is determined by a wire or drift chamber, possibly operating in Time-Projection mode. In the second detector configuration, Si microstrip detectors are used to provide very good energy resolution but with increased backscattering.  The improved energy resolution would allow study of the energy dependence of the correlation (there is an expected v/c dependence) as a systematic check on the performance of the spectrometer and to measure other effects such as Weak Magnetism.  We would begin the experiment with the scintillator/wire-chamber configuration because of the more straightforward technology, but we would take additional data with Si detectors with dramatically improved resolution and considerably different systematics.

The wire chambers for the beta detector are an important component of the experiment because they define the counting volume, and in coincidence with the plastic scintillator they minimize the background. The goals in designing the wire chambers are to obtain high counting efficiency while minimizing the mass and average Z to minimize electron backscattering. The proposed detectors will consist of a gas volume approximately 2 cm thick with a thin entrance window and a thin exit foil.  In the center there will be a plane of anode wires of 10 micron diameter gold plated tungsten spaced with a 1 mm separation in order to minimize the wires as a source of backscatter.  Cathode signals, each 5 mm wide, will be readout from strips etched 44) on a thin beryllium-coated mylar foil separating the wire chamber from the scintillator.  The cathode strips and anode wires will be orthogonal so that X-Y coordinate pairs will be provided by the wire chamber.  Position information will be determined with about 1 mm spatial resolution.  Each cathode strip will be connected to a preamplifier and then to a time-above threshold discriminator and TDC while the anode wires will be ganged together in sets of five and connected to a preamplifier, discriminator, and an ADC.

While it is possible to use thin aluminized mylar for the windows, we propose to construct the entrance windows using a technique we have described previously of pre-forming the window to a cylinder and supporting it with Kevlar yarn.40-42)  The windows are coated with about 1000 Angstroms of Be on the outside (to serve as a UCN reflector) and on the inside by a thin coating of beryllium strips (to serve as cathode pickups for the detector).  We have constructed windows with an average areal density of 2.4 mg/cm2 capable of supporting 1.09 bar. We propose to extend this technique by using carbon fibers to produce a strong window with better defined density variations. We believe it should be possible to achieve window thickness on the order of 1 mg/cm2 over the 15 cm diameter needed for this experiment which will reliably support up to 300 mbar  (although some development effort will be required).

| Gas | Pressure | Source | Beta Energy | Efficiency | Rate |
| --- | --- | --- | --- | --- | --- |
| Isobutane | 250 torr 750 torr | Back- ground | N/A | 98.5 | 1.6Hz |
| Isobutane | 250 torr 750 torr | 2 in. Pb Back. | N/A | 99.1 | .44Hz |
| Isobutane | 700 torr | Sr 90 | .55 MeV 2.28 MeV | 99.9 % | 52 Hz |
| Isobutane | 250 torr | Sr 90 | .55 MeV 2.28 MeV | 99.9 % | 51 Hz |
| Pentane | 700 torr | Sr 90 | .55 MeV 2.28 MeV | N/A | N/A |
| Pentane | 250 torr | Sr 90 | .55 MeV 2.28 MeV | 99.8 % | 59 Hz |
| Isobutane | 700 torr | Tl 204 | .76 MeV | 99.6 % | 14 Hz |
| Isobutane | 250 torr | Tl 204 | .76 MeV | 99.6 % | 14 Hz |
| Isobutane | 700 torr | Tl 204 2 in. Pb | .76 MeV | 99.9 % | 13.5 Hz |
| Isobutane | 250 torr | Tl 204 2 in. Pb | .76 MeV | 99.9 % | 12.6 Hz |

Table A7.3.  Measured efficiencies of prototype wire chambers.

At this pressure a heavy hydrocarbon gas, such as pentane provides a high electron density to keep dE/dx and the chamber efficiency up, while keeping the average Z in the gas down to minimize backscatter effects.  Wire chambers have been operated at low pressures (below 100 mbar) with pure hydrocarbon gasses in applications requiring good time resolution for heavily ionizing particles.43,44)  Some development effort will be required to determine the ideal gas for this application, but it is likely a very simple, one component, heavy hydrocarbon gas will suffice.

At 300 mbar of pentane a 700 keV electron incident normal to the chamber will loose on average 2.43 keV of energy in the chamber gas. In this gas the number of primary ion pairs (this is about 1/5 of the total number of ion pairs) produced is expected to be about 10 pairs / keV.45)  The total number of ion pairs produced (24) in the gas, even at this low pressure, should be enough to ensure close to 100% detection efficiency if the noise levels allow thresholds below the several electron level. With chamber gains of 104 or so this should be achievable.

We have made measurements of the efficiency of a prototype MWPC counter.  The counter has three detecting planes and the efficiency is defined as the ratio of the three-way coincidence and the coincidence of the first and third planes.  The rate is defined by the number of three-way coincidences per second.  The data taken so far does not show a great advantage to using pentane over isobutane.  Further study of lower energy betas may favor pentane.  Shielding with two inches of lead cut the background by 75 percent.  This shielding also brought the 204Tl efficiencies up to 99.9 percent (the lower efficiency value without the lead is due to inclusion of background which does not generate a three-fold coincidence in the detector).

The scintillators will be 3.5 mm, 15 cm OD thick plastic scintillators.  (The range of 782 keV betas in plastic scintillator is 3.1 mm.  Allowing for a small safety factor sets the scintillator thickness to be 3.5 mm.)  We will use Bicron BC-400 scintillator that has a light output of 65% of anthracene, and a 2.4 ns decay constant, and an attenuation length of 250 cm.  The scintillators will be coupled to 4 light pipes that are approximately 40 cm long which are mated to 50 mm diameter fast (3 ns rise time, 4 ns FWHM) photomultipliers (RCA 8850).  An optical fiber will be connected to the four light pipes in order to allow a LED pulser signal to be fed into the scintillator package for use in gain stabilization.  Requiring a coincidence between at least two of the PMTs will greatly reduce the noise due to dark current.  With the specified background noise rate of current of 5 kHz for these PMTs, using a 10 ns coincidence window between two PMTs will result in a residual noise rate of only 0.25 Hz.  By cooling the PMTs to 10 oC, this rate will be further reduced to 0.02 Hz 46) and thus is negligible.  We also note that this geometry is very favorable to good light collection efficiency and we thus expect to achieve better energy resolution than was possible in the PERKEO experiments that used thin plastic scintillators coupled by only two light pipes edges to the PMTs.

We have constructed a prototype scintillator that consists of 3.5-mm thick, 15 x 15 cm standard Bicron scintillator.  The scintillator is directly coupled to four light guides that come out in the direction of the plane of the scintillator at 90o to each other.  The adiabatic light pipes are coupled to fast (RCA 8850) PMTs.  Initial tests are underway to fully characterize the threshold, counting efficiency, resolution, and linearity of the prototype scintillator.

The PMTs will be in a fringe field of the solenoid magnet of order 5 Gauss.  The PMTs have a sensitivity to magnetic fields of a reduction in output amplitude by 50% in a field of 3 Gauss along the axis of the PMT and of 1-2 Gauss (depending on orientation) for fields transverse to the PMT axis.  To achieve 98% of the zero-field output amplitude, we need to reduce the fringe field to about 400 mGauss.  This can be readily achieved using Mu metal shields.  In order to check the stability of the PMTs and associated electronics, a stabilized LED pulser will be connected to each scintillator by a small light pipe.  Typical response functions measured using monoenergetic electrons are shown in Figure A10.3.

We are also prototyping Time Projection Chambers (TPC) and Si microstrip detectors. A small TPC has been assembled in order to compare its response to Monte Carlo predictions. The use of such a detector in the beta decay asymmetry measurements would provide direct information on the angular correlation in the decay, a very useful systematic check. Information on the decay angle also allows an improvement in the statistical uncertainty as the asymmetry is proportional to cos ( as with complete (and perfect) angular information the statistical precision is improved by a factor of 2.0 compared to averaging over all angles. We are also working with Micron Semiconductor and the Space Radiation Physics group at Caltech to develop appropriate Si detector systems for our experiment.

A7.5.5.	ELECTRONICS

The electronics associated with the PMTs are shown in Fig. A7.6.  There are 4 primary requirement of the scintillator electronics:  1)  to reduce single photoelectron noise,  2)  to achieve optimum energy resolution, and 3)  to maintain fast timing capability.  Requirement 1) is achieved by requiring a fast coincidence between at least two PMTs.  Requirement 2) is achieved by using linear gates to eliminate noise contributions from PMTs that do not have any signal above threshold.  Requirement 3) is achieved by using fast PMTs (RCA 8850) with a rise time of 3 ns and a FWHM of 4 ns) coupled to a fast scintillator (Bicron 400 with a decay constant of 2.4 ns) and fast electronics with constant fraction discriminators to reduce the effects of slewing.  The discriminator outputs from each scintillator are fed to a TDC in order to determine the time ordering and delay time between events in which a beta first strikes one detector and is backscattered into the other detector.

The electronics associated with the wire chambers are shown in Fig. A7.7.  There are 3 primary requirements of the wire chamber electronics:  1) to provide background reduction, 2)  to provide position information, and 3) to identify backscattered betas.  Requirement 1) is achieved by the coincidence requirement between the scintillator and the wire chamber.  Requirement 2) is achieved as both X and Y position information is provided by individual ADC readout of each cathode strip of the wire chambers.  Requirement 3) is achieved by using dE/dx information to identify double ionization events in the wire chambers.  This is only partially successful as there is a range of ionization in the wire chambers depending on the pitch angle of the betas as they traverse the wire chambers.  Thus, there is some overlap of dE/dx values for single betas traversing the wire chambers and backscattered betas that pass through the wire chambers twice.  However, if we are able to measure the diameter of the beta track in the MWPC reasonably well (( 1 mm resolution), then having measurements of the total energy (from the scintillator), of the beta track diameter and dE/dx (from the MWPC), we would be able to determine the pitch angle of the betas.  This would provide an improved ability to reject backscattered electrons, to map out the angular distribution in (thus providing important information for studies of systematic effects), and to reduce the statistical uncertainty as the factor of 2.0 reduction in statistical significance (see section A9.3) would go to unity if we could reconstruct the angular information in the decay with perfect precision.

There are 32 channels of anode strips for readout of the X position, 32 channels of anode strips for readout of Y position, and 32 channels of cathode wire readout (5 cathode wires ganged together).  Each of the anode strips is connected to a preamplifier that is connected to a time above threshold discriminator.  The TDC reads out both the rising edge and the falling edge of the discriminator signal so that in addition to the timing information, one can get an approximate measure of the amplitude of the signal.  The amplitude information allows one to interpolate the position between cathode strips.  The signals from the anode wires provides accurate dE/dx information.  Timing information between the MWPCs and the PMTs at the two ends of the spectrometer is obtained by feeding discriminator outputs from the detectors into another TDC.

A7.5.6.	DAQ

For data acquisition (DAQ) we are considering two options: an existing PC-based system (PCDAQ) developed at LANSCE as a multi-purpose program for CAMAC-based systems and a PC-linux based system coupled to the CERN PAW or ROOT packages. Our collaboration has extensive experience with both of these systems and we will choose the system that best meets our needs.

Figure A7.1.  Schematic view of the UCN polarizer/spin flipper.  The magnetic field profile along the central axis of the superconducting magnet is also shown.

Figure A7.2.  Schematic view of the depolarization test system used at the ILL.

Figure A7.3.  Top view of the beta asymmetry spectrometer.

Figure A7.4.  View of the detector system for the beta asymmetry spectrometer.

Figure A7.5.  Cross-sectional view of the superconducting solenoid and resistive coils at the ends of the solenoid.  The calculated field uniformity is also shown in the figure.

Figure A7.6.  Schematic diagram of the scintillator electronics.

Figure A7.7.  Schematic diagram of the wire chamber electronics.

APPENDIX 8

EXPECTED BACKGROUNDS

A8.1.	REQUIREMENTS

For the beta asymmetry experiment we would like to achieve a signal-to-background ratio of ≥ 100/1 with a threshold of 100 keV or lower.  Given estimated counting rates in the 100 Hz range, this translates to backgrounds in the Hz range or less.  Reaching these low background rates will require substantial effort and careful design.  There are two features of the beta asymmetry experiment that are central to background rejection:  the use of a strong magnetic guide field which allows 4 collection efficiency of the betas in a relatively small detector, and the use of a coincidence requirement between the proportional counter and scintillator in the spectrometer.

A8.2.	BACKGROUND MEASUREMENTS

Background measurements were made during the UCN running period of July 1997 with plastic scintillators and wire chambers.  Differential shielding measurements were also carried out during that period with a plastic scintillator in order to determine the amount of shielding that will be required for the beta asymmetry experiment.

Backgrounds associated with the spallation source are due primarily to two sources:  1) fast neutrons that moderate and then capture with some characteristic time constant producing a gamma ray and 2) “thermal” (i.e., moderated neutrons) which act as a dilute gas that also capture with some (possibly different) characteristic time constant producing a gamma ray.

Since it is currently not possible to deliver any beam to Area B, we cannot make any in-situ backgrounds measurements with beam on in Area B.  However, we have made background measurements at the Lujan Center in ER-1 at a distance of 1.5 m from the UCN rotor source shield wall and close to the FP11A beamline in ER-1.  Since the shielding of the Area B cave is quite similar to that in ER-1, we can use the ER-1 measurements as an estimate of what we can expect in Area B by scaling for the relative beam currents in Area B and ER-1.

The measurements were carried out using a 7.5 cm-diameter, 2-cm-thick plastic scintillator (Bicron BC-400) coupled directly to a 3” PMT.  The scintillator was calibrated using a 137Cs source.

The measured background rates under different shielding configurations are given in Table A8.1.  The total background rate is the total rate from about 20 keV to 1.1 MeV while the gated background rate has an energy cut for about 50 keV to 800 keV with a timing cut excluding the first 5 ms following the beam pulse.  We observed a strong increase in the total background rate for a period of a few ms following the proton pulse on the spallation target.  The two-dimensional plot of the background vs. time (modulo the PSR repetition rate of 20 Hz) along with the singles plot of the time and energy spectra are shown in Figure A8.1.  The beam-associated background is seen to decay away with a time constant of 2-3 ms.  Putting a 5 ms timing cut on the data following the proton pulse on target essentially eliminates the beam-associated prompt backgrounds.  Figure A8.2 shows the same plot, but with the energy and timing cuts placed on the data.

| Location/ Run # | Shielding Configuration | Total Background Rate (Hz) | Gated Background Rate (Hz) |
| --- | --- | --- | --- |
| ER-2 / 229 | 4” poly, 2” Pb bottom only | 508 | 394 |
| ER-2 / 231 | 4” poly bottom, 2” poly + 2” Pb all other sides | 15.7 | 6.1 |
| ER-2 / 232 | Same as 232, electrically isolate det | 11.1 | 4.9 |
| ER-2 / 233 | Same as 232 + add 2” poly top and sides | 6.6 | 3.1 |
| ER-1 / 238 | Same as 237 but remove poly all sides but bottom | 89.1 | 15.0 |
| ER-1 / 241 | Same as 233 | 49.1 | 11.1 |
| Area B | Same as 241, scaled for relative beam currents | 3.5 | 0.8 |
| Area B | Same as Area B, scaled for scintillator size in the beta asymmetry experiment. | 5.0 | 1.1 |

Table A8.1.  Measured and expected background rates in a 7.5 cm-diameter, 2-cm-thick plastic scintillator (no MWPC) with different shielding conditions.

Scaling by the relative beam current in Area B (5 A) compared to the data taken in ER-1 and ER-2 at 70 A, we arrive at an expected background count rate in Area B of 3.5 (0.8) Hz in the ungated (gated) spectrum.  This result must be scaled for the relative volume of the scintillator used in the background measurements (88 cm3) to those in the beta asymmetry experiment (62 cm3 each).  This results in a total expected beam-associated background rate (combined for the two detectors) in the beta asymmetry experiment of 1.1 (5.0) Hz for gated (ungated) operation, as is shown in Table A8.1.  This is already sufficient to meet our goal.  However, as some extrapolation is involved in determining these numbers, it would be prudent to further reduce the backgrounds.

A reduction in background can be achieved by placing a gas proportional counter in front of the plastic scintillator and required a coincidence.  This serves two purposes.  First, since the majority of the backgrounds are due to gamma rays, and gas proportional counters have very low sensitivity to gamma rays, the coincidence requirement should substantially reduce the backgrounds.  Second, position information from the proportional counter can be used to define the fiducial volume of the detector and thus eliminate edge effects.

In order to test the background reduction, we carried out measurements in ER-2 during the July 1997 run cycle.  Since the backgrounds in ER-1 and ER-2 are similar (except for absolute rate), this should provide a reasonable estimate that can be scaled to what we can expect in Area B.  These measurements used a 15 cm x 15 cm x 0.6 cm thick plastic scintillator sandwiched between two 15 cm x 30 cm x 1 cm thick gas proportional counter filled with 600 Torr of P-10.  This detector assembly was covered on all sides by 5 cm of lead and 2.5 cm of borated polyethylene.  The energy threshold on the plastic scintillator was set to about 30 keV.  The singles rate in the scintillator was about 90 Hz.  This dropped to 6.3 Hz when a wire chamber was placed in coincidence and to 3.4 Hz when a 1 msec counting period near time zero was removed from the counting time.

Several observations were made during these tests.   First, a significant source of background seemed to be associated with leaks in the shielding particularly through the floor. Second, the background was strongly peaked toward low energies.  Nonetheless, we observed a reduction of a factor of 14 by imposing only a simple coincidence requirement between the scintillator and wire chambers.  Taking the rate extrapolated to the two beta asymmetry detectors of 1.1 Hz in Area B, and including the reduction that can be achieved using the coincidence requirement with the scintillator, we arrive at an expected beam-associated background rate of about 0.1 Hz.

A8.3.	TYPES OF BACKGROUNDS

There are five types of backgrounds that must be dealt with:  1) backgrounds associated with the spallation source,  2)  room backgrounds from natural radioactivity, 3)  backgrounds from natural radioactivity within the spectrometer,  4) cosmic-ray induced backgrounds, and 5) backgrounds associated with capture of UCN in the spectrometer.

A8.3.1.	SPALLATION SOURCE BACKGROUNDS

Backgrounds from the spallation neutron source include protons, muons, pions, neutrons, and gammas produced by the spallation target.  Most of these backgrounds are strongly attenuated by the 4-m-thick bulk shield in the Area B cave.  The ambient background in ER-1 is primarily due to low-energy neutrons from the various beamlines and the overall radiation levels are typically a few mR/hr.  The room backgrounds in ER-2 due to spallation neutrons leaking out from beamlines is quite low ( < fraction of a mR/hr).  The room backgrounds in Area B should be lower than in ER-2 since the only neutrons brought out of the heavily shielded Area B cave are UCN and there are no other beam lines that will produce backgrounds in Area B.

It is also likely that there is a low-level component of neutron activation of materials in Area B.  In our background estimates, we assume that this component is a part of the natural room background.  When we made the background measurements in ER-1 and ER-2, the beam had been on almost continuously for a 4-month period.  Thus, it is a good approximation that any long-lived activities due to neutron activation had reached saturation level at the time of our measurements.  Since there has been no beam in Area B for more than four years, any neutron activation backgrounds in Area B should be significantly lower than in ER-1.

A8.3.2.	NATURAL RADIOACTIVITY - ROOM BACKGROUNDS

From the measurements listed in Table A8.1, it is clear that we need to provide adequate shielding (equivalent to at least 2” Pb plus 4” of borated polyethylene around the spectrometer in order to reduce room backgrounds to an acceptable level.  The background rate associated with natural activities in the room are already included in the background measurements made in ER-1 and ER-2 and thus are not included separately here.

A8.3.3.	NATURAL RADIOACTIVITY - SPECTROMETER BACKGROUNDS

Backgrounds from natural radioactivity within the components of the spectrometer arise primarily from uranium and thorium and their daughters, 40K, and cosmogenic activities such a 60Co and 137Cs.  Members of the collaboration have extensive experience in designing and constructing low background counting systems from work in nuclear beta decay (n, T2, and 19Ne) and in the SAGE and SNO solar neutrino experiments.  In determining the background we can expect in the beta asymmetry experiment, we make the assumption that we will not introduce any additional background above that which we measured in the fully shielded configuration of the plastic scintillator background measurements described above.  Estimates of the level of radioactivity that can tolerated in the spectrometer components indicate that the activity levels required of materials used in the spectrometer should be reasonably easy to achieve.  Thus, the assumption that we should be able to maintain the observed rates measured in the background tests seems to be a reasonable assumption.

A8.3.4.	COSMOGENIC ACTIVITIES

Cosmic-ray induced background has two components:  muons and hadrons.  The muon rate at LANSCE altitudes is about 0.016 Hz/cm2 and have an angular distribution of cos2 (where  is the angle with respect to a vertical axis).  The muons directly produce a signal both in the proportional counters and the scintillators.  However, as they typically have an energy greater than 1 GeV, they produce continuous ionization across the entire path in the scintillator and typically leave more than 1 MeV of energy deposited in the scintillator.  They also typically traverse the wire chambers at large angles and thus can be identified by their large E.  We estimate a rejection efficiency of > 95%.  Thus, the anticipated background from muons is < 1 x 10-2 Hz and thus will be negligible.

The hadronic component of the cosmic ray background is due to energetic (from a few MeV to more than a hundred MeV) protons and neutrons and has a flux of approximately 1 hadron/cm2/s at LANSCE altitudes.  The protons can be effectively stopped in the shielding surrounding the detector.  The neutrons cannot be effectively shielded.  However, the fast neutrons typically produce energetic recoil protons in the detector.  In general, most of the recoil protons will not escape the scintillator detector and if they do will produce a very high ionization rate in the proportional counters and thus can be very effectively rejected.  The dominant background from cosmic-ray hadrons will be neutron-induced bremmstrahlung.  Since most of this type of background results in very energetic photons, pair production is the most likely form of interaction in the scintillator and it is highly probable that more that one MeV will be deposited in the two detectors at the ends of the spectrometer.  Based on measurements of the gamma flux from cosmic-ray neutrons in shielding materials, we estimate that this type of background will contribute less than 0.02 Hz to the total background.  Again, the background measurements in ER-1 and ER-2 are consistent with such a small cosmogenic background rate.

A8.3.5.	UCN-RELATED BACKGROUNDS

Each time an UCN is lost, it can potentially create a background.  We have carried out Monte Carlo simulations of the UCN losses in the beta decay trap and found that the UCN will either beta decay (about 0.6%), be lost through the walls of the trap due to upscattering (26%), leave back through the inlet UCN guide (12%), or leave the trap through the ends (61%). We have then calculated the average solid angle that the detectors subtend for each type of UCN loss listed above and then use our expected UCN density and fractional loss rates to estimate the backgrounds from each of the loss mechanisms.

We expect about 2 x 105 UCN in the beta decay trap at any given time.  Most of the UCN leave the traps at the ends and are then absorbed in a 6Li-TPX coating on the wall.  The relative gamma yield is only 10-5 in 6Li and thus end losses are not the dominant source of background.

Neutrons that are lost in the walls of the beta decay trap will capture in the spectrometer materials and produce a capture gamma ray with a typical energy of a few MeV.  The average solid angle of the detectors averaged over the full spectrometer is about 4 x 10-4.  Folding in the interaction probability of a capture gamma ray in the scintillator and the coincidence requirement with the proportional counter, we estimate that UCN-related backgrounds will be less than 0.2 Hz in each detector.

A8.4.	EXPECTED BACKGROUND RATE

Using the data from the background measurements we have made and scaling to the scintillator size planned for use in the A experiment (15 cm OD x 0.35 cm thick), we expect a background counting rate in each detector of less than 0.5 Hz from 50 keV to 800 keV using a veto during the proton pulse. This takes into account the coincidence requirement between the scintillator and proportional wire chamber.  It also assumes that the backgrounds will be the same as measured in the test setup.  The dominant background is expected to be due to UCN capture in the spectrometer (0.4 Hz) and beam associated room backgrounds (0.1 Hz).

Figure A8.1.  Background data in the plastic scintillator with no timing cut.  The two dimensional plot of time vs. beta energy is shown in the upper left-hand corner.  The energy spectrum from 20 keV to 1.1 MeV is shown in the upper right-hand corner and the time spectrum from 0 to 50 ms after the proton beam pulse is shown in the lower left-hand corner.

Figure  A8.2.  Background data in the plastic scintillator with a 5 ms timing cut.  The two dimensional plot of time vs. beta energy is shown in the upper left-hand corner.  The energy spectrum from 20 keV to 800 keV is shown in the upper right-hand corner and the time spectrum from 5 to 50 ms after the proton beam pulse is shown in the lower left-hand corner.

APPENDIX 9

EXPECTED COUNT RATES AND STATISTICAL ACCURACY

A9.1.	EXPECTED SIGNAL RATE

We have carried out Monte Carlo calculations of the holding time of UCN in the beta decay trap.  The bottle geometry has a 2-cm ID UCN guide feeding a 10-cm ID trap that is 3 m in total length.  The central 2 m of the bottle is a specular diamond-coated guide and the 0.5 m on each end were diffuse reflectance diamond coated surfaces.  The bottle lifetime was calculated to be 4.7 sec.  We have carried out Monte Carlo calculations of the integrated UCN density in this UCN bottle.  We assume our anticipated production rate of 40,000 fully polarized UCN/s entering into the UCN trap (as was discussed in section A6.3).  This results in a total beta decay rate of 116 Hz.

A9.2	MONTE CARLO OPTIMIZATION OF UCN BETA DECAY TRAP

The expected beta decay rate is calculated directly from the expected steady-state density of UCN in the fiducial volume of the storage trap. The steady-state UCN distribution is determined by integrating the distribution of UCN in the guide/storage system as a function of time following the introduction of a pulse of UCN.  The time history of a UCN pulse can be obtained by tracking each individual UCN in the pulse as it is transported through the system until it is lost either through absorption/up- scattering in the container walls or by escaping through an aperture.  (Since, as will be shown, the storage times in the system are short with respect to the neutron lifetime, it is legitimate to ignore losses due to decay during the transport process.)  A computer program, TRANSIT, has been written to carry out the tracking of the UCN through the system. We report here on a series of TRANSIT simulations used to study the expected beta decay rate for a variety of guide/storage system designs.

The program will track a neutron through an arbitrarily oriented system of intersecting cylindrical, conical or rectangular guides that have specular and/or diffusive reflecting surfaces.  At each contact with a surface, the normal velocity component is compared with the critical velocity (Vc) of the wall material to determine if the conditions for reflection are met.  Accelerated motion, such as gravity, is allowed.  Random choices are used to account for wall losses due to absorption and up-scattering during an otherwise allowed reflection and to pick the direction of reflection in scattering from a diffusive surface.

The basic design of the proposed experiment involves a guide tube feeding UCN from the side into the center of an open-ended cylindrical trap that is surrounded by a solenoid and looked at by charged-particle detectors at each end.  The central section of the trap is a specular reflector to minimize escape back through the input guide and there are diffusively reflecting sections on each end to inhibit escape from the ends of the trap.  For this study the input guide was a horizontal 2-m-long 2-cm ID cylindrical diamond-coated UCN guide.

The cylindrical storage trap was taken to have a diameter of 100 mm and to have a Vc of 7.2 m/s (the estimated value for a diamond coating).  The wall losses were assumed to be 0.0005 per bounce, which is the measured value of the losses observed in the PNPI guides tested at the ILL.  With careful surface preparation and cleaning these loss rates even lower losses should be achievable.  This study looked at traps with total lengths of 3 and 4 meters, different diameters, and with diffusive end-sections of various lengths. The axis of the trap was parallel to the z axis.

The results are shown in Figures A9.1 and A9.2.  Due to a combination of statistical, systematic, and magnetic field considerations, we have settled on a UCN trap that has a total length of 3.0 m, an inner diameter of 10 cm, and diffusive end sections that are 0.5 m in length.

A9.3.	STATISTICAL ACCURACY

In order to achieve a given statistical accuracy , we expect 10) that  = 2.7 / (N.  The factor of 2.7 arises due to averaging over the beta energy spectrum and averaging over +/- 2 solid angle.  If we do not average over the beta energy, but rather measure directly the v/c dependence of the asymmetry, we would require that  = 2.0 / (N.  If we could also reconstruct with perfect accuracy the angular information of each decay, then would require that  = 1.0 / (N.  While we will certainly determine the energy dependence of the asymmetry with roughly 20% accuracy, we will conservatively assume that we do not do this in estimating the number of counts required to reach a given statistical accuracy.  Similarly, while we are investigating the possibility of using TPCs to provide angular information for each decay, we also assume that we will average over +/- 2 in estimating the number of counts required to reach a given statistical accuracy.

In order to achieve a measurement of A/A = 2 x 10-3,  ≈ 2.3 x 10-4.   We assume a total decay rate in the UCN bottle of 116 Hz.  We also assume a total detection efficiency of 98%, a fiducial volume cut of 69%, and a timing cut efficiency of 98%.  After all cuts we expect a count rate of 77 Hz.  To achieve a statistical accuracy of A/A = 2 x 10-3 requires observation of 1.4 x 108 decays, which can be done with 21 days of counting.  We note the important fact that the signal to background is expected to be 220/1.

A9.4.	RUNNING TIME REQUIRED

The LANSCE accelerator is expected to provide beam nine months out of each calendar year.  We are the sole users of beam in Area B and thus we expect to operate the SD2 source nine months every year.  However, as discussed earlier, we cannot run while PRAD is taking beam.  Since PRAD has a substantial amount of setup time, they take beam for only short periods.  We take this into account by allowing 10% of the available time for PRAD running.  We also have down time while the neutron spins are being flipped.  This requires we wait about 10 lifetimes of the UCN beta decay trap in order to allow the wrong spin state to have left the trap so that the total polarization due to residual wrong spin state UCN is < 10-4.  Thus, we must wait about 50 seconds after a spin flip before taking data.  As we expect to make spin flips every 10 minutes, this results in an 8% loss of time associated with spin flipping.  We also assume (based on the projected accelerator performance) an average live time of 90%.  In addition, we assume 10% down time in the experiment itself.  Thus, the effective duty factor in the experiment is estimated to be 67%.  Thus, 21 days of data acquisition corresponds to 1 month of calendar time.

We estimate that approximately 2 months of time will be required in initial operation and debugging.  Given the duty factor discussed above, this corresponds to about three months of data acquisition.  We then plan five months of systematic studies (one month of beam off followed by three months of beam on followed by one month of beam off).  In the third beam cycle, we plan for three months of data acquisition (60 days of actual data).  Thus, we anticipate that the experiment will require 12 calendar months of operation in CY 2002.  This allows a factor of 200% contingency in running time to acquire the required statistics.  With this very conservative schedule, we feel confident we can reach the quoted accuracy within the schedule we have laid out.

This would provide an overall precision (statistical and systematic uncertainties added in quadrature) of  /A = 2.0 x 10-3, an improvement by a factor of four over any existing experiment and thus would allow us to begin to address the important physics issues of the disagreement between the 0+ ( 0+ beta decays and the unitarity of the CKM matrix.  This would certainly have a great impact in the science community, far beyond that of simply determining the value of  and providing a resolution of the current experimental situation.

We note that we have been very conservative in our estimates of beam time required.  We also note that our projected result is statistics limited.  Thus, with either longer running time or more efficient use of the beam time allowed, it may be possible to obtain a final result of  /A < 1.0 x 10-3.  However, in order to be conservative, we base our projected accuracy to be  /A = 2 x 10-3.

Figure A9.1.   UCN retention times for traps of various lengths.

Figure A9.2.  Relative beta decay rates for UCN traps of different diameters and lengths.

APPENDIX 10

CALIBRATION

A10.1.	CONVERSION LINE SOURCES

Full calibration of the energy resolution function of the spectrometer is of paramount importance for a beta asymmetry experiment.  In the previous reactor experiments, this has been done using thin film conversion line sources such as 109Cd  (Ee = 84 keV), 139Ce (Ee = 127 keV), 114In (Ee =  162  keV),  113Sn  (Ee = 364 keV), 85Sr (Ee = 499  keV), and 207Bi (Ee = 481, 975, and 1047 keV).

While we will certainly calibrate the spectrometer using this type of source introduced at the center of the spectrometer, it would be advantageous to have a source which filled the spectrometer active volume in the same manner as the UCN.  We are investigating the possibility of making gaseous sources in which atoms of one of the standard conversion line sources are incorporated into a gaseous molecule.  This would allow us to calibrate the spectrometer over the entire range of beta energies for neutron beta decay in a manner in which the calibration source closely mimics the spatial distribution of the UCN.  However, even if we are unable to make such gaseous sources, an alternative source does in fact exist - several isotopes of Xe decay by internal conversion or by beta decay with energies up to a few hundred keV.  In addition to filling the UCN bottle region fully, such a source is massless and thus does not have the scattering tails typical of conversion line sources deposited on thin films.

The Xe isotopes can be easily produced in mCi quantities in one day of irradiation in a thermal reactor.  It is also possible to obtain isotopic Xe and to irradiate each isotope separately in order to resolve any problems with using multiple sources simultaneously.  The lifetimes of the isotopes are relatively short (a few days to a few weeks), but enough of the Xe isotopes can be produced in a single irradiation to provide a useful source for 1 - 2 months.

The Xe can be introduced into the center of the UCN bottle through a thin fill tube.  The Xe will then flow out of the bottle and be pumped away at the ends of the bottle.  We are investigating the possibility of being able to cool the beta decay trap to LN temperature.  In order to be able to cool the decay trap to LN temperature, we need to demonstrate that the diamond coating will remain bonded to the substrate when cooled.  (There is some limited information in the literature that inidcates this is possible.)  By controlling the temperature of the UCN bottle, we could change the conductance of the UCN guide tube for Xe and thus change the ratio of Xe in the guide tube to that in the field expansion region in order to check systematic effects.  We could also cool the guide tube to liquid nitrogen temperature and thus cryopump the Xe onto the walls of the UCN bottle.  This will allow us to check the fiducial volume of the UCN bottle, as defined by the proportional counters and to study for any betas scattered from the walls being able to make it into the fiducial volume of the spectrometer. We estimate that we can produce rates in the 100-1000 Hz range in the UCN fiducial volume with the Xe.  An additional advantage of the Xe is that it allows us to develop all of the detector systems off-line and thus to be ready for UCN when beam is available.

The isotopes of Xe of interest, their decay mode, the ratio of K conversion electrons to gammas, the half-line, the energy of the electron, and the relative strength of each isotope at 3 and 30 days after irradiation are given in table A10.1.

| Isotope | Decay Mode | k/ | Half-Life | Energy | Relative Strength* |
| --- | --- | --- | --- | --- | --- |
| 125Xe | EC |  | 17 hrs | 33 keV | 0.29/0.00 |
| 127Xe | EC |  | 36.41 days | 33 keV | 0.001/0.03 |
| 129mXe | IT | 6 | 8.89 days | 236 keV | 0.03/0.14 |
| 131mXe | IT | 33 | 11.77 days | 164 keV | 0.04/0.31 |
| 133mXe | IT | 6 | 2.19 days | 233 keV | 1.00/0.007 |
| 133Xe | - |  | 5.25 days | 346 keV | 0.69/1.00 |

Table A10.1.  Decay properties of Xe isotopes produced by irradiation in a reactor.

* Relative strength given for 3/30 days after end of irradiation.  133mXe is taken to have a relative strength of 1.0 for the entry for three days after irradiation.  133Xe is taken to have a relative strength of 1.0 for the entry for thirty days after irradiation.

As discussed above, we are also investigating the possibility of producing gaseous sources with the other conversion line sources listed in the first paragraph of this section.  This would allow us to calibrate the entire energy range of interest with sources that are spatially distributed in a manner similar to that of the UCN.  While it is possible to produce various gases containing the isotopes of interest, some care must be exercised in using these sources in terms of possible contamination of the spectrometer and safety and compatibility concerns of some of the possible molecular forms that might be used.

One interesting possibility is to polarize 133Xe.  The primary beta decay branch of 133Xe is a pure Gamow-Teller transition, thus A for 133Xe = 1.  If is proves feasible to polarize 133Xe and maintain its polarization in the UCN bottle (which may be somewhat difficult due to the quadrupole moment of 133Xe) with polarization relaxation times of order 10 seconds, then we would have a source with a large asymmetry which would allow us to study systematics off-line in determining our sensitivity to various false asymmetry effects.  While we are interesting in pursuing this possibility, at present we assume this will not be possible and thus do not base any of our studies of systematic effects on the availability of an off-line source with a non-zero beta asymmetry.

A10.2.	ACCELERATOR SOURCES

It is also clear that in order to push detector systematic effects down, it will be necessary to fully characterize the detector response using a high-resolution, variable-energy electron source.

We have begun an extensive calibration program in order to test prototype detectors and to allow detailed measurements of detector response for the final experiment.  For the ``high'' energy regime (E > 150 keV)  we are using the 1.5 MV dynamitron accelerator at NASA-JPL (see Figure A10.1).  This electron accelerator is used to study radiation damage in electronic chips and solar cells.  We have demonstrated that the accelerator can be run as low as 150 keV and produce a momentum analyzed beam with only 100 - 1000 particles/sec.  Initial measurements of scintillator detector response have been made under these conditions.

For the low energy regime (E < 150 keV) we have constructed a small electron accelerator at Caltech using spare power supplies and beam line components from the Kellogg Pelletron accelerator.   Following extraction from a W filament and initial focusing, the beam is accelerated and measured with a beam profile monitor and Faraday cup.  Extracted beams of up to 30 keV have been obtained and studies of beam optics and higher energy are underway.

In order to provide an absolute calibration and to allow off-line measurements with momentum analyzed radioactive sources we have constructed a novel iron-free electron spectrometer.  The spectrometer is based on a simple Helmholtz coil geometry that is easy to model and can be carefully mapped.  Based on detailed Monte Carlo studies we have discovered (apparently for the first time) a geometry that allows double focusing using only the field from the Helmholtz coil. Measurements with a 113Sn source have confirmed the focusing properties of the spectrometer and demonstrated a momentum resolution of 0.3%.   This device will be used at JPL in order to calibrate the accelerator/magnetic analysis system to 0.1% (the present calibration is only good to 5%).  We will also couple the spectrometer to the low energy Kellogg accelerator to provide high quality, continuous beams of low energy electrons for detailed measurements of detector response.  It is anticipated that this device will be shipped to LANL for detector calibrations during the beta decay asymmetry measurements.

Thus, using these two electron sources, it is possible to carry out extremely precise calibrations of the detector response from 5 keV to 1 MeV. The electron sources will thus provide us with a continuously variable source with resolution of 1 - 2 keV FWHM, an absolute energy calibration of ( 1 keV, and a corrected linearity of better than 5 x 10-4.

Initial measurements of detector response have already been performed at the JPL dynamitron.  A prototype scintillator detector (15cm x 15 cm) with 4 PMT readout was directly coupled to the vacuum system of the accelerator beamline without any vacuum window (to eliminate energy loss in the window).  In addition a Si surface barrier detector (200 square mm) was placed in the vacuum system on a movable arm to allow placement directly into the beam.  By first tuning the beam on an upstream Faraday cup (at currents of < 1 nA) and then reducing the current on the filament of the electron source, a rate of 1000 – 15,000 Hz of electrons could be directed onto the detectors. Spectra from both the scintillator and Si detector were taken at several electron beam energies.  An example of spectra taken at different energies for the prototype scintillator (silicon detector) are shown in shown in Figure A10.2 (A10.3).  Initial analysis of these data indicate that with careful tuning of the electron beam, low energy components of the electron beam (due to scattering from various apertures) can be significantly reduced.  Our preliminary analysis suggests that, with proper tuning, the measured detector response for both the scintillator and Si detector are consistent with detector backscattering with negligible contributions from the beam.

Figure A10.1.  Schematic view of the electron dynamitron at the JPL that will be used to fully characterize the detector response.

Figure A10.3.  Energy spectra taken with the prototype scintillator using the JPL dymanitron electron accelerator.  The energies are 180, 272, 359, 554, and 862 keV.

Figure A10.3.  Energy spectra taken with a silicon using the JPL dymanitron electron accelerator.  The energies are 862, 554, 445, 359, 272 and 180 keV (in rows starting at the top).  Both linear and logarithmic plots are shown for each energy.

APPENDIX 11

SYSTEMATIC EFFECTS

A11.1.	OVERVIEW

The central issue in accurately determining the beta asymmetry at the percent level and below are the systematic uncertainties associated with this measurement.  They are numerous, and should all be reduced and/or characterized at levels below the 0.1% level.  The angular distribution for neutron beta decay is proportional to 1 + v/c <P> A(E) cos (, where <P> is the average polarization of the neutron, ( is the angle the emitted electron makes with the neutron's polarization vector,  and A(E) is the beta asymmetry as a function of the energy E of the emitted electron.  Thus our task is to determine v/c, <P>, cos (, and the incident electron energy to sufficient precision for each observed decay.  From this information, the value of A(E) can be extracted.

Our strategy adopts various elements from the many previous measurements of the beta asymmetry of the neutron and of 19Ne.  We observe the neutron decays in a strong magnetic field, which serves to provide 4( collection efficiency for the emitted electrons (because they are forced to spiral along the field lines until they strike a detector face-- see figure 4).  The beta asymmetry is then determined by a ratio of the detector signals measured in each detector, with the neutron spin first parallel and then anti-parallel to the magnetic field axis.  Taking, for example,  N1( to be the count rate in detector number 1 with the spin parallel to the magnetic field, the “super-ratio” R can be defined such that:

R = (N1(N2() / (N1(N2().

Ignoring, at present, the contributions to the count rate due to backgrounds, the asymmetry is just given by:

The advantage of this formulation is that this ratio eliminates detector efficiency differences between the two detectors and fluctuations in the neutron density to first order (to levels well below 0.1%).  Another advantage of our geometry is that, if the angle ( is not detected, we formulate the measured asymmetry in terms of the average value of cos((), <cos(>.  This quantity is also extremely well determined for neutrons which decay in large magnetic fields.  Because all electrons are, in principle, detected, the average value of <cos(> is ± 0.5.  In fact, there are subtle effects in the efficiency for beta detection as a function of the angle ( which enter at roughly the 0.1 percent level and must ultimately be taken into account, either through Monte Carlo calculations or measurements of the beta detection efficiency as a function of angle.

The remaining systematic uncertainties can be broadly divided into three categories: those concerning knowledge of the A) neutron polarization and neutron spin dependent effects, B) electron collection, and C) backgrounds.

A11.2.	Neutron polarization

One of primary motivations of our proposed experiment is the tremendous advantage UCN offer in controlling the systematic uncertainties associated with neutron polarization.  This is one of the dominant systematics (unsurprisingly) in current experiments which utilize cold neutron beams polarized by super-mirror guides (for example) to determine the beta asymmetry.  Ultra-cold neutrons can, in principle, be completely polarized simply by passing them through a strong (7 T) solenoidal magnetic field.  The magnetic field interaction ( ( B) provides a potential barrier, permitting only the anti-parallel spin state (the magnetic moment of the neutron is negative) to pass through the solenoid.  The other spin state is reflected with 100 percent confidence.

The effectiveness of this procedure is limited by our ability to eliminate UCNs with energies above the repulsive magnetic potential, since any UCNs with energies greater than the repulsive barrier can pass through the polarizing field regardless of the direction of their spin.  To ensure this is the case, we rely on the fact that any UCN with energy greater than the material potential will not be stored or transported through our guides.  UCNs, however, are reflected from the surface of the wall when the normal  component of their kinetic energy is below the barrier provided by the material potential.  Thus, it is possible for a UCN with energy greater than the material potential to undergo many collisions and never enter the wall and be lost to the experiment.  To ensure the energy cut-off is sharply defined neared the material potential, we have tailored a “ballast” volume which is closely coupled to our superthermal source, and which ensures the UCNs undergo enough collisions with the wall to eliminate any with energies significantly above the material potential. This hard cut-off in the UCN energies then ensures complete polarization after passing through the polarization field.

In the reversed-spin configuration, the degree of polarization is determined by the spin flipper efficiency, which is expected to be ( 99.9%.  As the uncertainty in the polarization in determining the A coefficient applies only to the anisotropic part of the decay (i.e., scales to the value of A), the relative size of the systematic effect due to polarization is equal to the spin flip inefficiency.  Thus, the size of the systematic effect is A/A ( 1 x 10-3.  In principle, we can measure the efficiency of the neutron spin flipper to an accuracy of 10-6 using a set of crossed polarizer / analyzer spin flippers.  In practice, this can be done by closing the shutters at the end of the UCN trap, filling the bottle with the UCN with the spin flipper on, closing the UCN shutter between the spin flipper and the UCN bottle, turning the AFP off, and then opening the shutters between the AFP, polarizer, and UCN detector (with the UCN switch in the detector position).  Since this operation can be done in a few seconds, and the depolarization rate will have been separately measured with an accuracy of at least 10-4, we can measure the spin flipper efficiency to an accuracy of at least 10-4 by this procedure.  Thus, the systematic uncertainty in the polarization is limited by our knowledge of the AFP spin flip efficiency which will be A /A ( 1 x 10-4.

A11.3.	Depolarization

It is assumed here that neutron spin transport will not produce sizable depolarization of the neutrons.  One concern here is that the neutrons will pass through regions of inhomogeneous magnetic field which might depolarize the neutrons.  Because the neutrons move extremely slowly, the magnetic fields change slowly in the neutron rest frame.  In the worst case, very large field gradients exist at the entrance to the decay spectrometer, where UCN spins experience an effective rate rotation of up to roughly ( = 3000 rd/sec due to the motion of the UCN. For a guide field of Hguide = 240 Gauss, this would correspond to a maximum depolarization fraction of ( / ( Hguide ( 6 x 10-4.  Thus, even in the worst case, the depolarization probability is acceptable.  In fact, this worst case scenario is only experienced by a small fraction of the UCN. Our expectations of negligible depolarization due to spin transport are born out in part by related experiments on polarized 19Ne.  In practice, this assumption can be tested by valving off different parts of the UCN transport guides and measuring the depolarization rates using the technique described in section A7.4.  In the worst case, we take A/A < 6 x 10-4 and A /A ( 1 x 10-4.

The largest degree of depolarization due to interaction with surfaces will occur in the UCN bottle where the holding times are about 5 seconds, compared to a time of about 1 second spent in the neutron transport system beyond the polarizer.  As discussed in section A7.4, an upper limit on the depolarization in the UCN bottle (based on the ILL depolarization measurements) is < 7 x 10-4.  We note here as well that depolarization due to collisions with wall surfaces in the presence of large magnetic field gradients is negligible in our experiment, primarily because the field strength is always greater than 100 G 38).

An important feature of the spectrometer design is that we can measure the depolarization in situ, as discussed in section A7.4.  We can measure the depolarization to a level of 1 x 10-4 and thus we take A/A < 7.3 x 10-4 and A /A ( 1 x 10-4.  We can also perform our experiment by permitting the UCNs to flow into our decay solenoid briefly and then shutting off the flow of UCNs.  We can then monitor the beta asymmetry as a function of time while the loaded into the decay volume leak from the spectrometer (UCNs will continue to drain out of the spectrometer with a time constant of roughly 5 seconds).  Any decrease with time in the measured value of the asymmetry will indicate the presence of depolarization.

Combining the depolarization effects from spin transport and the interaction with walls, we assign a value of A/A < 9.4 x 10-4 and A /A ( 1.4 x 10-4.

A11.4.	NEUTRON SPIN ALIGNMENT

Any deviation in the spin alignment does not affect the isotropic part of the decay, but only the anisotropic part.  However, as long as the variation in the field direction is adiabatic (a condition the UCN meet extremely well), it does not matter what the field direction is along the UCN trap as long as we are certain that all of the field lines terminate on the beta detectors at the end of the spectrometer.  Thus, for example, the field direction in the center of the solenoid might be off by some angle .  The neutron spin will be aligned along the direction of .  When an UCN decays, the betas will spiral along the field lines to one end of the spectrometer or the other.  The local value of  determines the direction the betas travel along.  As long as the variation in field direction is sufficiently slow, the betas will adiabatically follow the field lines to the detector.  All decays within + (-) 2 of the local field defined by  will end up with the betas from that field region being detected in the + (-) 2 beta detector.  However this is only true if the axis of the beta detector is aligned with the magnetic field axis of the spectrometer.  If this is not true, then some of the betas emitted during the beta decay of the UCN will miss the detector.  As the isotropic and anisotropic components of the decay fill different phase space (and thus illuminate the detectors differently), misalignment effects may result in different efficiencies for the isotropic and anisotropic parts of the decay.  Aligning the magnetic axis of the solenoid to within 1 mrad of the axis of the detectors puts an upper limit on these effects of A/A ( 1 x 10-4.  Thus, we assign A/A ( 1 x 10-4 and A /A ( 1 x 10-4.

The direction of the guide field could also be affected by stray fields.  However, at the location of the spectrometer, the primary stray field is due to the earth’s magnetic field, which is less than 1 Gauss.  As the solenoid field is 1.0 T, stray fields change  by < 1 x 10-4 and thus are negligible compared to our specified field uniformity.

A11.5.	Variations in THE UCN density

A11.5.1.	SPATIAL VARIATIONS IN THE UCN DENSITY

Our experiment may have very small gradients that exist in the axial UCN density due to differences in the transport time down the different ends of the UCN trap.  We may expect the asymmetry in the UCN density along the UCN trap to most likely be < 2-3%.  As long as the magnetic field is sufficiently uniform, any spatial asymmetry in UCN density within the UCN trap does not lead to any false asymmetry for the beta asymmetry.  However, in the field expansion region, an asymmetry in the UCN density coupled with the magnetic mirror effect could produce a false asymmetry.  In order to mitigate this effect, we will have a 6LiH - TPX coating in the field expansion region to substantially reduce the UCN density in the field expansion region.  In the general, the size of this systematic effect is given by the product of the relative UCN decay rate in the field expansion region, the asymmetry in UCN density, and the size of the magnetic mirroring. The UCN decay rate in the field expansion region is estimated to be at the 2.5 x 10-3 level (see section A7.5.3).  With a field expansion ratio of 0.6, about 22% of the betas (integrated over the field expansion region) will be reflected back by the magnetic mirror effect and be detected in the wrong detector.  This is coupled with the (maximum) 3% asymmetry of the UCN density in the UCN trap.  Thus, this is at most a 1.7 x 10-5 effect and must also be correlated to some asymmetry in the spin flipping (maximum 20% change in phase space density).  We will certainly be able to correct for any difference in the UCN density in the beta decay trap that results from spin flipping by the APF.  However, even if we don't take this into account, the systematic effect is still less than 4 x 10-6.  Thus, this effect is completely negligible and we can certainly assignA/A < 4 x 10-6 and also A /A < 4 x 10-6.

A potential systematic of some concern is that the two spin states are not directed into the decay spectrometer in identical fashion.  For example, after passing through the polarizer the spin state which is anti-parallel to magnetic field is accelerated into the decay spectrometer, whereas the spins which are flipped (in the spin-flipper) are decelerated as they enter the decay spectrometer.  Although the super-ratio protects us (to first order) from rate variations due to slightly different loading efficiencies for the two spin states, more subtle effects can cause a systematic error in the measured value of the asymmetry.  Such a systematic might be connected to a different spatial distribution of the UCNs in the spectrometer for different spin states.  A variation in the detection efficiency across the face of the detectors can then lead to a systematic difference in the detection efficiency for the two spin states, and therefore to a false asymmetry.

This effect requires a conspiracy among several different factors, each of which is small.  Because we have adjusted the final energy of the UCNs to be the same for either spin state, the differences in the spatial distributions for the two spin states will be very small.  Certainly these differences must be smaller than difference in the overall loading efficiency, which is of the order of 20 percent.  This must couple to a variation in detection efficiency for the two spin states.  Given the extremely high overall detection efficiency for our MWPC’s (99.9 percent or higher), a reasonable upper limit on these variations is about 0.5 percent. Thus a characteristic systematic deviation due to this effect might be as big as 1 x 10-3.  We note that we can subdivide, in software, the detector response into a spatial grid of 20 elements and form super-ratios for each element of this array.  The size of this effect can then be reduced by roughly a factor of 20.  Thus we can quote an overall systematic error of the order of  A/A < 5 x 10-5 for this effect and also A /A < 5 x 10-5.

Combining the two effects described above we can assign a value of A/A < 5 x 10-5 and also A /A < 5 x 10-5 for the systematic effect due to spatial variations in the UCN flux

A11.5.2.	TIME VARIATIONS IN THE UCN FLUX

We will also have temporal variations in the UCN density, as the output from the UCN source depends on the stability of the proton beam.  Based on our experience with our present UCN source, the temporal variations on the short term (tens of seconds) is good to 2%.  Furthermore, as the count rates in the spectrometer are low, there are essentially no count-rate dependent effects in the experiment.  All that is important is that we accurately know the number of neutrons in the bottle in each of the spin states.  As only about 6 x 10-3 of the neutrons beta decay in the UCN bottle, and we monitor the number density by counting approximately 10% of the UCN in monitor detectors at each end of the UCN bottle, we can measure the number density in each spin state to an accuracy which is 4 times better than our statistical uncertainty.  We therefore estimate the systematic effect due to temporal variations to be the statistical accuracy of the beta asymmetry measurement divided by four.  We expect to observe 1.6 x 108 decays, thus the uncertainty is 1/(4 x (1.6 x 108 ).  Thus, we take A/A = 2 x 10-5 and also A /A = 2 x 10-5 for the systematic effect due to time variations in the UCN flux.

One of the strengths of our approach is that we plan to measure the UCN fluxes leaving the ends of the observation guide. We will also be able to monitor the total number of protons directed onto our spallation target and UCNs leaving the UCN storage bottle through a short guide to a monitor detector.  These measurements will allow us to study the systematic effect due to time variations by artificially binning the data into high and low rate data sets.  Thus, we will have several on-line monitors for the systematic effect of time variations in the UCN density.

A11.6.	Backscattered betas

An electron which encounters one of the detector faces and then undergoes multiple scattering or scatters at large angles after Coulomb scattering from a nucleus can be ejected from the detector and ultimately deposit detectable amounts of energy in the detector at the opposite end of the observation volume.  These events can largely be reconstructed through the use of timing, but ultimately one must apply a correction for the missed backscatters and for the spectral distortions induced by backscatter.

To deal with this problem, we use a specially modified and extensively tested Monte Carlo simulation code.  This code has been modified to properly deal with scattering in extremely thin foils.  Simulations of similar experimental geometries have produced excellent agreement with measured backscatter spectra and the results of beta asymmetry experiments.  Our ability to test the accuracy of these codes permits us to assign an uncertainty to the magnitude of the missed backscatter correction of about 20 percent.

We have applied this code in a preliminary survey of the backscatter from gas proportional counters and the results are promising.  Here we utilize the fact that we have expanded the field (thereby reducing the magnetic field strength), and thus electron trajectories are essentially parallelized when they enter lower field strength regions (by the same mechanism that produces magnetic "mirroring" when electrons enter higher field strength regions).  This reduction in the relative size of the transverse momentum ensures that the electrons have a high probability of penetrating deeply into the detector material and not backscattering.  In particular, this phenomenon eliminates the grazing incidence trajectories backscatter with extremely high probability.

One aspect of our experiment deserves particular mention with regard to the backscatter.  After the grazing incidence electron trajectories have been eliminated, the backscatter fraction from thin foils can be made very small through the use of low Z materials.  Thus the implementation of a MWPC as the primary detector for establishing the emission direction of the electron provides an additional improvement in the sensitivity of our experiment to the initial emission direction of the electron.

The dE/dx information from the MWPCs provides a powerful diagnostic of backscattering from the scintillators.  With a field expansion ratio of 0.6, all of the betas pass through the MWPC at an angle of ( 51o from normal incidence.  The maximum variation in dE/dx for betas passing through the MWPCs is a factor of 1.6.  If a beta backscatters from the scintillator, then it must drop at least 2 x dE/dxmin, where dE/dxmin is the value of dE/dx for a beta passing through the MWPC at normal incidence.  Of course, in general, the average spread in dE/dx for a beta traversing the MWPC and stopping in the scintillator is only about 1.2 x dEdxmin, and the average dE/dx of a backscattered beta is about 2.4 dE/dxmin.  If a beta backscatters from the scintillator, then either it will be mirrored back into the same scintillator (in which case the average dE/dx is 3.6 dE/dxmin) or be detected in the scintillator at the opposite end of the spectrometer, thus providing a unique signature for backscattering.  However, some of the betas will backscatter from the windows of the detector and the gas in the detector.  Given an expected dE/dx resolution of about 40%, we expect to be able to cleanly identify more than 90% of the betas backscattered from the scintillator.  However, one has to include the effects of backscatter from the MWPC windows, in the gas itself, and the effect of tails on the MWPC resolution function.  Including those factors, we estimate that we can cleanly identify at least 75% of the backscattered events.

The results of the calculations are shown in Fig. A11.1, where the missed backscatter fraction is shown for windows of various foil thicknesses and for different field expansion ratios.  In these calculations, we assume a mylar window with 500 Angstroms of Be evaporated on it (to serve as a ground plane and a reflector for the UCN) and calculate the fraction of backscatters which deposit energy less than the scintillator threshold (assumed to be 20 keV).  The results also include the effect of reflections in the tapered magnetic field which reduces the misidentified backscatter fraction by a factor of 2.8 for a field expansion ratio of Bo/B = 0.6 where B is the field at detector and Bo is the field in the UCN bottle.  We note that our preliminary Monte Carlo calculations of energy deposition in the MWPC indicate that using the MWPC in coincidence with the scintillators should provide further suppression of missed backscattered betas by a factor of 4.

From the results of the Monte Carlo calculations, it is clear that 1) it is desirable to achieve as low a threshold as possible in the scintillators, 2) that a field expansion ratio of 0.6 provides a strong reduction in backscattering while being a reasonable compromise with the solid angle (and therefore fiducial volume and count rate) from the UCN bottle, and 3) that MWPC window thicknesses up to 10 microns are reasonable.

For our geometry, our Monte Carlo simulations indicate that the missed backscatter fractions are at about the 0.2% level or lower (scintillator and field expansion only), consistent with the results of the PERKEO II experiment, which utilized a similar field expansion strategy to suppress backscatter (but without any MWPC).  In addition, we gain a further factor of 4 suppression by including MWPC information, as discussed above.  We note, however, that the missed backscatter fraction will be different for the isotropic and anisotropic components of the electron angular distribution, requiring a simulation of the missed backscatters.  The correction for this effect is, in the worst case, about 50% of the size of the missed backscatter fraction.  Thus, we assign a conservative systematic uncertainty to the missed backscatter fraction of A/A = 1 x 10-3.  As the accuracy of our theoretical description of the magnitude of the backscatter fraction has been demonstrated to be 20%, we assign a systematic uncertainty to backscattering effects of A /A = 2 x 10-4.  We are working to improve our understanding of the ability of the MWPCs to identify backscattering in an effort to further reduce this systematic uncertainty.

A11.7.	SCATTERED BETAS

Betas can be scattered in spectrometer by two mechanisms: interactions with the residual gas and through wall collisions.

The interaction probability for betas in the UCN bottle with the residual gas is less than 1% for a base pressure of 10-6 Torr in the spectrometer.  Most of these interactions are elastic scattering with only a few eV energy transfer.  Less than 10-3 of the betas scatter inelastically (resulting in atomic excitations).  Most of the inelastic collisions with the N2 and O2 residual gas transfer less than 100 eV to the molecules and we estimate less than 5% of the betas suffer energy losses which are greater than 100 eV.  Collisions which result in less than 100 eV of energy loss contribute to a widening of the resolution function of only 5 x 10-5 at 100 keV which has a negligible effect in coupling to any false asymmetry.  Collisions which result in an energy loss of more than 100 eV can be included by adding a very small low-energy tail to the resolution function.   A small fraction, estimated to be < 10-4, of these events can result in the beta being scattering into the opposite direction from which it was emitted.  This effect can create a false asymmetry only by coupling to asymmetries in the detector efficiency for the different neutron spin states, variations in the magnetic field, or an asymmetry in the UCN axial density.  The largest of these effects is a possible asymmetry in the UCN axial density, which is estimated to be < 3%.  Thus, we assign A/A < 3 x 10-6 and A /A < 3 x 10-6.

Betas that originate close to the walls of the UCN bottle can scatter from the walls.  In general, such betas cannot make it to the detector as they will continually strike the walls as they travel along the UCN bottle.  Only by scattering with the residual gas in the bottle can betas that have struck the wall be scattered and transported along the bottle into the detectors.  The same arguments given above apply in this case as well.  In addition, the fiducial volume of the bottle is 69% so that only 31% of the neutrons decay in the region where the betas from the decay can strike the walls.  Thus, the contribution of this effect is a factor of 3 smaller than from betas within the fiducial volume scattering from the residual gas, resulting in A/A < 1 x 10-6 and A /A < 1 x 10-6.

A11.8.	FIELD NONUNIFORMITIES

If field nonuniformities exist, it is possible for betas to be either reflected back into the wrong detector by a step in the field strength along the solenoid or to be trapped within the UCN bottle at the site of a local minimum of the field.

In the first case, we can estimate the size of this effect by noting that the reflection angle R is given by:

sin R = (B/Bo)1/2

where Bo is the maximum field in the UCN trap and B is the field value at which the neutron decay occurs.  For a specified field uniformity of 5 x 10-4, we find that R = 88.7o.  For a step in the magnetic field strength at one end of the solenoid (the worst case), one integrates from 88.7o to 90o and this corresponds to a solid angle for reflection out of 2 of 2.2 x 10-2 for the isotopic part of the decay.  The effect of this reflection on the detection efficiency of the part of the angular distribution of neutrons proportional to the A coefficient (weighted by cos() is only 5 x 10-4.  However, this is the worst possible case, where the field is uniform at the value B throughout the entire UCN trap and then suddenly rises to the value Bo at the end of the UCN trap.  As we can carefully map the magnetic field profile and trim it if needed to avoid such a worst case, an RMS average of the solenoid will give an approximate value to use for the field nonuniformity.  As the solenoidal field should be highly symmetric about the center point of the solenoid, the effect of reflection will be suppressed (only the isotropic part of the flux is affected by reflection, the symmetry ensures neither direction is preferred for the ultimate emission direction of the electron).  Assuming the field is symmetric at the 5% level about the center point of the solenoid and averaging over the UCN density distribution, one finds that the false asymmetry associated with reflections due to magnetic field nonuniformities is A/A ( 1 x 10-4.  We can accurately map out the fields to within 1 Gauss (out of the 1 Tesla field in the solenoid) and thus correct for any possible reflections at the 20% level.  Thus, we assign A/A = 1 x 10-4 and A /A < 2 x 10-5 due to the effect of possible gradients in the magnetic field of the UCN trap solenoid.

In the second case (of trapping of betas in a local field minimum), the trapped betas will scatter from residual gas in the UCN bottle and be ejected from the field trap.  These ejected electrons will be essentially isotropic and will dilute the value derived for A by the same amount as the magnitude of the degree of trapping.  The same arguments as given above apply here except that instead of integrating from 88.7o to 90o as above, one must now integrate the effect from 88.7o to 91.3o as the trapping is symmetric about 90o instead of being a step.  However, this must be weighted by the fact that only the anisotropic part of the decay contributes to this asymmetry.  As the anisotropic part of the decay (determined by the value of A) goes as cos , the false asymmetry generated is weighted by cos  over the trapping solid angle.  Thus, we find that A/A ( 2.0 x 10-5  and A /A ( 4.0 x 10-6 due to the of effect of possible local magnetic field traps of the UCN trap solenoid.

In addition to the above effect of local trapping, there are two other possible effects due to field nonuniformities.  The first is that a longitudinal gradient will affect the phase space distribution of the betas (but not their energy).  As this will change the angle at which the beta strikes the detector, it will affect the backscattering probability.  However, we already employ a large field expansion in order to minimize the effect of backscattering.  As the field expansion ratio we use is 0.6, and the filed uniformity within the UCN trap is specified to be < 5 x 10-4, this effect has an absolutely negligible effect on the systematic associated with backscattering and we neglect it here.

The second effect is that curvature of the field within the UCN trap can lead to drifts of the beta orbits and thus affect the position in which they strike the detector.  One can estimate the size of this drift vD from the formula:

vD = vT  ( / R) (sin2)  [ (R x Bo) / RBo]

where vp is the parallel velocity of the beta, vT is the total beta velocity, r is the radius of the beta track,  is the pitch angle of the beta track,  R is the radius of curvature of the magnetic field lines, and Bo is the average magnetic field.  In the worst case, with electrons moving parallel to the field direction, a specified field uniformity of 5 x 10-4, and the beta traversing the entire 3 m length of the trap, one finds a drift of 0.1 mm.  On the average, the effect is at least 8 times smaller than this.  Since the resultant drift is much smaller than our position resolution, it is a negligible effect and we do not include it in our error budget.

Thus, for the total systematic uncertainty associated with field nonuniformities, obtained by adding the above effects together in quadrature, we assign A/A = 1.0 x 10-4  and A /A ( 2.0 x 10-5.

A11.9.	MAGNETIC MIRROR EFFECT IN THE FIELD EXPANSION REGION

For any neutrons that decay in the field expansion region, some fraction may start off in one direction and be reflected into the other direction by the magnetic mirror effect.  Thus, an electron starting off in one direction may be turned around and first observed in the wrong detector, washing out the true asymmetry.  The estimated total fraction of decays occurring in the field expansion region is expected to be less than 4 x 10-4.  With a field expansion ratio of 0.6, 63% of the betas can be reflected.  As long as the spectrometer is completely symmetric and the UCN density is completely symmetric, this will not generate a false asymmetry, but will only cause a decrease in the overall value determined for A.  Our Monte Carlo calculations indicate that the UCN density asymmetry will be less than 3% and all other asymmetries are expected to be at the per cent level or less.  Thus, we assign the systematic uncertainty of the magnetic mirror effect to be A/A ( 8 x 10-6 and also A /A (  8 x 10-6.

A11.10.	FIDUCIAL VOLUME DEFINITION

The fiducial volume will be determined in the transverse directions using the position information from the multi-wire proportional chambers and in the axial direction by the distance between the edges of the 6LiH-TPX coated walls.  The uncertainty in the axial distance is better than 1 mm in a distance of 300 cm, or 3 x 10-4.  The temporal stability in the UCN density distribution is expected to be better than 1% over a 10 minute period (the time between spin flips).  Thus, A/A < 3 x 10-6 for the longitudinal fiducial volume definition.  For the transverse directions, we expect to achieve a position resolution of 1.0 mm in both the X and Y wire chambers.  Thus, we can define a fiducial volume with a 1.4 mm precision for the radius.  Given a fiducial volume diameter of 8.3 cm (the bottle diameter is 10.0 cm), the uncertainty in the fiducial transverse area is 6.4%.  What contributes to a systematic effect is any temporal variation in the determination of this area.  The detector efficiency is expected to be uniform at the < 1% level across the fiducial volume region cut.  The temporal stability over the period between spin flips (about 10 minutes) is typically better than 2%.  We expect any change in the detector efficiency to be less than 1 x 10-3 during spin flip.  Thus, the uncertainty associated with temporal variations in the detector transverse fiducial area is taken to be < 1.4 x 10-6.  Adding the longitudinal uncertainty to the transverse uncertainty in quadrature then yields an overall uncertainty in the fiducial volume definition of A/A ( 3.3 x 10-6 and also A /A (  3.3 x 10-6.

We note that we will be able to cryopump the Xe isotopes onto the walls of the UCN bottle.  We can then look to see how many betas are observed in the MWPCs at the radius that defines the fiducial volume.  We expect the number of betas to be very small, as most betas emitted from the surface of the UCN bottle will spiral back into it and be lost.  By admitting a few Torr of He gas, about 1% of the betas from the Xe on the wall will scatter in the He gas and then be transported to the MWPCs.  Thus, we will be able to accurately define the fiducial volume using the Xe isotopes for calibration.

A11.11.	DETECTOR INEFFICIENCIES

The multi-wire proportional counters have been measured to have an efficiency of 99.9% and the scintillators are expected to have an efficiency of 99.5% (mostly due to backscattered betas that are not reflected by the magnetic mirror effect).  We can measure the detector efficiencies off line using thin conversion line sources and two MWPCs in front of the scintillator.  Using one of the MWPCs as the trigger, we can then determine the efficiency of the other MWPC and of the scintillator.  We will also carry out this measurement in the spectrometer with the source mounted at the center of the spectrometer and the two MWPC - scintillator system mounted in the field expansion region.  Thus, we will accurately measure the detector efficiencies in situ.  We can determine the MWPC inefficiency to an accuracy of (0.1%)2 = 1 x 10-6 and the scintillator inefficiency to an accuracy of (0.5% x 0.1%) = 5 x 10-6.  Thus, we will have high sensitivity to any variations in detector efficiencies.

The detector efficiency cancels to first order when using the superratio and it is only second order effects due to variations in detector efficiencies with spin flip which affect the result for A.  We expect the detector efficiencies to vary by less than 10-3 during spin flip and for the temporal stability of the detectors to be better than 0.1% between spin flips.  Thus, we take the systematic effect due to detector inefficiencies to be the product of the detector inefficiency and the temporal stability of the detectors to arrive at the systematic uncertainty of A/A ( 5 x 10-6 and also A /A (  5 x 10-6.

A11.12.	DETECTOR RESOLUTION FUNCTION

The detectors will be calibrated offline using the JPL dynamitron and the 150 keV Cal Tech electron source.  We will also calibrate the detectors using both thin conversion line sources inserted at the middle of the UCN bottle as well as with several Xe isotopes that can also be injected at the center of the UCN bottle.  The Xe isotopes offer the advantage of being a massless source with no scattering effects as occur in conversion line sources deposited on thin carbon foils.  The Xe isotopes will fill the UCN bottle uniformly and thus have, to first order, the same distribution as the UCN.  There will be some differences between the Xe and UCN spatial distributions due to gravity effects and differences in the impedance of the UCN bottle for Xe and UCN.  However, both of these effects are small ( at the few per cent level) and can be corrected for at the few per cent level.  We will use the low-energy accelerators to provide a low-intensity electron beam with a well-characterized energy resolution of E/E = 0.3% FWHM, an absolute energy calibration of < 1 keV, and a corrected linearity of better than 3 x 10-4.  With the use of these sources, we anticipate being able to measure the first and second moments of the resolution function to better than 10% of the source widths. We will be also able to map out the scintillator response as a function of position using the MWPC spatial information.  Thus, we expect to be able to measure the pertinent moments of the detector response function to an average accuracy of about 3 x 10-4.  Thus, we assign A/A = 3 x 10-4 and A /A = 3 x 10-4.  We note for comparison that PERKEO II was able to measure the detector response function to 2.3 x 10-3 without being able to use a massless source that filled their decay region in the same manner as the cold neutron beam, without position information from the detector, and without use of a high-resolution, variable energy electron beam.

A11.13.	DETECTOR NONLINEARITY

The detector will be calibrated using thin conversion line sources, Xe isotope sources, and a continuously variable energy electron beam.  We will take great care in selecting the PMTs used with the scintillators in order to ensure a uniform photocathode response.  Also, using position information from the MWPCs, we will be able to correct for any variation across the scintillator.  This will be done using collimated beta sources (and a low-intensity variable energy electron linac to provide calibration data over the entire range of the neutron beta decay spectrum) without any magnetic field present.  The primary limitation on the measured differential nonlinearity will be the corrected linearity of the low-energy electron beam, which we estimate to be good to 3 x 10-4. In order to determine the effect of a nonlinearity in the detectors on the determination of the beta asymmetry, we note that a 1 x 10-2 nonlinearity in the PERKEO II experiment resulted in an effect on A/A of less than 2 x 10-3.  We take the same factor of 5 reduction in determining the effect in our experiment.  We have carried out Monte Carlo simulations in which the detector resolution was varied in a variety of ways.  Our conclusion was that the factor of 5 is reasonable and perhaps even a bit conservative.  Thus, we take A/A = 6 x 10-5 and A /A = 6 x 10-5 for the uncertainties due to detector nonlinearities.

A11.14.		DETECTOR BACKGROUNDS

a)  Room Backgrounds

There are several components of room detector backgrounds: natural room activity, spectrometer, and cosmogenic, as discussed in Appendix A8.3.  These backgrounds will not change with time (at least on a less-than-geological time scale) and can be measured accurately when the accelerator is not running.  We will then be able to determine the shape and fraction that this type of background contributes to our spectrum during running and be able to accurately subtract it.  As long as there is not an asymmetry in the background in the two different UCN spin states, backgrounds do not generate a false asymmetry. The systematic effect on the beta asymmetry experiment is the fractional background rate (background / signal) times the detector asymmetry for the different UCN spin states.  As we expect the detector efficiency to be independent of the UCN spin state at the ( 0.1% level and we expect a signal to room backgrounds of ( 1000/1, the maximum systematic effect is A/A ( 1 x 10-6.  We could directly measure and subtract this type of background (by closing one of the UCN shutters in the guide tubes between the UCN source and the beta asymmetry spectrometer) with an accuracy of at least 10%.  However, we choose the more conservative approach of not making any background subtraction and thus we assign a systematic uncertainty to room backgrounds of A /A ( 1 x 10-6.

b)  Beam-Associated Backgrounds

Beam-associated backgrounds are due primarily to fast neutrons being moderated and captured in the room, thus producing capture gamma rays.  As discussed in Appendix A8.3.1., these backgrounds decay with a time constant of a few milliseconds.  Thus, by analyzing the time dependence of the backgrounds, we can separate these backgrounds from room backgrounds.  From our test measurements, it appears that residual beam associated backgrounds (after imposing a time cut when the proton beam is on target) are likely to be less than 10% of the room-associated backgrounds.  The same arguments apply to beam-associated backgrounds as to the room backgrounds, and thus we assign A/A < 1 x 10-7 systematic effect and A /A < 1 x 10-7 uncertainty to beam-associated backgrounds.

c)  UCN-Related Backgrounds

One of the great strengths of our approach is that the backgrounds in our beta detectors due to UCNs will be extremely small.  Thus, our “beam-generated” backgrounds will be greatly reduced compared to cold neutron beam experiments.

UCN-related backgrounds are due to the upscattering losses of UCN and subsequent capture on materials in the spectrometer resulting in capture gamma rays that produce a background.  As discussed in section 8.3.5., we expect the UCN-related background to be at roughly the same level as room backgrounds.  We can separate the UCN-related background from the room background by varying the temperature of the UCN bottle.  As the upscattering rate is quite temperature dependent, we can vary the loss rate on the walls of the UCN bottle from almost 0% to about 30%.  Any background that is UCN-related will change with the temperature of the UCN bottle allowing us to distinguish it from room background.  Again, the same arguments apply to UCN-related backgrounds as to the room backgrounds, and with a signal to UCN-related backgrounds of 250/1, we assign A/A < 4 x 10-6 systematic effect withA /A ( 4 x 10-6 uncertainty to UCN-related backgrounds.

A11.15.	SUMMARY OF SYSTEMATIC UNCERTAINTIES

| Systematic Effect | A/A | A /A |
| --- | --- | --- |
| Polarization (including neutron spin flipping) | ( 1 x 10-3 | ( 1 x 10-4 |
| Depolarization | < 9 x 10-4 | ( 1 x 10-4 |
| Spatial variations in UCN density | < 5 x 10-5 | < 5 x 10-5 |
| Temporal variations in UCN density | 2 x 10-5 | 2 x 10-5 |
| Neutron spin alignment | 1 x 10-4 | 1 x 10-4 |
| Subtotal UCN Systematic Effects | 1.4 x 10-3 | 2.1 x 10-4 |
| Backscattered betas | 1 x 10-3 | ( 2 x 10-4 |
| Scattered betas - residual gas contribution | < 1 x 10-5 | < 1 x 10-5 |
| Scattered betas - wall contribution | < 3 x 10-6 | < 3 x 10-6 |
| Field nonuniformities | 1 x 10-4 | 2 x 10-5 |
| Magnetic mirror effect | < 8 x 10-6 | < 8 x 10-6 |
| Fiducial volume definition | < 3 x 10-6 | < 3 x 10-6 |
| Subtotal Electron Collection | 1.0 x 10-3 | 2.0 x 10-4 |
| Detector inefficiencies | < 5 x 10-6 | < 5 x 10-6 |
| Detector resolution function | 3 x 10-4 | 3 x 10-4 |
| Detector nonlinearity | 6 x 10-5 | 6 x 10-5 |
| Detector backgrounds - room | ( 1 x 10-6 | ( 1 x 10-6 |
| Detector backgrounds - beam associated | < 1 x 10-7 | < 1 x 10-7 |
| Detector backgrounds - UCN related | < 4 x 10-6 | < 4 x 10-6 |
| Subtotal Detector Effects | 3.0 x 10-4 | 3.0 x 10-4 |
| TOTAL | 1.7 x 10-3 | 4.2 x 10-4 |

Table A11.1.  Systematic effects and uncertainties.  A is the absolute size of the systematic effect (i.e., size of the effect relative to an asymmetry of 1.0) and A is the absolute size of the systematic uncertainty.  The relative uncertainty in A is A / (A( ( 9.1 A.

The uncertainty in each of the systematic effects discussed in the previous sections is given in Table A11.1.  Table A11.1 quotes both the total size of the systematic effect and the uncertainty assigned to it.  The final total systematic uncertainty in the beta asymmetry experiment is determined by adding all of the individual systematic uncertainties in quadrature.  Thus, we expect that the total systematic uncertainty in the beta asymmetry measurement will be A /A  ( 4.2 x 10-4.  Just as important, we note that the total corrections which must be applied in the beta asymmetry experiment due to systematic effects is A/A ( 1.7 x 10-3.  For comparison, the total systematic absolute uncertainty in PERKEO II was A /A = 6 x 10-3. Thus, even if we did not make any corrections at all for systematic effects, our systematic uncertainty would still be substantially better than that quoted by the best experiment to date.

While many of the systematic uncertainties must be carefully studied by Monte Carlo simulations, we do not expect the total systematic uncertainty to increase significantly over that given in Table A11.1.  Thus, we anticipate being able to measure the beta asymmetry with UCN in which 1) the total systematic effect (without any corrections) is 3 times less than the total corrected systematic uncertainty quoted in the best (Perkeo II) reactor measurement, and 2) a systematic uncertainty that is about a factor of 15 below that achieved in any previous experiment.

A11.16.	DATA ANALYSIS

We plan to carry out full Monte Carlo simulations of the entire experiment and to benchmark those simulations with extensive measurements both off-line and on-line.  This will include accurate measurements of the detector systems, measurements of backscattering, polarization and depolarization, and of the entire list of systematic uncertainties discussed in the previous sections.

We also note that the collaboration has extensive experience in precision measurements of beta decay, including measurements of tritium beta decay, 19Ne beta decay, and neutron beta decay (EMIT - a search for time-reversal violation in  polarized neutron beta decay - and measurements of the neutron lifetime and of the B correlation in polarized neutron beta decay).  Thus, a great deal of work has already been done and a number of the algorithms and computer codes for analyzing neutron beta decay and simulations of false asymmetries are in place.

We plan to construct a detailed, complete model of our experiment.  With this tool in place, we will have one of the critical elements required to produce a realistic assessment of the systematic uncertainties in our measurements.  Our Monte Carlo simulations of the experiment will be carefully benchmarked by taking data in modes in which large false asymmetries are generated (for example by introducing gradient fields in the spectrometer solenoid).

Figure A11.1.  Calculated backscatter percentage as a function of foil thickness and field expansion ratio B/Bo for values of B/Bo of 0.9, 0.8, 0.7, and 0.6.

APPENDIX 12

CALCULATION OF UPSCATTERING RATE IN PARA DEUTERIUM

APPENDIX 13

##### A13.1.  DETAILED COST ESTIMATE:  SD2 SOURCE

|  |  | Origin of |  |  |  |  | From | To LANL |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | Estimate | Quantity | Unit Cost | Total Cost |  | Collaboration | From DOE |
| Line B |  |  |  |  |  |  |  |  |
|  | Beam Line Components | E | 1 | 12 | 12 |  |  | 12 |
|  | Shielding for maze | E | 1 | 8 | 8 |  |  | 8 |
|  | Vacuum instrumentation | C | 3 | 2.5 | 7.5 |  |  | 7.5 |
|  | Line B commissioning | E | 1 | 36.7 | 36.7 |  |  | 36.7 |
|  | Subtotal |  |  |  | 64.2 |  | 0 | 64.2 |
| Area B Cave |  |  |  |  |  |  |  |  |
|  | Removal/disposal of equipment from cave | E | 1 | 19.2 | 19.2 |  |  | 19.2 |
|  | Coring of Roof/Shield Walls | Q | 1 | 12 | 12 |  |  | 12 |
|  | Additional Shielding | E | 1 | 20 | 20 |  |  | 20 |
|  | Subtotal |  |  |  | 51.2 |  | 0 | 51.2 |
| SD2 Source |  |  |  |  |  |  |  |  |
|  | Tungsten target | E | 1 | 7 | 7 |  |  | 7 |
|  | Tungsten removal system | E | 1 | 15 | 15 |  |  | 15 |
|  | Carbon beam dump | E | 1 | 20 | 20 |  |  | 20 |
|  | Cooling Water System | Q | 1 | 38 | 38 |  |  | 38 |
|  | Be Reflectors | A | 1 | 6 | 6 |  |  | 6 |
|  | Water system installation | E | 1 | 12.8 | 12.8 |  |  | 12.8 |
|  | PSS controls | E | 1 | 18 | 18 |  |  | 18 |
|  | Subtotal |  |  |  | 116.8 |  | 0 | 116.8 |
| SD2 Moderators |  |  |  |  |  |  |  |  |
|  | Vacuum Chambers | E | 1 | 8 | 8 |  |  | 8 |
|  | LHe Systems | E | 1 | 9 | 9 |  |  | 9 |
|  | Poly moderator | E | 1 | 4 | 4 |  |  | 4 |
|  | Be reflectors | E | 1 | 33 | 33 |  | 20 | 13 |
|  | LN Systems | E | 1 | 20 | 20 |  |  | 20 |
|  | Vacuum pumps/Instrumentation | A | 1 | 19.3 | 19.3 |  | 19.3 |  |
|  | Remote monitoring | E | 1 | 8 | 8 |  |  | 8 |
|  | Guide tube | Q | 1 | 10 | 10 |  |  | 10 |
|  | Subtotal |  |  |  | 111.3 |  | 39.3 | 72 |
| UCN Storage Bottle |  |  |  |  |  |  |  |  |
|  | Vacuum chamber | E | 1 | 8 | 8 |  |  | 8 |
|  | UCN Bottle | E | 1 | 13 | 13 |  |  | 13 |
|  | UCN Valves | Q | 3 | 6 | 18 |  |  | 18 |
|  | Vacuum Pumps | A | 1 | 19.3 | 19.3 |  | 19.3 |  |
|  | Vacuum hardware | E | 1 | 8.8 | 8.8 |  |  | 8.8 |
|  | Pumping port guide tube | Q | 3.3 | 3 | 9.9 |  |  | 9.9 |
|  | Subtotal |  |  |  | 77 |  | 19.3 | 57.7 |
| UCN Guide |  |  |  |  |  |  |  |  |
|  | UCN Transport Guides | Q | 8 | 2.5 | 20 |  |  | 20 |
|  | Vacuum Chamber/Components | E | 1 | 11 | 11 |  |  | 11 |
|  | UCN switches | Q | 2 | 12.5 | 25 |  | 12.5 | 12.5 |
|  | UCN Valves | Q | 3 | 6 | 18 |  | 6 | 12 |
|  | Vacuum components | E | 1 | 4 | 4 |  |  | 4 |
|  | Remote handling | E | 1 | 25 | 25 |  |  | 25 |
|  | Subtotal |  |  |  | 103 |  | 18.5 | 84.5 |
|  |  |  |  |  |  |  | Cost to | Cost to DOE |
|  |  |  |  |  |  |  | Collaboration | To LANL |
| Subtotal |  |  |  |  | 523.5 |  | 77.1 | 446.4 |
| Contingency |  | Estimated |  | 20% |  |  |  | 62.7 |
|  |  | Quote/Catalog |  | 10% |  |  |  | 15.3 |
|  |  | Total |  | 17% |  |  |  | 78.0 |
| Subotal w Contingency |  |  |  |  |  |  | 77.1 | 524.4 |
| MAT Tax |  |  |  | 3.25% |  |  |  | 17.0 |
| G&A Taxes |  |  |  | 31% |  |  |  | 167.9 |
| Total Cost to DOE |  |  |  |  |  |  |  | 709.3 |
| Origin of Estimate: A = Actual cost of existing equipment, C = catalog, E = estimate, Q = quote |  |  |  |  |  |  |  |  |

A13.2.  DETAILED COST ESTIMATE:  BETA ASYMMETRY EXPERIMENT

|  |  | Origin of | Quantity | Unit Cost | Total Cost |  | From | To LANL | To Princeton | To CalTech |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | Estimate |  |  |  |  | Collaboration | From DOE | From NSF | From NSF |
| Superconducting Solenoid |  |  |  |  |  |  |  |  |  |  |
|  | Solenoid w pwr supply | Q | 1 | 450.0 | 450.0 |  |  |  |  | 450.0 |
|  | Installation | E | 1 | 2.0 | 2.0 |  |  |  |  | 2.0 |
|  | Three-axis Magnetometer | C | 1 | 10.0 | 10.0 |  |  |  |  | 10.0 |
|  | Field mapping system | E | 1 | 5.0 | 5.0 |  |  |  |  | 5.0 |
|  | Subtotal |  |  |  | 467.0 |  | 0.0 | 0.0 | 0.0 | 467.0 |
| Resistive Coils |  |  |  |  |  |  |  |  |  |  |
|  | Resistive Coils | E | 2 | 4.5 | 9.0 |  |  |  |  | 9.0 |
|  | Main power supply | A | 1 | 15.0 | 15.0 |  | 15.0 |  |  |  |
|  | Resistive Coil Cooling System | C | 1 | 16.0 | 16.0 |  |  |  |  | 16.0 |
|  | Computer Control and Interface | E | 1 | 5.0 | 5.0 |  |  |  |  | 5.0 |
|  | Support Structures | E | 1 | 3.0 | 3.0 |  |  |  |  | 3.0 |
|  | Subtotal |  |  |  | 48.0 |  | 15.0 | 0.0 | 0.0 | 33.0 |
| AFP/Polarizer |  |  |  |  |  |  |  |  |  |  |
|  | Superconducting Solenoid | A | 1 | 155.0 | 155.0 |  |  |  | 155.0 |  |
|  | RF Amplifier | A | 1 | 8.6 | 8.6 |  | 8.6 |  |  |  |
|  | RF Equipment | A | 1 | 10.2 | 10.2 |  | 10.2 |  |  |  |
|  | Magnetometer | C | 1 | 1.5 | 1.5 |  | 1.5 |  |  |  |
|  | Computer interface | C | 1 | 1.9 | 1.9 |  | 1.9 |  |  |  |
|  | Subtotal |  |  |  | 177.2 |  | 22.2 | 0.0 | 155.0 | 0.0 |
| UCN Beta Decay Trap |  |  |  |  |  |  |  |  |  |  |
|  | UCN Polarizing Guides | E | 6 | 2.5 | 15.0 |  |  | 15.0 |  |  |
|  | Guide Fabrication Tooling | E | 1 | 14.3 | 14.3 |  |  | 14.3 |  |  |
|  | UCN decay tube (diamond coated) | E | 3 | 1.2 | 3.6 |  |  | 3.6 |  |  |
|  | Cooling | E | 1 | 6.5 | 6.5 |  |  | 6.5 |  |  |
|  | Temperature monitoring | C | 1 | 1.8 | 1.8 |  |  | 1.8 |  |  |
|  | Supports | E | 1 | 0.8 | 0.8 |  |  | 0.8 |  |  |
|  | Vacuum chamber | E | 1 | 8.3 | 8.3 |  |  | 8.3 |  |  |
|  | UCN Shutters | E | 2 | 2.4 | 4.8 |  |  | 4.8 |  |  |
|  | Pb/6LiH shielding | E | 2 | 2.3 | 4.6 |  |  | 4.6 |  |  |
|  | Subtotal |  |  |  | 59.7 |  | 0.0 | 59.7 | 0.0 | 0.0 |
| Vacuum systems |  |  |  |  |  |  |  |  |  |  |
|  | Pumps | Q | 2 | 16.9 | 33.8 |  | 33.8 |  |  |  |
|  | Ion gauge/TC controllers | Q | 2 | 2.4 | 4.9 |  | 4.9 |  |  |  |
|  | Valves | C | 2 | 3.2 | 6.4 |  | 6.4 |  |  |  |
|  | Vacuum Hardware | E | 2 | 1.3 | 2.5 |  | 2.5 |  |  |  |
|  | Subtotal |  |  |  | 47.5 |  | 47.5 | 0.0 | 0.0 | 0.0 |
| UCN detectors |  |  |  |  |  |  |  |  |  |  |
|  | 3He Detectors | A | 4 | 7.0 | 28.0 |  | 28.0 |  |  |  |
|  | 6LiF Detectors | E | 8 | 5.8 | 46.4 |  | 46.4 |  |  |  |
|  | Section Total |  |  |  | 74.4 |  | 74.4 | 0.0 | 0.0 | 0.0 |
| Beta detectors |  |  |  |  |  |  |  |  |  |  |
|  | Prototypes | A | 1 | 9.0 | 9.0 |  | 9.0 |  |  |  |
|  | Scintillators/Wire Chambers | E | 2 | 17.5 | 35.0 |  | 35.0 |  |  |  |
|  | Scintillators/Wire Chambers Electronics | E | 2 | 35.0 | 70.0 |  | 70.0 |  |  |  |
|  | Si Microstrip Detector | E | 2 | 30.0 | 60.0 |  | 60.0 |  |  |  |
|  | Si Microstrip Electronics | E | 2 | 15.0 | 30.0 |  | 30.0 |  |  |  |
|  | Subtotal |  |  |  | 204.0 |  | 204.0 | 0.0 | 0.0 | 0.0 |
| Shielding |  |  |  |  |  |  |  |  |  |  |
|  | Wax containers | E | 16 | 0.3 | 4.0 |  |  | 4.0 |  |  |
|  | Borated wax | Q | 1 | 9.5 | 9.5 |  |  | 9.5 |  |  |
|  | Subtotal |  |  |  | 13.5 |  | 0.0 | 13.5 | 0.0 | 0.0 |
| Enclosure |  |  |  |  |  |  |  |  |  |  |
|  | Climate control/HEPA Filters | E | 1 | 4.7 | 4.7 |  |  | 4.7 |  |  |
|  | Electrical/IPSS | E | 1 | 2.5 | 2.5 |  |  | 2.5 |  |  |
|  | Subtotal |  |  |  | 7.2 |  | 0.0 | 7.2 | 0.0 | 0.0 |
| Calibration |  |  |  |  |  |  |  |  |  |  |
|  | Spectrometer | A | 1 | 40.0 | 40.0 |  | 40.0 |  |  |  |
|  | 130 kV Power Supply | E | 1 | 3.0 | 3.0 |  |  |  |  | 3.0 |
|  | Fiber Optics Control System | E | 1 | 12.0 | 12.0 |  |  |  |  | 12.0 |
|  | Subtotal |  |  |  | 55.0 |  | 40.0 | 0.0 | 0.0 | 15.0 |
|  |  |  |  |  |  |  | Cost to | Cost to DOE | Cost to NSF | Cost To NSF |
|  |  |  |  |  |  |  | Collaboration | To LANL | To Princeton | To CalTech |
| Subtotal |  |  |  |  |  |  | 403.1 | 80.4 | 155.0 | 515.0 |
| Contingency |  | Estimated | 20% |  |  |  | 30.0 | 13.8 | 0.0 | 10.0 |
|  |  | Quote/Catalog | 10% |  |  |  |  | 1.1 | 0.0 | 0.0 |
|  |  | Total DOE | 19% |  |  |  |  | 15.0 |  |  |
|  |  | Total NSF* | 15% |  |  |  |  |  | 0.0 | 10.0 |
| Subtotal w Contingency |  |  |  |  |  |  | 433.1 | 95.4 | 155.0 | 525.0 |
| MAT Tax |  |  | 3.25% |  |  |  |  | 3.1 |  |  |
| G&A Taxes |  |  | 31% |  |  |  |  | 30.5 |  |  |
| TOTAL |  |  |  |  |  |  | 433.1 | 129.0 | 155.0 | 525.0 |
| TOTAL COST OF EXPERIMENT |  | 1193 |  |  |  |  | Cost to | Cost to DOE | Cost to NSF | Cost To NSF |
|  |  |  |  |  |  |  | Collaboration | To LANL | To Princeton | To CalTech |
| Origin of Estimate: A = Actual cost of existing equipment, C = catalog, E = estimate, Q = quote |  |  |  |  |  |  |  |  |  |  |
| * Contingency on superconducting solenoid already included in quoted price |  |  |  |  |  |  |  |  |  |  |

APPENDIX 14

  - UCN SOLID DEUTERIUM SOURCE SCHEDULE

14.2.	BETA ASYMMETRY SCHEDULE

APPENDIX 15

OTHER POSSIBLE FUTURE EXPERIMENTS

While this proposal has dealt specifically with a beta asymmetry measurement, we certainly plan to carry out other neutron beta decay experiments using a modified spectrometer.  Specifically, by incorporating the ability to detect the recoil protons into the spectrometer, we will be able to directly measure the electron-neutrino (a) and neutron spin-neutrino (B) angular correlations.  Precision measurements of these quantities would allow us to make, in combination with our measurement of the beta asymmetry, a search for new Physics Beyond the Standard Model with a sensitivity far better than presently possible.  While we have not yet studied the systematic effects in either the a or B correlation experiments, scaling from our estimates of the systematics in the beta asymmetry experiment, we believe that measurements of the a and B correlations could be made with improvement in the accuracies by a factor of 5 or more.

The recoil protons can be detected by accelerating them to about 35 keV through a thin entrance window of a Multi-Step Avalanche Counters (MSACs). 47-48)  These are counters in which the E / p (electric field to pressure) ratio is so high that multiplication occurs in the gas throughout the volume of the detector.  In a 30 g/cm2 thick entrance window, a 35 keV recoil proton will lose about 30 keV of energy, thus leaving 5 keV to be deposited in the gas of the MWPC.  As such low energy protons are very highly ionizing, they stop in a few Torr-cm of gas.  Thus, recoil protons are characterized by a 5 keV signal in the MSAC.  By comparison, electrons typically leave less than 30 eV in the MSAC.  In addition, the stopping power for X-rays in a few Torr-cm of a hydrocarbon gas is very low.  Thus, a very high signal to background ratio can be achieved for the recoil protons.

The challenge in recoil proton detection with a MSAC is the entrance window.  It must be thin, impervious to gas leakage, able to hold at least 10 Torr of gas, and be able to be cycled reliably.  Such a window can be constructed out of parylene (manufactured by DuPont).  We have developed and tested a process to make these windows.  First, a thick layer (a few mg/cm2) of polyvinyl alcohol (PVA) is deposited on an aluminum mandrel.  A layer of parylene is then deposited on the PVA substrate by vapor deposition.  The parylene is in the form of a powder which is placed in a vacuum chamber and heated in a crucible to a few hundred C.  The parylene forms a vapor with a pressure of a few Torr that coats the PVA surface quite uniformly.  The mandrel is then removed and immersed in water.  The PVA is water soluble and dissolves leaving only the thin parylene film.  The film can be removed from the water and then mounted on the MSAC window frame.  In order to hold a pressure of a few Torr, the window must be supported by a wire mesh.  We have constructed windows of parylene with a thickness of 40 g/cm2 and a diameter of 5 cm using a thin (95% transmission) Ni mesh with 5 mm spacing for support.  This window was cycled numerous times to 20 Torr.  Parylene is quite inelastic and the window showed slight permanent bowing between the wire mesh.  However, this should not substantially affect detector performance.

Thus, it appears possible to construct MSACs capable of detecting recoil protons with a very high signal to noise.  These MSACs would be mounted directly in front of the MWPCs providing the ability to detect both the recoil protons and betas with high efficiency over 2 x 2 solid angle.

While constructing the beta asymmetry experiment, we also plan to work on the development of MSACs for recoil proton detection.  We would anticipate installing these counters in the spectrometer following completion of the beta asymmetry experiment to start a and B correlation experiments.

We also plan to investigate the possibility of using Time Projection Chambers (TPCs) for tracking of the betas.  Calculations indicate it should be possible to construct TPCs with a spatial resolution of about 1 mm for low energy betas.  It would then be possible to track in three dimensions the betas from neutron beta decay.  By placing the TPC in a strong magnetic field (such as exists in the field expansion region of the beta asymmetry spectrometer) it would be possible to measure the radius of curvature of the tracks.  Calculations indicate that, including the contributions to position resolution from multiple scattering in the gas and from the intrinsic detector resolution, one should be able to determine the radius of curvature, and thus the momentum of the beta, to better than 5% accuracy. for betas with energies greater than 100 keV.  If this should prove possible, it would represent a significant improvement in the beta energy resolution over that possible with a scintillator.  Just as important, the tracking information would provide directly the emission angle of the beta with an angular resolution of a few degrees.  This would provide two additional benefits:  1)  instead of averaging over the 2 solid angle (with its resultant loss of sensitivity of a factor of 2), one could directly fit the entire cos distribution, and 2)  the increased ability to study systematic effects in detail. In addition, the statistical power of the data would increase, as the factor of 2.7 reduction in statistical significance (see section A9.3) would go to unity if we could reconstruct the angular information in the decay with perfect precision.  Thus, with a TPC it may prove possible to further improve the precision of the beta asymmetry measurement, even without any increase in UCN flux.  Ultimately, we plan to carry out a measurement of weak magnetism which requires high statistical and systematic precision.  A weak magnetism measurement would certainly benefit from the improved statistical and systematic measurements that a TPC might provide.

We also will investigate the possibility of using large diameter Si(Li) detectors which would provide and energy resolution of a few keV.  The advantages of improved energy resolution would improve our ability to make a precision measurement of the neutron beta decay spectrum.  This would allow us to extract weak magnetism in polarized neutron beta decay and the Fierz interference term (b) in unpolarized neutron beta decay.  However, this must be balanced against the larger systematic effects due to increased backscattering from Si.  Our first measurement of the beta asymmetry will allow us to address the issue of backscattering in great detail.  Thus, following our first beta asymmetry measurement we expect to be able to accurately assess the benefits to be gained by going to Si(Li) detectors.  In addition, by implementing either optical or x-ray detectors in coincidence with Si(Li) or scintillator detectors, we would be able to make a measurement of the radiative decay of the neutron.  This has never before been observed and is important in understanding the radiative corrections to neutron beta decay when we ultimately push down to the 10-4 level of sensitivity.

It is also possible that other approaches to measurements of polarized neutron beta decay may ultimately lead to higher accuracies.  Experiments in which the UCN fall in the gravitational field, forming a UCN beam would offer the advantages that the UCN would never touch a solid surface after passing through a polarizer (thus ensuring identically 100% polarization) and pass only once through an AFP spin flipper.  Such a system could also employ a low holding field to maintain the polarization, and with use of tracking chambers for the betas and position sensitive proton detectors, it might be possible to fully reconstruct the decays.  Other possible systems might employ magnetic spectrometers to accurately measure the beta spectrum shape or electrostatic spectrometers to accurately measure the recoil proton shape.  Such systems might be used in measurements of the time-reversal-violating triple correlation coefficient D.

Finally, UCN seem to provide the best hope for an improved measurement of the neutron lifetime.  We are currently discussing with Prof. Serebrov’s group possibilities for a neutron lifetime measurement using UCN that would have an accuracy of ( 0.1 seconds, an improvement by a factor of 10 over existing measurements.

A SD2 UCN source would have sufficient UCN density and total UCN production rate to accommodate several experiments simultaneously.  Thus, one can envision being able to develop different approaches to measurements of UCN beta decay at the same time that other measurements are taking data.  Thus, we envision a broad research program in fundamental neutron physics being carried out at a SD2 UCN facility.

In conclusion, we plan to continue to develop a program in UCN beta decay that will carry on well past the conclusion of the beta asymmetry experiment.  Several of the experiments in this program would use a modified version of the beta asymmetry spectrometer.  With improved detectors  (MSACs, and possibly TPCs and Si(Li) detectors) and the increased count rates with a future UCN source, we expect to carry out a set of precision measurements of a, b, A, B, radiative decya, the neutron lifetime, and weak magnetism.  We believe it should be feasible to carry out these measurements to search for new Physics Beyond the Standard Model with a sensitivity which is the best in the world.

APPENDIX 16

COLLABORATION RESPONSIBILITIES

The collaboration has a great deal of diverse capabilities and experience which provides a very strong base to carry out the beta asymmetry experiment.  The general division of responsibilities between the institutions has been agreed upon and is briefly described here, along with a brief description of expertise.  The responsibilities listed for each institution are in order of primary area(s) of responsibility (underlined) followed by secondary responsibilities.  All institutions will participate to varying degrees in running the experiment and analyzing data, therefore those responsibilities are common and not broken out by institution.  The manpower at each institution dedicated to this experiment is also listed - in some cases (such as postdocs and students) we anticipate new hires to fill currently open positions.

###### California Institute of Technology

Expertise:  Detector development and deployment, parity violation experiments, optically polarized 	3He targets, cryogenic hydrogen and deuterium targets

Manpower:  3 faculty, 3 postdocs, 1 student, 1 technician - 4.5 FTE

Responsibilities:  Detector development and construction, detector calibration, solenoid construction, Monte Carlo simulations of detector response, development of SD2 source

Institute Laue-Langevin

Expertise:   UCN experiments

Manpower:  1 Scientific staff member, 0.1 FTE

Responsibilities:  Characterization of materials for use in coating the UCN guides and bottle, UCN tests of equipment

Japan Atomic Energy Research Institute

Expertise:  Multilayer neutron mirrors

Manpower:  1 Faculty - 0.1 FTE

Responsibilities:  Multilayer supermirror for SD2 source

Los Alamos National Laboratory

Expertise:  Nuclear beta decay, low-level counting, UCN sources, radioactive source preparation, 	detector systems, data acquisition

Manpower:  10 Staff members, 3 postdocs, 3 technicians - 5.5 FTEs

Responsibilities:  SD2 source, development of SD2 source, UCN beta decay trap mechanical systems, total systems integration, controls and monitoring data acquisition, 3He UCN detectors, vacuum systems, depolarization measurements of materials, beta detectors,

Petersburg Nuclear Physics Institute

Expertise:  UCN experiments

Manpower: 3 Faculty, 5 engineers, 1 technician - 2.5 FTE

Responsibilities:  58Ni-coated stainless steel guides, development of SD2 source, depolarization measurements of materials

Princeton University/University of North Carolina

Expertise:  Nuclear beta decay, polarized targets

Manpower:  1 Faculty, 1 postdoc, 2 students, 1 technician - 4.0 FTEs

Responsibilities:  UCN polarization and spin flipping, solenoid design, depolarization measurements, development of SD2 source, prototype detectors, Monte Carlo simulations of detector response

Tohoku University

Expertise:  UCN detectors, UCN transport analysis, elementary and fundamental physics

Manpower:  1 Faculty - 0.1 FTEs

Responsibilities:  UCN detectors

University of Kyoto

Expertise:  UCN experiments, UCN source development, cryogenics, neutron polarization

Manpower:  3 Faculty - 0.6 FTEs

Responsibilities:  Cryogenic design, UCN source tube, development of SD2 source, UCN polarization studies

University of Tokyo

Expertise:  Si(Li) detector development

Manpower:  1 Faculty - 0.1 FTEs

Responsibilities:  Fabrication of Si(Li) detectors

Virginia Polytechnic and State University

Expertise:  Symmetry experiments, data acquisition, UCN guides

Manpower:  2 faculty, 1 student - 1.3 FTEs

Responsibilities: UCN guides, bottle, and beta decay trap, beta detector data acquisition,

TOTAL MANPOWER:  19.7 FTES

APPENDIX 17

BRIEF BIOGRAPHIES OF THE COLLABORATION MEMBERS

Alduschenkov,  Alexei - Petersburg Nuclear Physics Institute:

Education: Ph.D., Physics -Petersburg Nuclear Physics Institute (1979);  Senior scientist - Physical Faculty,  Diploma in Physics- Leningrad University (1966).

Research:  Polarized cold neutrons, precision measurements of neutron polarization, neutron beta decay experiments.

Asahi, Koichiro - Tokyo Institute of Technology:

Education: Associate Prof. - Tokyo Institute of Technology; Ph.D. - Univ. of Tokyo (1977); Overgrad. Univ. of Tokyo  Master Course (1975); Doctor Course Univ. of Tokyo (1977); Graduated Kyushu University (1973).

Research: Ultralow Temperature Physics, Nuclear Beta Decay Experiments, Nuclear Beam Polarization, Fundamental Physics with Polarized Nuclei, Superconducting Magnets

Bowles, Thomas - Los Alamos National Laboratory, University of Washington:

Education: Ph.D., Physics - Princeton (1978); B.S., Physics and Mathematics - Univ. Colo. (1973); Affiliate Professor, Univ. Washington (1995-present); Fellow, LANL, 1994-present; Staff Member, LANL (1979-94); Postdoctoral Research Assoc., Argonne National Lab. (1976-79).

Honors:  Fellow, Am. Phys. Soc. (1993); Fellow, LANL (1994), Officer - LANL Fellows (1996-1999); Nuclear Science Advisory Committee (1999 – present); Executive Committee Div. of Nucl. Phys. of the Am. Phys. Soc. (1996-98); Co-chair, DNP Home Page Committee (1997-1998); Chair, DNP Nominating Committee (1993); LANL Postdoctoral committee (1988-92; Chair - 1989-92); LAMPF Technical Advisory Panel (1982-85); Jacob von Ek Award, Univ. Colo. (1973), Phi Beta Kappa, Sigma Pi Sigma, Delta Phi Alpha - Univ. of Colo. (1973).

Research:  tritium beta decay, solar neutrino physics (SAGE and SNO), ultra low-level counting techniques, dark matter search, fundamental symmetries, time reversal violation in polarized neutron beta decay, UCN sources and physics; also have published results in nuclear astrophysics, nuclear structure, photonuclear and pion physics, second class currents, nuclear parity violation, and neutrino physics.

Carr, Robert – California Institute of Technology

Education:  M.Phil. – Yale Univ. (1969); B.S. – Iowa State Univ. (1966); Professional Staff Member – Cal. Tech. (1983-present); Adjunct Instructor for Physics – Univ. of New Haven (1977-83); Staff – Yale Univ. (1971-83);

Research: Running, repairing and modifying electron linac and tandem pelletron ion accelerator; design and maintenance of circulating liquid hydrogen targets, including writing operations manual and instructing colleagues in their proper operation.

Filippone, Brad - California Institute of Technology:

Education: Ph.D. - University of Chicago (1983); M.S. - Univ. of Chicago (1979); B.S. - Pennsylvania State University (1977); Professor of Physics - California Institute of Technology, (1995-present); Assoc. Prof. of Physics Cal. Inst. of Tech. (1990-95); Asst. Prof. of Physics, Cal. Inst. of Tech. (1984-90); Research Fellow - Cal. Inst. of Tech. (1983-84); Postdoctoral Physicist - Argonne National Laboratory (1982-83);

Honors: Alfred P. Sloan Fellowship (1987-91); Chairman - NPAS Users Committee (1988-89); Member - NSF Proposal Review Panel (1998); Member - APS Division of Nuclear Physics Executive Committee (1997-present); Member - Nuclear Science Advisory Committee (1997-present); Member - NSF Special Emphasis Panel (1996); Member - National Research Council Committee on Nuclear Physics (1996-present); Chairman, CEBAF Program Advisory Committee (1996- present); Member - CEBAF Program Advisory Committee (1993-96); LAMPF Program Advisory Committee (1992-94); DOE Review Committee on Experimental Nuclear Physics Program (P-Division) - LANL (1991); Core Panel Member, National Research Council Committee on Theory and Laboratory Astrophysics (1989-90); Member - CEBAF Hall C Steering Committee (1988-90).

Research:  Nuclear astrophysics, parity violation, HERMES experiment, quark effects in nuclei, beta decay.

Fowler, Malcom - Los Alamos National Laboratory:

Education:  Ph.D. - Washington University (1971); M.A. - Washington University (1967), B.S. Chemistry - Univ. of New Mexico (1966);  Staff member - LANL (1975 - present); Postdoctoral Fellow in Nuclear Chemistry - Lawrence Berkeley Laboratory (1973-1975); Postdoctoral Fellow in Nuclear Chemistry - McGill University (1972-1973).

Honors:, Chairman of the Central New Mexico Section of the American Chemical Society (ACS) (1991-92), advisor to the Central New Mexico Section of the ACS (1992 - present), member of Sigma Xi.

Research: Radiation Detector and Nuclear Instrumentation Development, Study of Rare or Exotic Nuclear Reactions, Ultrasensitive Radiochemical Analytical Techniques.

Geltenbort, Peter - Institut Laue-Langevin:

Education: Ph. D (Physics), First Class Honours, Univ. Tuebingen (1984); Staatsexamen in Mathematics and Physics - Univ. Tuebingen (1979); Institut Laue-Langevin, Grenoble, Scientist (Staff) (1983 - present); Univ. Tuebingen, Scientific Asst. (1979), Scientific Employee (1979-83).

Research:  At ILL,  responsible for a fission fragment spectrometer (1983-89), head of the Detector Group (1989-93), responsible for the Ultra-cold and Very Cold Neutron Installations (1993-present).  Research experience in nuclear fission, radiation detectors, UCN physics, neutron interferometry, nuclear astrophysics, microstrip gas counters, lifetime and electric dipole moment of the free neutron, and thermal neutron cross sections relevant in nuclear astrophysics.

Hill, Roger - Los Alamos National Laboratory:

Education:  Ph.D.- Univ. of California, Berkeley (1964); Staff member - LANL (1986-present); Research Professor - Univ. of New Mexico (1982-86); Technical staff - El Paso Europe (1972-82); Researcher - Rutherford High Energy Laboratory (1966-72); Postodoctoral fellow - Univ. of Chicago (1964-66).

Research:  Pion-nucleon charge-exchange, kaon scattering, polarized targets, polarization measurements, CP violation in K decay, hydrodynamic modelling, low energy experiments, neutrino oscillations, Test Ban Treaty verification, neutron radiography, data acquisition and analysis, Monte Carlo modelling, MWPCs, UCN sources and experiments.

Hime, Andrew - Los Alamos National Laboratory:

Education:  Ph.D. - Oxford University (1991); M.S. - University of Guelph (1988); B.S. - Univ. of Guelph (1986); Staff member - LANL (1995-present); J.R. Oppenheimer Fellow - LANL (1992-95).

Honors:  J.R. Oppenheimer Fellow - LANL (1992-95); Overseas Research Fellow of the Royal Commission for the Exhibition of 1851 (1988); NSERC Fellowship for Post Graduate Studies (1986); NSERC Fellowship for Student Research (1984, 1986); Alma Mater in-course Scholarship - Univ. of Guelph (1985);W.C. Blackwood Entrance Scholarship in Physics - Univ. of Guelph (1982).

Research:  Solar neutrino physics, neutrino mass measurements, ultra-low level counting techniques, optical trapping of radioactive isotopes, dark matter search, beta asymmetry measured using magnetically trapped 82Rb, UCN beta decay.

Hino, Masahiro - University of Kyoto:

Education: JSPS (Japan Soc. Promotion of Science) Research Fellow at Research Reactor Institute, Kyoto University (present position); Ph.D. - Kyushu Univ. (1996); Overgrad.. Master Course (1993); Doctor Course Kyushu Univ. (1996); Graduated Kyushu University (1991).

Research: Cold Neutron Spin Interferometry, Neutron Optics, Neutron Spin Polarizer/Analyzer

Hoedl, Seth – Princeton University

Education: Ph.D. student - Princeton University (1998-present); B.S., Physics -  Stanford University (1998).

Research:  Particle physics, fundamental phyics.

Hogan, Gary – Los Alamos National Laboratory:

Education: Ph.D., Physics - Princeton University (1979); M.A., Physics, Princeton University (1976); B.Sc. with Highest Honors, Physics, University of Texas (1974); Technical Staff Member – LANL (1984 - present); Research Asst. Prof. – Temple University (1982 - 1984);  Director-Funded Postdoctoral Fellowship – LANL (1979 - 1982);  Postdoctoral position - Princeton University (1979).

Honors:  Director’s Postdoctoral Fellow – LANL (1979-82); 1998 LANL Distinguished Performance Award [Small Team]; 1997 LANL Distinguished Performance Award [Large Team].

Research:  Nuclear and particles physics, rare decays, proton radiography, fundamental neutron physics.

Ito, Takeyasu – California Institute of Technology:

Education:  D.Sc. in Physics - University of Tokyo (1997); M.S. in Physics - University of Tokyo (1994);  B.S. in Physics - University of Tokyo (1992);  Postdoctoral Scholar in Physics, California Institute of Technology (1998-Present);  Postdoctoral Fellow, Laboratori Nazionali di Frascati, INFN, Italy (1998); JSPS (Japan Society for Promotion of  Science) Research Fellow - University of Tokyo (1996-1997)

Honors: Japan Nucler Physics Forum "Shinjin-sho" prize (1998)

Research: Low energy kaon nucleon interaction, exotic atoms, parity violating electron scattering, neutron beta decay

Jones, Cathleen - California Institute of Technology

Education: Ph.D. in Physics - California Institute of Technology (1992); M.S. in Physics - (1987); B.S., summa cum laude, Physics, Texas A&M University (1982); Senior Research Associate -Cal. Inst. of Tech. (1997-present).

Honors:  Executive Committee Div. of Nucl. Phys. of the Am. Phys. Soc. (1996-98); Co-chair, DNP Home Page Committee (1997-1998).

Research:  Polarized beams and targets, parity violation, fundamental symmetries.

Kawai, Takeshi - University of Kyoto:

Education:  Associate Prof.; Research Reactor Institute, Kyoto University; Ph.D. - Kyoto Univ. (1990); Overgrad. Kyoto Univ. Master Course (1964); Graduated Gifu University (1962); Visiting Researcher from Ministry of Education at ILL (1991).

Research:  Cold Neutron Source Developments, Ultracold Neutron Production, Low Temperature Technology, Neutron Optics.

Kharitonov, Arcadi - Petersburg Nuclear Physics Institute:

Education:  Lead Engineer; Diploma in Engineering - Leningrad Technology Institute (1966).

Research:  Cryogenics, vacuum techniques, engineering.

Kirch, Klaus – Los Alamos National Laboratory

Education:  Ph.D. – ETH Zurich (1997), Diplom – Univ. of Cologne (1994); Postdoctoral Fellow – ETH Zurich (1997-99).

Honors:  Director’s Postdoctoral Fellowship – Los Alamos National Laboratory

Research:   Muon physics, fundamental neutron physics, ultra-cold neutrons, solar neutrinos.

Kitagaki, Toshio - Tohoku University:

Education: Prof.Emeritus, Tohoku Univ; Ph.D. - Tohoku University  (1956); Graduated Osaka University  (1946); Prof. - Tohoku University  (1961-86); Visiting Scientist with rank of visiting Prof. - Princeton University (1956-59).

Honors:  Member - The US/Japan Committee on High Energy Physics, between DOE of USA and Monbushou of Japan (1980-88).

Research: Accelerator Experimental Particle Physics, Bubble chamber, UCN detector; development of LiOH solid state detector.

Lamoreaux, Steve - Los Alamos National Laboratory:

Education: Ph.D. (Physics) - University of Washington (1986); M.S. (Physics) - University of Oregon (1982); B.S. (Physics) - Univ. of Washington (1981); Staff member - LANL (1996-present); Research Associate Professor - Univ. of Washington Physics Dept. (1986-96).

Honors: Francis M. Pikin Award of the American Physical Society (1999); Fellow - American Physical Society; co-author of book - “Ultra-Cold Neutrons” (1991)

Research:  Precision atomic and neutron experimental techniques; theory of neutron matter interactions; lasers and optoelectronics, theory and experimental techniques;  radiofrequency spectroscopy.

Lassakov, Mihail - Petersburg Nuclear Physics Institute:

Education: Ph.D. in Physics - Petersburg Nuclear Physics Institute (1992); Senior scientist - Physical faculty, Diploma in Physics - Leningrad University (1982);

Research:  UCN and cold neutrons, polarization of UCN, storage of polarized UCN, neutron beta decay experiments.

Liu, Chen-Yiu - Princeton University:

Education:  Graduate student in physics - Princeton University.

Research:  Solid deuterium UCN source, beta asymmetry measurement with UCN.

Martin, Jeffery W. - California Institute of Technology

Education:  Ph.D. - Massachusetts Institute of Technology (1999); B. Sc. (Hons.) in Physics - University of Manitoba (1995);  Postdoctoral Scholar at California Institute of Technology (1999-present).

Honors:  U.M. Allen Medal (1995); AECL research award (1994, 1995); Canada Scholarship (1991-1995); NSERC Undergraduate Research Award (1993, 1994).

Research:  Beta decay, parity violation, nucleon and nuclear structure.

McKeown, Robert - California Institute of Technology

Education:  Ph.D. in Physics - Princeton University (1979); B.A. in Physics - SUNY-Stony Brook (1974); Professor of Physics, California Institute of Technology (1992-present); Assoc. Prof. of Physics - Cal. Inst. of Tech. (1986-92); Asst. Prof. of Physics - Cal. Inst. of   Tech. (1981-86); Asst. Physicist - Argonne National Lab. (1979-80); Research Associate - Argonne National Lab. (1978-79).

Honors:  Fellow of the American Physical Society; National Science Foundation Presidential Young Investigator (1984-89); RHIC Detector Technical Advisory Committee (1995-present); NSAC Long Range Plan Working Group (1995); Member, NSERC Review Committee for Saskatschewan Accelerator  Laboratory (1995); Member, Panel Review of DOE Nuclear Physics Research Program (1994); Editorial Board, Physical Review C (1994-present); Member, National Advisory Committee, Institute for Nuclear Theory (1993-95); Member, (Chair - 1993) Nuclear Science Advisory Committee (1992-95); Vice-Chair Gordon Research Conference on QCD in Nuclear Physics (1991); APS Division of Nuclear Physics Executive Committee (1992-94); NSAC Subcommittee on Implementation of the Long Range Plan (1992); EPRI Review on Anomalous Nuclear Measurements in Deuterium/Metal Systems (1991); NSAC Long Range Plan working group (1989); Committee on Future Directions at LAMPF (1989-90); Program Review, Bates Linear Accelerator Center (1989); Chair CEBAF Users Group Board of Directors (1990); CEBAF Users Group Board of Directors (1989-91); Chair LAMPF Users Group Board of Directors (1990); LAMPF Users Group Board of Directors (1989-91); NSAC Subcommittee on Instrumentation (1988-89); APS Division of Nuclear Physics Program Committee (1989); CEBAF Hall B Co-program manager (1986-89); CEBAF Program Advisory Committee (1986); LAMPF Program Advisory Committee (1986-89); NSAC Long Range Plan working group (1983).

Research:  Weak interactions, fundamental symmetries, neutrino physics, parity violation, polarized beams and targets, quark effects in nuclei, beta decay.

Miyachi, Takashi - University of Tokyo:

Education: Research Associate - Center for Nuclear Science Research, University of Tokyo (present position); Ph.D. - Tokyo Institute of Technology (1967); Overgrad. Tokyo Institute of Technology  Doctor Course (1967); Graduated Tokyo Institute of Technology (1963).

Research: Nuclear and Fundamental Physics, Solid State Nuclear Detectors

Morris, Chris - Los Alamos National Laboratory:

Education:  Ph.D. - University of Virginia (1973); B.S. - Lehigh University (1969); Fellow - LANL (1996-present); Staff Member - LANL (1977-96); Postdoctoral fellow - Univ. of Virginia (1973-77).

Honors:  Fellow - LANL (1996); Fellow - American Physical Society (1986); Inventors award - LANL (1985, 1987); 2 patents.

Research:  Medium energy physics, proton radiography, neutron beta decay, UCN sources and experiments.

Pichlmaeir, Axel – Los Alamos National Laboratory

Education:  Ph.D. – Technical University of Munich (1999); Diplom – Tech. Univ. of Munich (1995).

Research:  Fundamental neutron physics, ultra-cold neutrons, solar neutrinos.

Pitt, Mark - Virginia Polytechnic Institute and State University

Education: Ph.D. in Physics - Princeton University (1992); M.A. - Princeton University (1987); B.S. - California Institute of Technology (1985); Assistant Professor - Virginia Polytechnic Institute (1997-present); Senior Research Fellow - Caltech (1995-96); Research Fellow - Caltech (1992-1995).

Honors: National Science Foundation Early Faculty CAREER Award (1998-present); Robert A. Millikan Research Fellowship in Experimental Physics, Caltech (1992-1995).

Research: Polarized targets and beams, parity violation in electron scattering, beta decay, nucleon form factors.

Rudnev, Yuri - Petersburg Nuclear Physics Institute:

Education:  Scientist; Diploma - Leningrad University (1966)

Research:  Superconducting magnetic systems, cryogenics, semiconducting detectors, neutron beta decay.

Seestrom, Susan - Los Alamos National Laboratory:

Education:  Ph.D. - University of Minnesota (1981); Postdoctoral fellow - LANL (1981-83); Postdoctoral fellow - Univ. of Minnesota (1983-86); Technical staff member - LANL (1983 - present).

Honors:  Fellow - Am. Phys. Soc.; Executive Committee of Div. of Nuclear Physics of the Am. Phys. Soc. (1992-95); Exec. Comm. of the Am. Phys. Soc. (1996-present); Div. of Nuclear Physics Nominating Committee (1996-97; Chair 1997); Board of Directors of LAMPF (1990-92); Div. of Nucl. Phys. Program Committee (1986-88).

Research:  Weak interaction nuclear physics, fundamental symmetries studied using neutron beams, nuclear structure and reaction mechanisms, UCN sources and beta decay experiments.

Serebrov, Anatoli - Petersburg Nuclear Physics Institute

Education:  Professor - Petersburg Nuclear Physics Institute (1993); Ph.D. - Petersburg Nuclear Physics Institute (1990); Diploma - Leningrad University (1969); Director of the Neutron Physics Division - Petersburg Nuclear Physics Institute.

Research:  Weak interactions and elementary particles, electric dipole moment of the neutron, neutron beta decay, fundamental symmetries, UCN sources, depolarization of UCN.

Soyama, Kazuhiko - Japan Atomic Energy Research Institute

Education: Research Staff, Japan Atomic Energy Research Institute (present position); Graduated  Rikkyo Univ. (1983).

Research: Engaged in JAERI Reactor JRR-3 Modernization Reconstruction Project from 1984, Solid State Nuclear Detectors, Presently responsible on development of neutron super-mirror and neutron focusing device using multilayer mirror.

Tipton, Bryan -  California Institute of Technology

Education: Ph. D. - Massachusetts Institute of Technology ( 1999); B.S. in Physics – The Pennsylvania State University (1994); Millikan Postdoctoral fellow - Cal. Inst. of Tech ( 1999-present).

Research:  neutron beta decay, nucleon substructure, polarized beams, solar neutrinos, reactor neutrinos.

Vasilev, Anatoli - Petersburg Nuclear Physics Institute:

Education:  Scientist;  Diploma - Leningrad University (1985).

Research:  Electronics, computers, experimental techniques.

Utsuro, Masahiko - University of Kyoto:

Education:  Professor, Research Reactor Institute, Kyoto University ; Ph.D. - Osaka University (1972); Overgrad. Osaka Univ. Master Course (1962); Graduated - Osaka University (1960); Visiting Researcher from Ministry of Education at ILL and Tech. Univ. Munich (1976-77)

Research:  Cold Neutron Source Developments, Ultracold Neutron Production, Ultracold Neutron Experiments, Neutron Optics, Slow Neutron Scattering

Vogelaar, R. Bruce – Virginia Polytechnic Institute and State University:

Education:  Ph.D. in Physics - California Institute of Technology (1989); M.S. - Cal. Inst. of Tech. (1984); B.S. - Hope College (1982); Assoc. Prof. – Virginia Tech (1998-present); Asst. Prof. - Princeton Univ. (1991-present); Research staff - Princeton Univ. (1989-91).

Honors:  Sigma Xi Research Award in Physics; Charles E. Lake Memorial Award.

Research:  Solar neutrino experiments (Borexino), ultra low-level counting techniques, nucleosynthesis, beta decay.

Walstrom, Pete - Los Alamos National Laboratory

Education:  Staff Member - LANL (1997-present); Ph.D. Cornell University, Laboratory of Nuclear Studies (1972); B.S. Harvey Mudd College (1967); Specialist, Engineering Physics - Grumman Corp. (1988-97); Assoc. Scientist - Univ. of Wisconsin, Madison (1984-88);, Staff member - Oak Ridge National Laboratory - 1972-84)

Research:  Design, analysis, and testing of high-precision static and dynamic magnet systems, superconducting magnet designs.

Wilhelmy, Jerry - Los Alamos National Laboratory

Education: Ph.D. University of California at Berkeley (1969); B.S. Chemical.Engineering - University of Arizona (1964); Fellow - LANL (1982-present);  Staff member - LANL (1972-82); Research Scientist, Max Planck Institut fur Kernphysik (1978-79); Visiting Scientist - Weizmann Institute (1978, 1982); Post Doctoral Fellow, Lawrence Berkeley National Laboratory (1969-72).

Honors:  Fellow - LANL (1982), Tau Beta Pi,  Lawrence Livermore National Laboratory - Transactinium Element Panel; Department of Energy - Transplutonium Advisory Committee; National Research Council - Transplutonium Assessment Panel, National Academy of Science/ National Research Council Committee on Nuclear and Radiochemistry.

Research: weak interaction processes, solar neutrino studies, nuclear fission, production and properties of heavy elements, heavy ion reactions, supercritical atomic fields, ultrasensitive nuclear detection techniques, nuclear reactions on off stable species, and applied nuclear reaction diagnostics.

Young, Albert - Princeton University:

Education:  Assistant Professor;  Ph.D. in Physics - Harvard University (1990);  B.A. in Physics - University of Washington (1982); Asst. Prof. - Princeton University (1996-present); Lecturer - Princeton Univ. (1994-96); Research Associate - Princeton University (1992-94); Junior Research Fellow - California Institute of Technology (1990-92).

Research:  Electron-ion collisional processes and plasmas, fundamental symmetries, time reversal in 19Ne beta decay, beta decay asymmetry in 19Ne beta decay, optical pumping of polarized radioactive 36K, beta decay of polarized 36K, APEX experiment, spin dependence of the muon capture rate on 3He, spin relaxation in oriented alkali metal vapors, UCN beta decay.

Yuan, Junhua – California Institute of Technology

Education:  Ph.D. student – Cal Tech (1998-present)

Research:  Fundamental neutron physics.

APPENDIX 18

REFERENCES

1)  Smith, K.F. et al., Phys. Lett. B234 (1990) 191

2)  Altarev, I.S. et al., Phys. Lett. B276 (1992) 242.

3)  Mampe, W. et al., Phys. Rev. Lett. 63 (1989) 593.

4)  Nevizhevsky, V. et al., JETP 75 (1992) 405.

5)  Mampe, W. et al., JETP Lett. 57 (1993) 82.

6)  Ignatovich, V., JETP Lett. 62 (1995) 1.

7)  Sakurai, J.J., Invariance Principles and Elementary Particles, Princeton University Press 	(1964) 161.

8)  Byrne, J., Rep. Prog. Phys. 45 (1982) 115.

9)  Erozolimskii, B.G., Nucl. Instr. Meth. A284 (1989) 89.

10)  Gluck, F. et al., Nucl. Phys. A593 (1995) 125.

11)  Wilkinson, D.H., Phys. Lett. 31B (1970) 447.

12)  Grenacs, L., Ann. Rev. Nucl. Part. Sci. 35 (1985) 455.

13)  McKeown, R.D. et al., Phys. Rev. C22 (1985) 738.

14)  Dubbers, D., Nucl. Phys. A257 (1991) 239c.

15)  Klemt E. et al., Z. Phys. C37:  179 (1988).

16)  Bopp P., et al., Phys. Rev. Lett. 56 (1986) 919, Bopp P. et al., Nucl. Instr. Meth. A267 	436 (1988).

17)  Dohner J., et al., Nuc. Instr. Meth. A284 (1989) 123.

18)  Erozolimskii, B.G. et al., Phys. Lett. B236 (1991) 33.

19)  Serebrov, A., private communication

20)  Kuznetov, I., private communication

21)  Schreckenbach, K. et al., Phys. Lett. B349 (1995) 427.

22)  Reich, J. et al., NIM 440 (2000) 535.

23)  Carnoy, A.S. et al., J. Phys. G:  Nucl. 	Phys. 18 (1992) 823.

24)  Wilkinson, D.H., NIM A257 (1993) 201.

25)  Wilkinson D. H., Z. Phys. A 348 (1994) 129.

26)  Savard, G. et al., Phys. Rev. Lett. 74 (1995) 1521.

27)  Fujikawa, B., private communication

28)  Particle Data Group, Phys. Rev. D54 (1996) 567.

29)  Mostovoy, Yu., Preprint IAE-6040/2 (1997).

30)  Steyerl, A. and Malik, S.S.,  Nucl. Instrum. Methods. A284 (1989) 200.

31)  Fraser, J.S. et al., Physics in Canada 21 (1965) 17.

32)  Brun, T.O. et al., Phys. Lett. A75  (1980) 223.

33)  Cavaleiro de Miranda, P.M., Ph.D. Thesis, Univ. of Sussex (1987) 126.

34)  Hayes, C.E. et al., Journal of Magnetic Research 63 (1985) 622.

35)  Abragam, A., The Principles of Nuclear Magnetism (Oxford Press:  London) 35 (1961).

36)  Abe, K. et al., Phys. Rev. Lett .79 (1997) 26.

37)  Gamblin, R. and Carver, T., Phys. Rev. 138, (1965) A946.

- Serebrov, A. et al, to be published in Nucl. Instr. Meth. (1999).

39)  Pendlebury, M., private communication

40)  Mortata, J.L. et al., Phys. Rev. Lett. 70 (1993) 394.

41)  Morris, C.L. et al., A379 (1996) 243.

42)  Atencio, L.G., et al., Nucl. Instr. Meth. A334 (1993) 643.

43)  Binon, F. et al, 94 (1971) 27.

44)  Breskin, A. Nucl. Instr. Meth. 141 (1977) 505.

45)  F. Sauli, in “Experimental Techniques in High Energy Physics”, ed. by Thomas Ferbel, 	Addison-Wesley Publishing Company, Inc. (1987) 79.

46)  Philips Photonics photomultiplier tube catalog, p. 15.

47)  Charpak, G. and Sauli, F., Phys. Lett. B78 (1978) 523.

48)  Breskin, A. et al., Nucl. Instr. Meth. 161 (1979) 19.

# Text boxes

Cold neutron detector

UCN

Detector

Shielding

58Ni coated stainless guide

Vacuum chamber

Tungsten Target

77 K poly

Solid D2

Be reflector

Polyethylene

Liquid N2