Discussion Points for this Meeting
How is beam delivered to UCN?
  - How is 1 min on / 3 mins off achieved for UCN?
Where should we locate the UCN source?
How do we proceed on conceptual to technical design for the UCN source and experiment?
How much space is required for UCN?
How much does it cost?
When do we need it by?

---
How much space is required for UCN? Masuda's conceptual drawing.
Potential Layout in Proton Hall (rev. 9/6/07)
layout still needs some work... cryogenics location, shielding, remote handling

---
How do we proceed on conceptual to technical design for the UCN source and expt?
Issues:
radiation
cryogenics
neutronics
division of tasks
Masuda, Golub, others? very interested in cryogenics and neutronics
need TRIUMF support to bring to fruition

---
Where should we locate the UCN source?
Proton Hall (?)
UCN
12m x 12m boxes
BL5

---
How is beam delivered to UCN? (a concept)
simultaneous operation with ISAC-3 by decoupling on kHz scale with kicker/ion source manipulation. Advantageous for ISAC-3: run all three targets simultaneously.
ion source current vs. time
kick to ISAC-3-1
kick to ISAC-3-2
kick to ISAC-3-3
(UCN)
I(t)
1 msec
10 msec
t
To achieve 1 min on / 3 min off:
Using another kicker, the UCN
beam would be diverted either
to UCN spallation target, or to
the new ISAC-3 dump.
More general question: Will kickers be used on BL4N or not? Can we benefit from this?

---
How much does it cost?
Cryostat cost relatively well-understood (1.4 M$ CAD)
Shielding, remote handling yet to be estimated. Base on experience from TRIUMF, LANL, and RCNP? (Prior to shielding simulations.)
Flagship experiment target cost of <$2M (scale of TWIST experiment).

---
When do we need it by?
Planning for next 5yp period, beginning 2010.
Prior to 2010, pursue development of new UCN cryostat for TRIUMF at RCNP, Osaka.
  - This would allow us to demonstrate all the gain factors from horizontal extraction, better UCN guides. (aside from beam power)
After 2010, begin construction of UCN source at TRIUMF (2010 = coincident with major reconstruction for ISAC 3).