Agenda for 10-4-7
Recap – conclusions from the UCN workshop.
Collaboration building, funding options, and timetable.
Main purpose of this meeting: technical issues for TRIUMF.

---
1. UCN Workshop Summary
A resounding “yes” from the international UCN community.

---
Comments on
Spallation He-II UCN Source
Unique source concept that is feasible.
This should be pursued somewhere.
TRIUMF would be an ideal place.
Technical issues and costing should be pursued.
Need to identify clear physics goal. Optimize source-experiment coupling.
Relationship to JPARC should be solidified.

---
Comments on
Flagship UCN Experiment
High UCN densities are a very good thing.
For TRIUMF concept, important to focus on expts where density important, as opposed to production rate.
  - Gravity – great chance to make big impact.
  - Lifetime – LANL effort – can we make use of this? (most likely candidate for LOI, IMHO)
  - RIB-UCN interactions – great concept!
  - nnbar – subsequent to meeting, email from A. Young which was very positive, but required 400 uA.
  - EDM – tough
  - Angular correlations – competition with CN experiments particularly difficult, systematics must be carefully argued.
  - Solid state physics – important! Need applications, further R&D. Apparatus is very cost effective.

---
Comments on Flagship UCN Expt
gravity – currently limited by UCN density, a real chance to make an impact.
neutron lifetime – tough business, but new magnetic traps are in infancy. still time to contribute.
EDM – tough business, large collaboration required, cost, but possible to make headway given high UCN density.
nnbar – UCN production rate, can He-II compete with SD2? may have niche with UCN, cheaper than beam expts which cost $100M
RIB-UCN interactions should be pursued with high priority! unique to TRIUMF

---
General Comments
What kind of cost levels are you talking about?
  - $2M+outside contributions (scale of TWIST). Japanese contributions. For bigger expts, TRIUMF would draw outsiders by availability of high UCN density.
How much current can you take?
  - 40 uA pk, 10 uA avg.
  - cooling, shielding, remote handling req'd.
  - have to be careful of gamma heating
Manpower
  - better to concentrate manpower than having many small groups.

---
2. Collaboration, funding, timetable
Bob Golub very enthusiastic about TRIUMF UCN project (he literally “wrote the book” on UCN)
  - He-sources superior to SD2 sources due to no absorption, simplicity of concept.
  - spallation sources superior to reactor sources in the ability to optimize CN flux.
Gobub interested in collaborating on developments toward He-II UCN source.

---
Collaboration
2007, Masuda intends make funding request to Japanese sources for UCN source upgrade. Golub, Martin, all Canadian collaborators ... invited to support this effort. (not sure exactly what Masuda requires – letters of support? signatures?)
2008, Canadian request

---
Collaboration – as presented to TRIUMF board
strong KEK group who have already created a world-class facility (Masuda et al)
strong interest from Canadian SAP community
well-attended working group at August TRIUMF townhall meeting
big event: UCN workshop at TRIUMF Sept. 13-14, 2007
  - world experts in attendance
Interest in submitting a CFI proposal for UCN source in 2008 from Canadian groups

---
Schedule
Prior to 2010, pursue development of new UCN cryostat for TRIUMF at RCNP, Osaka.
  - This would allow us to demonstrate all the gain factors from horizontal extraction, better UCN guides. (aside from beam power)
After 2010, begin construction of UCN source at TRIUMF (2010 = coincident with major reconstruction for ISAC 3).

---
Cost
Cryostat, LHe cooling costs very well-understood (1.4 M$ CAD)
Shielding, remote handling yet to be estimated. Base on experience from TRIUMF, LANL, and RCNP. (Prior to shielding simulations.)

---
3. Technical Issues for UCN
Location.
Beam sharing (dependent on location).
Space (dependent on location).
To carry out precision experiments, it is highly advantageous to pulse the UCN source. E.g. RCNP uses 1 min beam on, 3 mins beam off. During beam off, UCN can be counted (or their decays, etc.)
  - pulsing at ion source incompatible with ISAC.
  - achieve pulsing by diverting beam to well-shielded dump using kicker.

---
UCN
(12m x 12m)

---
UCN
- other options
BL5

---
Solutions Discussed for Technical Issues (thanks, accel group!)
Location: BL4A area
  - UCN source viewed as an ISAC-3 target station, located in Proton Hall
  - Advantages:
    - UCN fully integrated into ISAC-3 program in terms of physics (fundamental symmetries) and facility (another ISAC-3 target station).
    - simultaneous operation with ISAC-3 by decoupling on kHz scale with kicker/ion source manipulation. Advantageous for ISAC-3: run all three targets simultaneously.
    - use another kicker to divert beam to dump in ISAC-3 area to achieve UCN pulsing (1 min on / 3 mins off).
    - recent designs of ISAC-3 BL4N take the beam further into Proton Hall (towards UCN). And more shielding already required in that area.
  - Disadvantages:
    - space in Proton Hall getting tight.
    - coupled to ISAC-3.
Location: ISAC-3 target hall.
Location: BL5 port (new port)

---
simultaneous operation with ISAC-3 by decoupling on kHz scale with kicker/ion source manipulation. Advantageous for ISAC-3: run all three targets simultaneously.
ion source current vs. time
I(t)
1 msec
10 msec
t
kick to ISAC-3-1
kick to ISAC-3-2
kick to ISAC-3-3
(UCN)

---
Solutions Discussed for Technical Issues
Location:
  - BL5 area
    - Advantages:
      - decoupled from ISAC 3.
    - Disadvantages:
      - new beam port must be constructed
      - beam line must not conflict with cyclotron probe extraction point
      - high-power dump required to achieve pulsing with kicker.
      - space in Proton Hall tighter – likely requires excavation for dump.

---
Potential Layout in Proton Hall (rev. 9/6/07)
layout still needs some work... cryogenics location, shielding, remote handling