UCN and SCRF/ISAC interface issues
proposal for UCN (CFI, 2008)
  - 10 uA at 25% duty cycle (1 min on, 3 min off)
  - use BL4A (TISOL)
duty cycle is incompatible with ISAC targets, but may be necessary for low background for UCN experiments
strategy for UCN (after discussions with SCRF/accel)
  - accept beam on BL4A when ISAC 2nd target station is off, or part-time during target development periods, or when e-linac in operation (This could be a substantial part of the BL4 time initially available.)
  - accept sole user status in low-intensity periods so that duty cycle can be achieved at source.
space requirements in proton hall tight, but can be managed
LHe source would not be common to e-linac, but could be housed in same space.

---
Future Upgrades
(5YP and beyond)
other options for duty cycle
  - fast kicker + local beam dump in hall
    - local shielding of dump required
    - reorganization of proton hall more appropriate to be on same time scale as ISAC 2nd target station
  - manipulation of internal cyclotron beams
    - requires further study
  - carbon stripper with mechanical motion in/out to pulse beam
    - difficult
other options besides sharing BL4 with ISAC
  - two stripper foils on same extraction probe + septum
    - difficult, more appropriate for BL1
  - BL1, BL5
    - major reconstruction
  - (gamma,n) or photofission source of neutrons (Behr)
    - requires further study