An Ultracold Neutron Source for TRIUMF
Jeff Martin (U. Winnipeg)
for Chuck Davis (TRIUMF), Akira Konaka (TRIUMF), Yasuhiro Masuda (KEK),
and the rest of the UCN working group
1. UCN interactions
2. UCN physics experiments
3. Source work at RCNP and TRIUMF
4. CFI, relationship, collaboration, KEK

---
Ultracold Neutrons
Ultracold Neutrons
UCN are neutrons that are moving so slowly that they are totally reflected from a variety of materials.
So, they can be confined in material bottles for long periods of time.
Typical parameters:
  - velocity < 8 m/s
  - temperature < 4 mK
  - kinetic energy < 300 neV
Interactions:
  - gravity: V=mgh (h < 3 m)
  - weak interaction (allows UCN to decay)
  - magnetic fields: V=-B (100% polarization)
  - strong interaction

---
World comparison
Source type
Ec and τs
UCN density
ρUCN(UCN/cm3)
TRIUMF
5 kWav proton
0.8K He-II
Ec = 210 neV
τs = 150 s
1.8 x 104 at experimental port
Grenoble
60MW reactor
0.5K He-II
Ec = 250 neV
τs = 150 s
1000 in He-II
SNS
cold neutron beam
0.3K He-II
Ec = 134 neV
τs = 500 s
430 in He-II
Munich
20MW reactor
SD2
Ec = 250 neV
104 in source
North Carolina
1 MW reactor
SD2
Ec = 335 neV
1300 in source
PSI
12 kWav proton
SD2
Ec = 250 neV
τs = 888 s
2000 in source
Los Alamos
2.4 kWav proton
SD2
Ec = 250 neV
τs = 2.6 s
120 in source

---
UCN Physics
fundamental interactions of UCN
  - EDM
  - gravity
  - beta-decay
  - nnbar
astrophysics
  - BBN
  - r-process
surface physics
development towards JPARC 2nd target station

---
UCN quantum states in gravity
test of gravity at 10 um scale

---
Surface Physics
Many ideas to use UCN to study 10 nm thin surface films
  - (n,gamma)
  - UCN loss measurements
  - n scattering
  - reflectometry
      - polarization for magnetic films
shown to be sensitive to low-frequency excitations (interesting for surface physics)
In all cases, lack of UCN worldwide is the problem

---
World comparison
Source type
Ec and τs
UCN density
ρUCN(UCN/cm3)
TRIUMF
5 kWav proton
0.8K He-II
Ec = 210 neV
τs = 150 s
1.8 x 104 at experimental port
Grenoble
60MW reactor
0.5K He-II
Ec = 250 neV
τs = 150 s
1000 in He-II
SNS
cold neutron beam
0.3K He-II
Ec = 134 neV
τs = 500 s
430 in He-II
Munich
20MW reactor
SD2
Ec = 250 neV
104 in source
North Carolina
1 MW reactor
SD2
Ec = 335 neV
1300 in source
PSI
12 kWav proton
SD2
Ec = 250 neV
τs = 888 s
2000 in source
Los Alamos
2.4 kWav proton
SD2
Ec = 250 neV
τs = 2.6 s
120 in source

---
RCNP UCN Source (Masuda, et al)
1 ua protons at 400 MeV => 10 UCN/cc to expt.
Already has external users!
- e.g. Korobkina, Young (NCSU)

---
O

---
Collaboration
led by Winnipeg, Manitoba groups
strong KEK group who have already created a world-class facility (Masuda et al)
well-attended working group at this townhall meeting
UCN workshop at TRIUMF Sept. 13-14, 2007
  - world experts in attendance
Interest in submitting a CFI proposal in 2008 from these groups

---
Shameless advertising
International Workshop:
UCN Sources and Experiments
September 13-14, 2007
TRIUMF, Vancouver, Canada
http://www.triumf.info/hosted/UCN
Registration is free, but please do register
~25 speakers from all over the world
ILL, FRM-II, NCSU, LANL, PSI, KEK, Mainz, ...
Supported by TRIUMF and TUNL

---
Some key statements for the white paper
e-linac in same general area (space)
BL4 used to feed ISAC (time)
UCN would be planned to minimize conflict with either program
UCN source at TRIUMF would be a world-class facility
A flagship experiment at this UCN source would impact knowledge of fundamental interactions of neutrons

---
Summary
An opportunity exists to create the world's highest density UCN source at TRIUMF
A flagship physics experiment done this facility would be world's best
We would like to pursue this unique and timely opportunity

---
Shameless advertising
International Workshop:
UCN Sources and Experiments
September 13-14, 2007
TRIUMF, Vancouver, Canada
http://www.triumf.info/hosted/UCN
Registration is free, but please do register
~25 speakers from all over the world
ILL, FRM-II, NCSU, LANL, PSI, KEK, Mainz, ...
Supported by TRIUMF and TUNL

---
Speakers at TRIUMF
UCN Workshop
Sept. 13-14, 2007
H. Abele*, Heidelberg
S. Baessler, Mainz/UVa
L. Buchmann, TRIUMF
M. Daum, PSI
S. Gardner*, U. Kentucky
P. Geltenbort*, ILL
E. Gutsmiedl, Munich FRM-II
R. Golub, NCSU
B. Filippone, Caltech
P. Huffman, NCSU
T. Ito, LANL
E. Korobkina, NCSU
C.-Y. Liu, Indiana U.
M. Makela, LANL
J.W. Martin, U. Winnipeg
Y. Masuda, KEK
C. Morris, LANL
P. Mumm, NIST
J. Nico*, NIST
J. Ng, TRIUMF
S. Paul*, T.U. Muenchen
M. Pospelov*, U. Victoria/Perimeter Inst.
J.-M. Poutissou, TRIUMF
W.M. Snow*, Indiana U.
F. Wietfeldt, Tulane U.
A. Young, NCSU
O. Zimmer*, ILL

---
Aug. 1
morning - plenary session, charge, and introduction of working groups
12:00 lunch
13:00 Welcome + Charge (Martin) (10+5)
13:15 UCN Sources Worldwide and for TRIUMF (Masuda) (45+10)
14:10 Photofission, (gamma,n) Sources and UCN (Behr) (10+10)
14:30 coffee (30)
15:00 SCRF joint session: Electron Linac Design (Koscielniak) (20+10)
15:30 UCN Infrastructure and Proton Hall Floorplan (Davis) (10+10)
15:50 Proton Hall Radiation Limits (Trudel) (10)
16:00 Discussion (Chair: Davis) (30)
16:30 tour of proton hall? (if desired) (Davis) (30)
Aug. 2
09:00 Continued infrastructure Discussion (60)
10:00 UCN Physics Intro (Martin) (10+5)
10:15 UCN Beta Decay (Melconian) (20+10)
10:45 coffee (30)
11:15 n-EDM (Masuda and/or Hayden?) (20+10)
11:45 radioactive beams (Buchmann) (10+10)
12:05 lunch
13:15 gravity levels (Konaka) (5+10)
13:30 other physics (Martin) (15+10)
13:55 discussion of physics priorities and strategy (chair: Martin) (35)
14:30 begin writing
      more joint sessions
      draft Aug. 3 morning presentation
Aug. 3
morning - presentations of results from the working groups.
Agenda

---
Back-ups

---
Options considered
for duty cycle
  - fast kicker + local beam dump in hall
for BL4 sharing with ISAC
  - two stripper foils on same extraction probe + septum
    - difficult, more appropriate for BL1
  - other lines: BL1, BL5
  - (gamma,n) or photofission source of neutrons (Behr)
    - requires further study
for space
  - locate UCN source in ISAC 2nd target
for LHe
  - modest consumption 200 L/day

---
Outline of White Paper
Physics
  - prioritized and realistic, as much as possible
UCN Source
  - proposed intensity at TRIUMF
  - world context and relevance
Required Infrastructure
  - floorspace, shielding
  - duty cycle
  - He liquefier
Required funding
  - CFI and collaboration, and international

---
Possible topology
Measuring (n,ɣ) cross sections of the r-process (Buchmann)
132Sn stored in ring interacts
with free neutron (UCN) target.
132Sn current 5e17 /s
UCN density 2e4 /cc
meter-long target
sigma ~ 100 mb
=> 50 interactions per hour
recoil separator
Accelerator
Possible tunnel
UCN
Storage ring
Recoil separator